## Slide 1
SA2#144E CC1:
AF Instance change
Source: Huawei

## Slide 2
Background
Due to the UE mobility, the AF served the UE can be relocated. Per TS23.502 clause 4.3.6,
  If the target AF need update the target AF instance information, the AF triggers the Nnef_TrafficInfluence_Create/Update, which includes the AF ID and notification target address. ---Info directly from PCC rule
  In the Nnef_TrafficInfluence_AppRelocationInfo, the updated UP change event information is provided to the SMF, i.e. the indication of AF change, target AF ID and notification target address of the target AF are included.--- Info from AF.
The information provided by the AF directly is overlapped with the information provided by the PCC rule. Due to that, three questions are asked by CT3:
  Q1: If the AF needs to update the target AF instance information, does the AF need to trigger the Nnef_TrafficInfluence_Update service operation to the NEF, and the update of AF influence control on traffic routing is delivered to the SMF within the PCC rule via N7?
  Q2: If answer of Q1 is yes, what’s the motivation to use Nnef_TrafficInfluence_AppRelocationInfo to include the target AF instance information?
  Q3: If answer of Q1 is no, how will the SMF consolidate the target AF information received by Nsmf_EventExposure_AppRelocationInfo with existing PCC rules if the information is not received via N7?

## Slide 3
Proposal on the table
CATT proposal(S2-2102396/2397)
  501CR: In the AF request table, the AF update related IE are introduced to support the Nnef_TrafficInfluence_Update service operation.
  502 CR: remove the all three parameters in the Nnef_TrafficInfluence_AppRelocationInfo and clarify the Nnef_TrafficInfluence_Create/Update operation is used for the AF instance change.
Huawei proposal(S2-2102561/2562/2560)
  502 CR: except the indication of AF change, remove other two parameters in the Nnef_TrafficInfluence_AppRelocationInfo and clarify the Nnef_TrafficInfluence_Create operation is used for the AF instance change.
  One corresponding LS reflect the proposal CR is suggested.
Nokia proposal(S2-2102935/2939/2933)
  502 CR: Nnef_TrafficInfluence_AppRelocationInfo is used for positive or negative Ack. And for all the information such as DNAI, N6 routing info, etc. AF invokes the Nnef_TrafficInfluence_Create/update operation, thus ensuring SMF receives all info via PCF
  One corresponding LS reflect the proposal CR is suggested.

## Slide 4
Open issues
Based on the offline discussion, these are still open issues and needs further discussions:
Whether the indication of AF change need be notified to SMF via the Nnef_TrafficInfluence_AppRelocationInfo service operation in case of AF instance change. This is to let SMF be aware that notification address is to be changed.
Whether the SUBSCRIPOTN resource URI can be updated via the Nnef_TrafficInfluence_update service operation as it is restricted to the single UE case and not supported in existing stage-3 specification. Also this impacts the Rel-16 frozen specification.
Whether AF invokes Nnef_TrafficInfluence_Create/update to send all information i.e. DNAI, N6 routing info, etc. to SMF via PCF, instead of sending directly via Nnef_TrafficInfluence_AppRelocationInfo

## Slide 5
Way forward Proposal
Based on the offline discussions:
Take these papers as baseline Rel-16 CRs for further discussion: S2-2102396 and S2-2102397 (CATT)
Take this paper as baseline Rel-17 CR for further discussion : S2-2102562 (Huawei)
Take this paper for LS out (subject to CRs agreement) : S2-2102933 (Nokia)

## Slide 6
Thank You!