## Slide 1: SA2#144E eNS_Ph2 CC#1

## Slide 2: Topic 1 NSAC for number of PDU session(KI#2)
How to perform NSAC for number of PDU session(KI#2)
  Option 1: AMF interacts with NSACF (2322(NTT DoCoMo),2931(Lenovo))
  Option 2: SMF interacts with NSACF(2572(Huawei), 2622(Samsung), 2856(NEC, Apple, Nokia, Nokia Shanghai Bell, Ericsson, LG Electronic).
  Proposal 1a: agree option 2
  Proposal 1b: further work on roaming/ETSUN case in which whether AMF or V-SMF/I-SMF interacts with NSACF.

## Slide 3: Topic 2 Distributed NSACF
There are several FFS on how to support distributed NSACF.
One solution is proposed 2569(Huawei, HiSilicon,China Unicom, China Telecom) to introduce primary NSACF and secondary NSACF in order to resolve the FFS.
Corresponding CR in 2570/2571 for KI#1 and 2572 for KI#2
  Proposal 2: agree the principles in the solution above and further work in details during this meeting

## Slide 4: Topic 3 Service on NSACF
Whether to use common service in NSACF for KI#1(number of UE ) and KI#2(number of PDU session)
  Option 1: common service
    Nnsacf_NSAC_Check for both(2910(ZTE)), NSAC type to differentiate KI#1 and KI#2
  Option 2: different service
    KI#1: Nnsacf_NumberOfUEsPerSliceAvailabilityCheckAndUpdate (Existing)
    KI#2: Nnsacf_NumberOfPDUsPerSliceAvailabilityCheckAndUpdate(2857(NEC, Apple, Nokia, Nokia Shanghai Bell, Ericsson, LG Electronics),2622(Samsung))
Proposal 3: discuss this topic, quick SoH on question which option is preferred