## Slide 1: KI#6 WF discussion

## Slide 2: Snapshot of status
After extensive online and offline discussion which resulted in the multicompany input being updated to allow a S-NSSAIs to have multiple SRG membership (as in Huawei and Ericsson independent proposals), we are at a point where two approaches have been identified
Approach A (supporting companies+Ericsson):
  the Configured NSSAI with all S-NSSAIs in subscription information with any SRG value is provided only to supporting UEs (alongside SRG information so the UE can avoid attempting to register with SRG-incompatible slices).
  Non-supporting UEs and non-supporting VPLMNs only get the S-NSSAIs with SRG=0, which includes the default S-NSSAIs.
  Main goal (or benefit) is to have deterministic behaviour at all times
  A UE Always attempts to register with compatible slices by definition unless it needs an updated configuration (i.e. the SRG information has changed in the subscription but the UE is not yet up to date).
  Huawei argue providing legacy UEs with a reduced set of SRG-compatible slices with SRG=0 (as non supporting VPLMNs) is an unacceptable downside of this solution
  See S2-2102773r04 and S2-2102800r02
Approach B (Huawei):
  A supporting network is not aware of whether a UE supports the feature or not so any UE is provided a Configured NSSAI with all S-NSSAIs in subscription information irrespective of the SRG value, and the SRG value is provided to all UEs but some may not understand it and the network does not know which do not understand it, so the network does not have a way to detect misconfigured UEs.
  Non-supporting VPLMNs only get the S-NSSAIs with a certain SRG value decided by the HPLMN, which conceivably include the default S-NSSAIs
  Main goal (or benefit) is to not exclude any S-NSSAI in subscription from the ability of a legacy UE to use it but the behaviour of non supporting UEs when some requested S-NSSAIs are not allowed is not known.
  The Companies in the other camp argue that some unpredictable non deterministic behaviour can be expected in the system and this may harm the UE, the network, or both. Besides there is still the limitation of non supporting VPLMNs that is likely to lead to the same reduced set of S-NSSAIs in both solutions can only be guaranteed for roaming UEs so the main benefit of this solution is not achieved in this case at least. It is not clear why the limitation for non supporting PLMN is not applied also to not supporting UEs to achieve deterministic behaviour in the UE also, given that limitations do apply anyhow.
    “If the serving network does not support SRG information, the UDM determines based on the subscription information which S-NSSAIs can be sent to the AMF, so that all S-NSSAIs provided to the serving network are allowed to be present simultaneously in the Allowed NSSAI”
  See S2-2102773r05 and S2-2102800r03

## Slide 3: WF: Decide whether to pursue A or B
Approach A
  See S2-2102773r04 and S2-2102800r02
Approach B
  See S2-2102773r05 and S2-2102800r03