## Slide 1: KI#6 WF discussion

## Slide 2: Snapshot of status from CC#2 (skip in CC#3)
After extensive online and offline discussion which resulted in the multicompany input being updated to allow a S-NSSAIs to have multiple SRG membership (as in Huawei and Ericsson independent proposals), we are at a point where two approaches have been identified
Approach A (supporting companies+Ericsson):
  the Configured NSSAI with all S-NSSAIs in subscription information with any SRG value is provided only to supporting UEs (alongside SRG information so the UE can avoid attempting to register with SRG-incompatible slices).
  Non-supporting UEs and non-supporting VPLMNs only get the S-NSSAIs with SRG=0, which includes the default S-NSSAIs.
  Main goal (or benefit) is to have deterministic behaviour at all times
  A UE Always attempts to register with compatible slices by definition unless it needs an updated configuration (i.e. the SRG information has changed in the subscription but the UE is not yet up to date).
  Huawei argue providing legacy UEs with a reduced set of SRG-compatible slices with SRG=0 (as non supporting VPLMNs) is an unacceptable downside of this solution
  The supporting companies argue that a default minimum set of sliced for not supporting UE and PLMNs need to be understood anyhow by the customers.
  See S2-2102773r04 and S2-2102800r02
Approach B (Huawei):
  A supporting network is not aware of whether a UE supports the feature or not so any UE is provided a Configured NSSAI with all S-NSSAIs in subscription information irrespective of the SRG value, and the SRG value is provided to all UEs but some may not understand it and the network does not know which do not understand it
  Non-supporting VPLMNs only get the S-NSSAIs with a certain SRG value decided by the HPLMN, which conceivably include the default S-NSSAIs
  Main goal (or benefit) is to not exclude any S-NSSAI with SRG values in subscription from the ability of a legacy UE to use it
  The Companies in the other camp argue that some unpredictable non deterministic behaviour can be expected in the system and this may harm the UE, the network, or both. The behaviour of non supporting UEs when some requested S-NSSAIs are not allowed is not known. Besides there is still the limitation of non supporting VPLMNs that is likely to lead to the same reduced set of S-NSSAIs in both solutions can only be guaranteed for roaming UEs so the main benefit of this solution is not achieved in this case at least. It is not clear why the limitation for non supporting PLMN is not applied also to not supporting UEs to achieve deterministic behaviour in the UE also, given that limitations do apply anyhow in roaming to non supporting VPLMNs and customers should decide which is the basic set of slices to use anyhow.
    “If the serving network does not support SRG information, the UDM determines based on the subscription information which S-NSSAIs can be sent to the AMF, so that all S-NSSAIs provided to the serving network are allowed to be present simultaneously in the Allowed NSSAI”
  See S2-2102773r05 and S2-2102800r03

## Slide 3: Snapshot of status for CC#3
Approach A (unchanged in substance from r01 and r04)
  Changed: now the SRG=0 is replaced by the SRG for the Default S-NSSAI(s). A default S-NSSAI at least is assumed to be present in a subscription including the SRG values.
  All is the same as in r04 except a note is added that a supporting PLMN and its supporting roaming partners may configure the Non-supporting UEs with all the S-NSSAI in subscription the supporting AMF receives, but this is not a recommended behaviour the UE behaviour is not predictable.
  See S2-2102773r09
Approach B:
  Adds the indication of support by the UE and the option to handle supporting UEs as in r04/r09 BUT
  A HPLMN sends a dynamically determined SRG to a non supporting PLMN, without specifying it is the same as the one a supporting PLMN send to a non supporting UE (which may be specified by an additional indicator stating which SRG is the default SRG, optionally).
  The Supporting AMF can send to the non supporting UE either all the S-NSSAIs or the ones of the default SRG if the default SRG indication is received.
  The Companies in the other camp argue that a consistent and predictable service experience shall require the same group is sent to a non supporting VPLMN and a non supporting UE (as in r01, and r04). This should be the standard behaviour. Also it is unacceptable the HPLMN unilaterally by not providing an indication of default SRG decides what the VPLMN shall do and the VPLMN has to suffer of any unpredictable UE-network interaction based on unilateral HPLMN decision. However we can live with a bilateral agreement as a non-recommended by 3GPP exception, as in r09.
  See S2-2102773r07

## Slide 4: WF: Decide whether to pursue A or B
Approach A
  See S2-2102773r09
Approach B
  See S2-2102773r07