## Slide 1
PCF authorizing MBS Session policy - For discussion

## Slide 2
MB-PCF authorizing MBS Session for both broadcast and multicast MBS Session
PCF
MB-SMF
NEF/MBSF
AF
MB Session Start (service requirement)
MBS Policy Association Req/Resp
Currently message flow (concluded in TR 23.757)
  MB-SMF optionally interacts with PCF at MBS Session Start/Stop
    Using similar approach as SMF interacting PCF at PDU Session establishment
  MBS Session policy expected to be very simple
    E.g. MBR/GBR/5QCI/ARP authorized for a certain application
Ericsson comment in r1:
Brought back this slide (removed by Nokia) to show what is the current status, and Ericsson’s understanding what policy/QoS could be authorized by PCF for MBS Session.

## Slide 3: Related TDOCs
Tdoc number | Title | Source | Affected clauses |  |  |  |  |  | Note | WF proposal
 |  |  | Annex A | 9.X (General description) | 9.Y (PCF service with SMF) | 9.Z (PCF service with NEF) | 7.1.1 | 6.6 |  | 
S2-2102726 | 23.247: MBS Application and Service Configuration Options | Tencent |  |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102439 | 23.247: Policy control for Multicast and Broadcast services | CATT |  |  |  |  |  |  | General description | 
S2-2102946 | 23.247: PCF service for Interactions between MB-SMF and PCF. | Nokia |  |  |  |  |  |  | Interaction between MB-SMF and PCF | Separate one
S2-2102724 | 23.247: Requested MBS QoS and Dynamic PCC | Tencent |  |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102725 | 23.247: MBS Session-AMBR | Tencent |  |  |  |  |  |  | Session AMBR for MBS should be considered for individual delivery | Separate one
S2-2102947 | 23.247: NEF PCF interactions. | Nokia |  |  |  |  |  |  | Interaction between NEF and PCF | 
Tdoc number | Title | Source | Affected clauses |  |  |  | Note | WF proposal
 |  |  | 7.3.1 | 7.3.2 | 7.3.3 | 7.3.x |  | 
S2-2102728 | 23.247: Update MBS Session Establishment for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102729 | 23.247: Update MBS Session Update for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102730 | 23.247: Update MBS Session Release for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
Tdoc number | Title | Source | Affected clauses |  |  |  |  | Note | WF proposal
 |  |  | 7.1.1 | 7.1.2 | 7.1.1.x de-configuration | 7.1.1.y configuration update | 7.2.1.3 |  | 
S2-2102354 | 23.247: Update on common procedures for multicast and broadcast services | Samsung |  |  |  |  |  | Adding de-configuration and configuration update procedure | Should be merged into one
S2-2102392 | 23.247: Updates for MBS session configuration | Huawei |  |  |  |  |  | Timing of establishing N6 connection | 
S2-2102437 | 23.247: Procedures of configuration for MBS | CATT |  |  |  |  |  |  | 
S2-2102673 | 23.247: [7.1.1]-Update to configuration procedures | vivo |  |  |  |  |  | Separate the “big” configuration procedure. | 
S2-2102727 | 23.247: Update the MBS Session Configuration Procedure | Tencent |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102338 | 23.247: Clause 7.1.1: Clarification on MBS service area | LG Electronics |  |  |  |  |  |  | 

## Slide 4: Different proposed options
Option 1 (currently concluded in TR 23.757 Ericsson proposal, no CR)
  Service requirements are included in message from NEF to MB-SMF and then forwarded to PCF
PCF
MB-SMF
NEF/MBSF
AF
MB Session Start (service requirement)
MBS Policy Association Req/Resp
Ericsson comment in r1:
Ericsson reminds Nokia (Thomas) that the PCF interaction illustrated here is also proposed in Nokia Sol#3 in TR23.757 and included in conclusion (clause 8.2.3)

## Slide 5: Different proposed options
Option 2 (Tencent)
  If PCF is used, it triggers establishment of MBS context at MBS

## Slide 6: Different proposed options
Option 3 (2947 (Nokia), 2673(Vivo)?, 2439 (Intel, Lenovo, Tencent, Motorola Mobility)?)
  Similar to existing PCC
  Session binding based on MBS session context at PCF
  For initial configuration, NEF can store session information in database and/or establish PCC authorization session
  For updates, direct interaction between NEF and PCF
  PCF retrieves stored configured session information from database (Nokia: UDM, Vivo: UDR)
  BSF used to discover PCF with MBS session context

## Slide 7: Comparison of Options
Option 1
  Unclear how policy authorization requests can be rejected
  Large containers might be required for service decription
  MB-SMF would be affected for service informnation updates even if PCF does not updated authorized QoS
  Unclear how PCF can use preconfigurede input for policy decisions (without database access)
Option 2
  Substantial change of MB-SMF PCF interactions compared to existing PCFSmPolicyControl (might become an MB-SMF service)
  Unclear how PCF can use preconfigurede input for policy decisions (without database access)
Option 3
  Aims for alignment with existing PCC procedures

## Slide 8
Answers to Questions by Ericsson
S2-2102947 NEF PCF interactions
Q2: why is BSF is needed?
Nokia reply: BSF enables AF and or MB-SMF to detect PCF. (Depending on what entity contacts PCF first, the other needs to contact same PCF for session binding)
MB-PCF
MB-SMF
AF
MB Session Start (service requirement)
Authorizing MBS Session
MB Session Start Response
Q1: For trusted AF, NEF may not be needed. If so, public safety AS would be impacted to do authorization first and then do MBS Session start ?
Nokia Reply: Public safety would use MB2 interface and MBSF. Thus, no impact
Ericsson comment in r1:
Nokia seems to assume that 5MBS can only be used for Public Safety via MB2 and there is no possibility to adapt to SBI architecture, which in my view is a severe limitation of 5MBS.
Ericsson comment in r1:
What do we want to achieve with PCF for MBS Session management ? Why introducing such complexity?

## Slide 9
Answers to Questions by Ericsson
S2-2102727 Update the MBS Session Configuration Procedure
Q: Establishment or Notify?
Notify does not work as there is no MBS policy association established yet.
Nokia: Agree, would need to be establishment

## Slide 10
Answers to Questions by Ericsson
S2-2102439 Policy control for Multicast and Broadcast services
Q1: Why is Session binding needed?
Nokia: AF and MB-SMF both establish connections towards the PCF
Q3: MB-SMF interacts with PCF when AF started the MBS Session, but not at UE join.
Nokia: I agree. MB-SMF is unaware of UUs joining
Q2: Do we have some examples what PCRT may be needed?
Nokia: I left that FFS in my service proposal. Might be that we have nothing in the first release. Also depends on information provided by AMFs and SMFs
Ericsson comment in r1:
Why should both AF and MB-SMF establish connection towards the PCF?

## Slide 11
Thank You!