## Slide 1: SA2#145e eNPN preparation conference call
20210512

## Slide 2: Revisions of approved CRs
There are a number of cases with multiple versions of revised CRs that were approved at the last meeting
  In some cases it seems there were no off-line discussions prior the meeting or discussions took place while no agreements could be made
  Proposal: can we keep one mail thread at the meeting using the tdoc with first source company from SA2#144E?
    Discussions of course need to take into account proposals from other revisions.

## Slide 3: UE capabilities for additional parameters using UPU
CT1 options:
  Alternative-1: in the UPU transparent container carrying the UPU acknowledgement; or
  Alternative-2: in the registration request message during the registration procedure.
S2-2104336 stating
  SA2 preference is to minimize the impacts on AMF as to easier enable the use of extended UPU also in roaming scenarios.
  SA2 will align the SA2 specifications with the CT1 and SA3 specifications, if needed.
S2-2104584 stating
  SA2 discussed the alternative options provided by CT1 and decided that Alternative-1 is the most appropriate. SA2 suggests CT1 to take the lead and standardise this option and SA2 will later align accordingly
S2-2104602 stating
  In Alt. 1, it is possible that the UPU procedure cannot be initiated when the UE is in SNPN access mode or accesses an SNPN via a PLMN as described in CT1 LS. In this case, the UE cannot indicate the supported parameters update data set type to the network.
  Given the above, and comparing these two alternatives, SA2 decided to include Alt.2 (see attached CR) allowing the UE to inform the network about which parameter(s) are supported in the UPU procedure prior to initiating the UPU procedure.
Way forward?
  ..
 | S2-2103760 | LS In | Action | LS from CT WG1: Reply LS on UE capabilities indication in UPU | CT WG1 (C1-212599)
 | S2-2104336 | LS OUT | Approval | [DRAFT] Reply LS on UE capabilities indication in UPU | Ericsson
 | S2-2104584 | LS OUT | Approval | [DRAFT] Reply LS on UE capabilities indication in UPU | Qualcomm
 | S2-2104602 | LS OUT | Approval | [DRAFT] Reply LS on UE capabilities indication in UPU | MediaTek Inc.
 | S2-2104603 | CR | Approval | 23.501 CR2949 (Rel-17, 'B'): The supported parameters set type indication for UPU | MediaTek Inc.

## Slide 4: KI#1: Interface between AAA-S and SNPN
Only submitted option is using NSSAAF as interworking between SBI and AAA protocols:
  AUSF shall discover and select the NSSAAF, and then forward EAP messages to the NSSAAF. The NSSAAF selects AAA Server based on the domain name corresponds to the realm part of the SUPI, relays EAP messages between AUSF and AAA Server (or AAA proxy) and performs related protocol conversion.
Proposed way forward is to progress the proposal using NSSAAF
S2-2104442 | CR | 23.501 CR2926 (Rel-17, 'C'): Interaction between AUSF and AAA Server | CATT, Ericsson, Huawei, Nokia, Nokia Shanghai Bell
S2-2104443 | CR | 23.502 CR2820 (Rel-17, 'C'): Add a new NSSAAF service to support interaction between AUSF and AAA Server | CATT, Ericsson, Huawei, Nokia, Nokia Shanghai Bell

## Slide 5: Updating CH controlled lists for SNPN selection
CT1 indicated preference for UPU over SoR, SA3 has not yet replied
CRs from Huawei, Ericsson and MediaTek propose to use UPU, but CR from Xiaomi propose to use SoR
Way forward:
  Can we progress UPU?
S2-2103747 | LS In | Reply LS on updating the Credentials Holder controlled lists for SNPN selection | CT WG1 (C1-212419)
S2-2104176 | CR | 23.501 CR2754R1 (Rel-17, 'F'): Update of CH controlled prioritized list of preferred SNPNs and GINs | Huawei, HiSilicon
S2-2104215 | CR | 23.502 CR2789 (Rel-17, 'F'): Update of prioritized list of preferred SNPNs and Group IDs to the UE | Huawei, HiSilicon
S2-2104352 | DISCUSSION | Discussion for updating the preferred list. | Xiaomi
S2-2104353 | CR | 23.502 CR2717R1 (Rel-17, 'B'): Support for update of Credentials Holder controlled prioritized list of preferred SNPNs | Xiaomi
S2-2104356 | CR | 23.501 CR2839R1 (Rel-17, 'B'): Support for update of Credentials Holder controlled prioritized list of preferred SNPNs | Xiaomi
S2-2104338 | CR | 23.502 CR2801 (Rel-17, 'B'): Additional parameters using UE Parameters Update via UDM Control Plane Procedure | Ericsson
S2-2104606 | CR | 23.501 CR2951 (Rel-17, 'B'): Updating the Credentials Holder controlled lists for SNPN selection | MediaTek Inc.
S2-2104607 | CR | 23.502 CR2846 (Rel-17, 'B'): Updating the Credentials Holder controlled lists for SNPN selection | MediaTek Inc.

## Slide 6: Handling of SUCI/SUPI format for CH selection
S2-2103978 see next 3 slides
S2-2104332 issue: “if the SNPN and the Credentials Holder are using the same PLMN ID and IMSI based SUPI is used, currently the HNI(MCC/MNC) of the corresponding SUCI is not able to distinguish if the UE is from the Credentials Holder or if the UE is a native subscriber.”
  Option 1.
  UE indicate NID of subscribed SNPN or indicate it is using PLMN subscription. AMF in serving SNPN will be able to distinguish if UE is from another SNPN or it is from PLMN, even when another SNPN or PLMN is using the same MCC/MNC as the current serving SNPN. AMF is able to use this information to perform AUSF/UDM selection.
  Option 2
  Except HNI in SUCI, other parts of the SUCI can be utilized for differentiating the serving SNPN and the Credentials Holder, for example the Routing Indicator. Then, if SNPN and Credentials Holder are using the same MCC/MNC, the Routing Indicator must be coordinately assigned for each network. Furthermore, there is a recent development in CT4 to add home network public key id in the SUCI as query parameter(C4-210158) which has the potential to be enhanced for the use case of access to SNPN with CH.
  Option 3
  When IMSI based SUPI is used, SNPN must choose different PLMN ID than Credentials Holder in order to establish relation with the Credentials Holder. Credentials Holders do not share the same PLMN ID.
S2-2103978 | DISCUSSION | Discussion on the format of SUPI/SUCI used to access to a SNPN | vivo
S2-2103979 | CR | 23.501 CR2830R1 (Rel-17, 'B'): Handling of SUPI/SUCI format of a UE from credentials holder when accessing to a SNPN | vivo
S2-2104332 | CR | 23.501 CR2919 (Rel-17, 'B'): KI#1 T3: Handling of SUPI/SUCI format when accessing to a SNPN | Ericsson

## Slide 7
Issues from S2-2103978
In rel-17, an SNPN-1 can be accessed by a UE from Credentials Holder, e.g. SNPN-2 UE or a PLMN UE. Two issues raised when IMSI format SUPI is used
  Issue#1 how the AMF in SNPN-1 knows the NID of the SNPN-2 UE.
    There is argument that the following note in 23.501 is sufficient to fix Issue#1.
      “NOTE 1: When Credentials Holder is an SNPN, and the MCC and MNC of the SNPN is not unique, then IMSI based SUPI is not supported as the MCC and MNC need not be unique always; instead USIM credentials are supported using Network Specific Identifier based SUPI.”
    However, “not unique” can be understood as 1) not unique to identify a PLMN, e.g. value “999”; or 2) unique to identify a PLMN, but is not unique to identify a SNPN, shall use NID together. We believe 1) is the correct understanding for the note, so Issue#1 still exits.
  Issue#2 how to distinguish SNPN-1 and PLMN in case their MCC and MNC are same.
    There is argument that it is a corner case. However, NID is introduced because PLMN ID are not sufficient to identify SNPN. So a PLMN and a SNPN having the same PLMN ID is not a corner case.

## Slide 8
Solution option for Issue#1 from S2-2103978
Solution option for Issue#1
Option#1: When Credentials Holder is an SNPN, in case of SNPN-2 UE accessing to SNPN-1 and using IMSI based SUPI, it additionally provides its NID in the Registration Request message. The AMF in SNPN-1 use the PLMN ID of the SUPI and NID in the Registration Request message for AUSF/UDM selection.
Option#2: Update the Note “When Credentials Holder is an SNPN, and the MCC and MNC of the SNPN is not unique, then IMSI based SUPI is not supported as the MCC and MNC need not be unique always; instead USIM credentials are supported using Network Specific Identifier based SUPI.” as “When Credentials Holder is an SNPN, USIM credentials uses Network Specific Identifier based SUPI.”
Proposal1: It is proposed to take the above options into account.

## Slide 9
Solution option for Issue#2 from S2-2103978
Solution option for Issue#2
Option#1: When Credentials Holder is an PLMN, when the PLMN ID of the SNPN accessing by the UE and PLMN are same, the UE use the NSI based SUPI to access the SNPN.
Option#2: When Credentials Holder is an PLMN, the UE use the NSI based SUPI to access the SNPN.
Proposal1: It is proposed to take the above options into account.

## Slide 10: Handling of SUCI/SUPI format for CH selection
23.501 states:
  “Network Specific Identifier are not supported for the case the Credentials Holder is provided by a PLMN”
  “PLMN operator can use its own PLMN IDs for SNPN(s) along with NID(s),”
Way forward?
  For support of CH as SNPN
    …
  For support of CH as PLMN
    …

## Slide 11: Whether to document registration procedure as part of existing procedure or separately
Both S2-2104229 and S2-2104622 proposes separate clause, while S2-2104692 re-uses existing clause
Way forward:
  Propose to document onboarding registration procedure in a separate clause
S2-2104229 | CR | 23.502 CR2632R2 (Rel-17, 'B'): Registration Procedure for UE Onboarding | [Intel, Ericsson, MediaTek Inc.], Huawei
S2-2104622 | CR | 23.502 CR2849 (Rel-17, 'B'): Registration procedure for UE onboarding SNPN | Intel, Nokia, Nokia Shanghai Bell, Ericsson
S2-2104692 | CR | 23.502 CR2860 (Rel-17, 'B'): Onboarding Indication in RRC Connection Establishment | Samsung