## Slide 1: FS_DetNet discussion status before SA2#152E
Ericsson

## Slide 2
Agenda
Intro [György]
Resolution of FFS items:
  Documents from China Telecom on Solution 2 and Solution 6.
  Document from Ericsson on Solution 3.
  Any additional FFS discussion if solution authors are present.
Review and discuss the list of main open questions.
Wrap-up: discuss the way forward

## Slide 3
DetNet study status
8 solutions documented for the 2 KIs
Many FFSs remain in the solutions
In next SA2 meeting in August, study must conclude according to work plan
Preparation before SA2#152E:
  Target: resolve as many FFS as possible
  Additional CC/email follow-up may be needed
  Resolution of FFSs masy be merged into a single rapporteur input document before the meeting
  Note the strict agenda budget for upcoming meeting: 7 documents according to workplan
Normative phase planned for Jan-Feb 2022
Subsequent slides show main differences between the solutions as input to the evaluation

## Slide 4
Outstanding main issues
Solution # | 1 (Ericsson) | 2 (China Telecom) | 3 (Ericsson) | 4 (Huawei) | 5 (ETRI) | 6 (China Telecom) | 7 (ZTE) | 8 (Nokia)
Key issue # | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 1, 2
Which protocol is used between 5GS and DetNet controller? | YANG over Netconf or Restconf, i.e., IETF protocol | 3GPP | YANG over Netconf or Restconf, i.e., IETF protocol |  | 3GPP | FFS | YANG over FFS | YANG over Netconf or Restconf
Is an optional NEF supported between TSCTSF and DetNet controller? If so, what is the protocol stack used? | No | Yes, NEF is mandatory. | No | Yes | FFS whether NEF is used, FFS how to extend Restconf | Yes. NEF protocol conversion between Netconf/Restconf and 3GPP. | FFS | No
Which entity collects and provides exposure information to the DetNet controller? | TSCTSF | NEF |  |  |  |  |  | TSCTSF
How do we map e2e DetNet requirements to per 5GS requirements? |  |  | Pre-configured TSCTSF mapping or YANG extension | FFS |  | FFS | FFS | We use DetNet controller parameters as 5GS specific QoS requirement.
How is routing information handled? |  |  | TSCTSF verifies routes provided by DetNet controller |  |  |  |  | NW-TT uplink routing exposed to DetNet controller

## Slide 5
KI#1: Information reporting from 5GS to DetNet controller
Solution # | 1 (Ericsson) | 8 (Nokia)
Interface identifier | Yes | Yes
Type of interface | Yes | Yes
IP address, | Yes | Yes
subnet (prefix length) | Yes | Yes
Neighbour address(es) | Yes | 
Node ID | Yes | Yes
MAC address |  | Optional
MTU size |  | Optional
NW-TT routing table | No | Yes

## Slide 6
KI#2: Parameter mapping from DetNet controller to 5GS.
Solution # | 3 (Ericsson) | 4 (Huawei) | 6 (China Telecom) | 7 (ZTE)
Max-latency | Required delay | QoS req. | PDB | 
Min-bandwidth | GFBR | QoS req. | GFBR | 
Max-loss | PER | QoS req. | Error Rate | maxPacketLossRate
Max-latency-variation | - | -, TBD |  | 
Max-consecutive-loss-tolerance | - | -, TBD |  | Survival time
Max-misordering | - | -, TBD |  | 
Interval | Periodicity | TSC info |  | Periodicity
max-pkts-per-interval | Max burst size, MFBR | -, TBD |  | Max burst size
max-payload-size |  | -, TBD |  | 
min-pkts-per-interval | - | -, TBD |  | 
min-payload-size | - | -, TDB |  |