## Slide 1: Discussion on PIN issues and corresponding proposals
Zhenhua Xie
vivo
S2-2209007

## Slide 2
Issue of whether 5GC is responsible for PIN management
Assumption:
  Meaning of PIN management
    A: resources configuration/deconfiguration related to a PIN, including setup/delete PDU Sessions related to a PIN (URSP/PIN Routing Selection Policy generation and provisioning)
    B: resources status/QoS authorization related to a PIN, including, modify QoS authorization for a PIN, activation/deactivation a PIN
    C: traffic QoS and routing control
    D: member modification for a PIN (PEMC, PEGC, and PINE)
  NEF exposes APIs for A, B and C, and PCF/SMF handling the requests. The NEF APIs are, e.g.,
    A: Create/Delete PIN (PIN ID) (expose nothing)
    B: Modify PIN (PIN ID, QoS auth info) (expose QoS authorization info)
    B: Activate/Deactivate PIN (PIN ID) (expose nothing)
    C: Modify PIN (PIN ID, packet filters, QoS) (expose topology and communication type/style)
  PEGC and SMF support C
    UE (PEGC) initiates PDU Session Modification, which eliminates exposure of topology and communication type (voice, video, etc.)/style (e.g., who’s server/client)
Questions:
  Whether does NEF expose APIs for D?
    E.g., Create/Modify PIN (PIN ID, PEMC IDs, PEGC IDs, PINE IDs) (expose member info)
  Should it be possible for PEGC and SMF to do B, and D？
    E.g., over PDU Session Modification, which eliminates exposure of everything
Proposal:
  TBD (both supported?)

## Slide 3
Issue of identification
Questions:
  Whether PIN ID needs to be known by 5GC?
    Data KEY of Policy and QoS related to a PIN
    May be Data KEY of members (PEMC, PEGC, PINE) related to a PIN if 5GC needs to store member information
  Whether PIN ID is allocated by 5GC?
    AF allocates, AF ID + PIN ID is unique
    5GC (i.e., NEF) allocates a unique ID (like NEF allocates Reference ID for some operations)
  Whether PINE ID needs to be known by 5GC
    If 5GC knows PINE ID, is it a kind of management on PIN (storage)?
    What is the usage of the PINE ID by 5GC except storage?
Proposal:
  TBD (e.g., is aware of at least PIN ID)

## Slide 4
Issue of non-3GPP QoS assistance information and proposal
Interim conclusions:
  5G QoS parameters (including QoS characteristics, GFBR/MFBR) may be sent to PEGC to assist the deriving of N3GPP QoS parameters
  5GC may take into account the delay budget between PINE and PEGC to guarantee the end to end delay for PINE traffic.
Issue:
  “5G_QOS_INFO” described in TS 24.502 is sent by N3IWF/TNGF to UE when initiating child SA creation, the Additional QoS Info in the 5G_QOS_INFO may include (table 9.3.1.1-2 of 24.502):
    QoS characteristics (resource type: GBR, Delayed critical GBR, non-GBR; priority level: 1-127; PDB; PER; AW; MDBV)
    Maximum Flow Bit Rate downlink (MFBR downlink);
    Maximum Flow Bit Rate uplink (MFBR uplink);
    Guaranteed Flow Bit Rate downlink (GFBR downlink);
    Guaranteed Flow Bit Rate uplink (GFBR uplink);
    Notification Control;
    Maximum Packet Loss Rate downlink; and
    Maximum Packet Loss Rate uplink.
  It is N3IWF/TNGF instead of 5GS that generates Additional QoS Info who takes into account the 5G QoS profile received via N2 instead of N1
  The “Additional QoS Info” is used for the access between UE and N3IWF, instead of the other side.
Proposal:
  TBD

## Slide 5
Issue of URSP and proposal
Traffic descriptor (TD) of URSP rule:
Alternative solutions:
  Alt#1: Extend TD of URSP for PIN traffic mapping, e.g., using “source descriptors” or “gateway descriptors”
  Alt#2: Do not extend URSP, but provisioning mapping info with URSP, e.g., TD uses DNN, and mapping info is <PIN ID, DNN>
  Other possible ways
Proposal:
  TBD (e.g., both URSP and PIN Routing Selection Policy is delivered to PEGC)
Information name | Description | Note
Application descriptors | It consists of OSId and OSAppId(s). | The information is used to identify the Application(s) that is(are) running on the UE's OS. The OSId does not include an OS version number. The OSAppId does not include a version number for the application
IP descriptors | Destination IP 3 tuple(s) (IP address or IPv6 network prefix, port number, protocol ID of the protocol above IP). | A URSP rule cannot contain the combination of the Traffic descriptor components IP descriptors and Non-IP descriptors
Non-IP descriptors | Descriptor(s) for destination information of non-IP traffic | 
Domain descriptors | Destination FQDN(s) or a regular expression as a domain name matching criteria. | 
DNN | This is matched against the DNN information provided by the application. | 
Connection Capabilities | This is matched against the information provided by a UE application when it requests a network connection with certain capabilities. (NOTE 4) | The format and some values of Connection Capabilities, e.g. "ims", "mms", "internet", etc., are defined in TS 24.526 [19]. More than one connection capabilities value can be provided

## Slide 6
Issue of PDU Session number per PIN and proposal
Interim conclusion:
  A PEGC may establish a Single or multiple PDU Sessions used for PIN communication. One PEGC may serve more than one PIN and in this case, there is at least one PDU session per PIN
Other proposal:
  Shared PIN session that a PEGC transfers traffic of multiple PINs and other APP
  Dedicated PIN session that PEGC transfers traffic of one or multiple PINs
  Dedicated PIN session that per PDU session per PINE
Issue:
  Not clear what is the purpose for a PIN to have more than one PDU Sessions per PEGC
  QoS differentiation is able to be done by QoS flows
  If one PIN at a PEGC has two PDU Sessions is allowed, it is same that divide the PIN into two, and one per PDU Session
  If multiple PINs at a PEGC share one PDU Session, it is same that combines those PINs as one big PIN and uses sub-networks by PEMC/AF for those original PINs
Proposal:
  TBD (e.g., only one PDU session per PIN per PEGC/PEMC)