## Slide 1
KI#4 Common EAS, Common DNAI Selection

## Slide 2
Some remaining issues for KI#4:
How AF provide common EAS, common DNAI.
How Traffic Correlation ID is designed.
Where the 5GC selected common EAS/DNAI shall be stored.
How to coordinate among SMFs.
KI#4: Influencing UPF and EAS (re)location for collections of UEs

## Slide 3
1.How AF provide common EAS, common DNAI
AF
NEF
UDR
SMF(s)
PCF(s)
Nnef_TrafficInfluence(correlation indication, common EAS/DNAI)
Storing the information
Nudr_DM_Notify
Npcf_SMPolicyControl_UpdateNotify(correlation indication, common EAS/DNAI)
Common EAS/DNAI selection for a set of UEs
AF
NEF
UDR
SMF(s)
PCF(s)
Nnef_TrafficInfluence(correlation indication, group id)
Storing the information
Nudr_DM_Notify
Npcf_SMPolicyControl_UpdateNotify(correlation indication, group id)
Common EAS/DNAI selection for a set of UEs
UDM
Nnef_ParameterProvision(group data(common EAS))
Nudm_SDM_Notification Notify(group data(common EAS))
Optiion#1: Provided by AF Traffic Influence
Optiion#2: Provided by group data
NOTE：as concluded in TR23.700-48, the indication for selecting common EAS/DNAI is provided via AF Traffic Influence

## Slide 4
2.How Traffic Correlation ID is designed.
Traffic Correlation ID is used by SMF to identify a set of UEs, i.e. each UE in the UE set associated with the same Traffic Correlation ID.
SMF
SMF
PCF
UDR
AF traffic influence information data stored in UDR
PCC rule(AF influenced Traffic Steering Enforcement Control, influence-id)
Option#1: “influence-id”of AF traffic influence information data created by UDR is used as Traffic Correlation ID
Assuming only one UDR for the set of UEs
UDR
PCF
NEF
AF
Option#2: AF provides Traffic Correlation ID in AF request
AF Request(Traffic Correlation ID)
PCC rule(Traffic Correlation ID)
In some cases, the group id can be used as Traffic Correlation ID

## Slide 5
3.In case the common EAS/DNAI is selected by 5GC, where the common EAS/DNAI shall be stored.
Option#1: stored as part of AF Traffic influence information data in UDR
Option#2: stored as part of group data in UDR
Because the group data only exist when the dynamic group is used, but the AF Traffic influence information data always exist no matter whether the dynamic group is used or not, so Option#1 is proposed.
In KI#4 conclusion:
The UEs in the UE collection are identified by a UE list, group ID or any UE may be used. Optionally, Spatial Validity Condition, may be used to limit the UEs in the UE collection to a specific area.

## Slide 6
4.How to coordinate among SMFs.
Option#1:
Option#2:
SMF-1
SMF
SMF
SMF
New service(UE location etc)
One SMF（SMF-1） collects UE information from other SMFs and determine the common DNAI.
- SMF-1 could be discoveryed via BSF.
- new service between SMFs.
After a common EAS/DNAI is determined by a SMF, it’s stored in UDR, and UDR notifies other SMFs serving UEs from a set of UEs.

## Slide 7
Thank you