## Slide 1: AIMLsys KI#6 discussion: AIML traffic detection and 5QIs
Samsung

## Slide 2: Resolving Editor’s note on AIML traffic detection
An Editor’s note in S2-2301580 on AIML traffic detection needed to be resolved.
‘Editor’s Note: Whether application AI/ML traffic can be detected is FFS.’
Considering the characteristics of the AIML traffic, AIML traffic detection will be needed to assist the operators in organising the AIML service and applying various charging policies.
  High traffic volume for DL and UL, multiple rounds transmission during model training, a large number of UEs, high reliability requirements for model downloading etc.
Otherwise AI/ML and non-AI/ML traffic from the same application cannot be differentiated
Potential solutions to detect AIML traffic by 5GC:
  UE indicates that the PDU session carries AIML traffic via NAS,
    e.g. the UE includes PDU Session Pair ID and MBS container request in PDU session establishment/ modification for URLLC and MBS services.
  Based on QoS requirements, i.e. according to the 5QIs for AIML services.
  Other solutions are welcome 

## Slide 3: 5QIs for AIML services
In the last meeting, LS was sent to SA1 in S2-2301578 to check the AIML KPI values in TS 22.261. e.g., whether the 2ms latency is feasible for 5GS.
In S2-2300670, OPPO pointed out that Max allowed UL end-to-end latency in SA1 is different from the Packet delay budget in QoS parameters in SA2 and clarified that SA2 should discussion the PDB.
No existing standardised 5QI cannot meet the following requirements:
  e.g. PDB = 10ms for AI/ML inference between UE and Application Function, reliability 10e-5 (SA1 KPI)
  e.g. PDB = 100ms for AI/ML model downloading/Federated learning, reliability 10e-5 (SA1 KPI)
Table 7.10-1 KPI Table of split AI/ML inference between UE and Network Server/Application function
Uplink KPI |  |  |  |  | Downlink KPI |  |  |  | Remarks
Max allowed UL end-to-end latency | Experienced data rate | Payload size | Communication service availability | Reliability | Max allowed DL end-to-end latency | Experienced data rate | Payload size | Reliability | 
2 ms | 1.08 Gbit/s | 0.27 MByte | 99.999 % | 99.9 % |  |  |  | 99.999 % | Split AI/ML image recognition
100 ms | 1.5 Mbit/s |  |  |  | 100 ms | 150 Mbit/s | 1.5 MByte/‌frame |  | Enhanced media recognition