## Slide 1
)
Rel 18 „Enhancement of support for Edge Computing in 5GC- phase 2”
  Still open, actually one of the main open points for the next meeting, is the DNS traffic forwarding between UE, V-EASDF, HPLMN DNS server

## Slide 2
issue related with DNS traffic forwarding between V-EASDF and HDNS server
Rel 18 „Enhancement of support for Edge Computing in 5GC- phase 2” / HR-SBO
Issue is that VPLMN and HPLMN may each use private IP addressing on N6 + inter PLMN security
V-UPF
V-EASDF
H-UPF
H DNS server
N3
N9
Direct exchange not possible
VPLMN private addressing on N6
N6
N6
UE
RAN
HPLMN private addressing on N6
IPUPS
IPUPS
GTP-u tunelling over N3/N9 hides private IP addresses
Direct exchange between V-EASDF and HPLMN (HDNS) DNS server not possible
Reusing IPUPS allows reuse of existing Inter PLMN security mechanism

## Slide 3
Solution: traffic to be tunnelled on the N9 tunnel of the PDU Session  No Change to HPLMN
Rel 18 „Enhancement of support for Edge Computing in 5GC- phase 2” / HR-SBO
V-SMF to control tunnelling between V-EASDF and V-UPF
V-UPF
V-EASDF
H-UPF
H DNS server
N3
N9
Direct exchange not possible
UL 1
UL 2
UL 3
DL 1
DL 2
DL 3
UL DNS request from UE to HDNS server
  .UL1 from UE to EASDF: per existing specs
  UL 2 from V-EASDF to the N9 tunnel of the PDU Session: V-EASDF needs to tunnel the DNS request to the V-UPF and V-UPF controlled by V-SMF to inject traffic from this tunnel to the N9 tunnel of the PDU Session
  UL3 Then traffic handled per existing specs
DL DNS response from HDNS server to UE
  DL1: from HDNS server to VUPF : per existing specs
  DL2: from the N9 tunnel of the PDU Session to V--EASDF : V-UPF needs to tunnel the DNS response to the V-EASDF (V-UPF controlled by V-SMF)
  DL3 Then traffic handled per existing specs

## Slide 4
Solution: traffic to be tunnelled on the N9 tunnel of the PDU Session  No Change to HPLMN
Rel 18 „Enhancement of support for Edge Computing in 5GC- phase 2” / HR-SBO
V-SMF to control tunnelling between V-EASDF and V-UPF
V-UPF
V-EASDF
H-UPF
H DNS server
N3
N9
Direct exchange not possible
UL 1
UL 2
UL 3
DL 1
DL 2
DL 3
V-SMF for UL DNs traffic
  Gets (UL) Tunnel termination from V-UPF (per UE)
  Controls V-EASDF to send DNS requests not matching other DNS message detection rules towards HDNS server over the tunnel to V-UPF
  V-UPF controlled by VSMF to forward over N9 UL traffic received in the per UE tunnel (from V-EASDF)
V-SMF for DL DNs traffic
  Gets (DL) Tunnel termination from V-EASDF
  controls V-UPF to forward DL traffic received over N9 from HDNS Server in the tunnel to V-EASDF