## Slide 1: HR-SBO: Overlapping UE IP addresses for V-EASDF

## Slide 2: Background
S2-2302704 includes the proposed changes to KI#1 HR-SBO solution from SA2#155, with the following EN:
  Editor’s note: It is FFS how to route the DNS traffic between the UE and the V-EASDF where multiple DNN networks with the same IP address range are deployed in different HPLMNs or in the same HPLMN
There have been 3 proposals to handle the issue:
  Separate the local part of DN corresponding to the HPLMN DN (S2-2302771)
  Apply N6 routing tunnel between the L-UPF and V-EASDF(S2-2302771)
  Translate DNS query to unique IP address towards the V-EASDF (S2-2302335)
Notes: . Proposal B impacts EASDF heavily. Tech issue 2 should only propose 1 solution (PCF or UDM) but not both. EN for Tech issue #6 misses the goal to preserve privacy. Tech issue #3 does not deal with the structured information need (there could be issues related to how to handle policy updates and send PCC info per service)

## Slide 3: A. Separate the local part of DN corresponding to the HPLMN DN
SMF selects different Local UPF based on the DNN, S-NSSAI, HPLMN ID and IP Domain
Impacts:
  IP domain of HPLMN is not known by VPLMN  solution is not complete
  Multiple logical UPFs and V-EASDFs scalability
  DNSContext Create/Update to create context w/out UE IP address

## Slide 4: B. Apply N6 routing tunnel between the L-UPF and V-EASDF
V-SMF makes a N6 routing tunnel between the Local UPF and the V-EASDF for routing DNS traffic between the UE and the V-EASDF
Impacts:
  Support of tunnelling in V-EASDF
  N6 routing on UPF
  DNSContext service:
    To create context w/out UE IP address
    To configure tunnel info to EASDF

## Slide 5: C. Translate DNS query to unique IP address towards the V-EASDF
Local PSA UPF for the UE DNS traffic towards the V-EASDF translates the source UE IP address to a unique IP address towards the V-EASDF. Either V-SMF or Local PSA allocates the unique IP address
Impacts:
  Source IP translator functionality in UPF
  N4 for requesting IP translation
Notes:
  Similar functionality already exists in the UPF for the translation of destination IP address
  Translated IP address range need not be a public IP address range

## Slide 6: Evaluation
All solutions have an impact on SMF
Is not complete and does not scale
Impacts EASDF and N6 routing on UPF
Has minimal impact on the UPF