## Slide 1: GMEC: pre-meeting Discussion
SA2#156-e

## Slide 2: Agenda
ENs for Key Issue #1: Enhance group attribute management
ENs for Key Issue #3: NEF exposure framework for provisioning of traffic characteristics and monitoring of performance characteristics
Implementation of conclusion for Key Issue #4: Multiple SMFs for VN group communication
AoB

## Slide 3: KI#1: ENs for Group-MBR
ENs:
  （23501/23503）Editor’s note: If Group-MBR should apply only to 5GVN groups or also to groups created e.g. using O&M is FFS
  （23501） Editor's note: Whether Group-MBR is applicable for 5G VN group only or also for other groups is for further study.
Way Forward：
  OPTION 1 【open】: If Group-MBR should apply to 5GVN groups, the Group-MBR should also apply to other type of groups under certain condition (e.g. group is linked to a DNN, S-NSSAI, and the PDU Sessions are exclusively used for the group traffic)
  OPTION 2【open】: If Group-MBR should apply only to 5GVN groups
  OPTION 3【OUT】: If Group-MBR should apply to 5GVN groups and to groups created e.g. using O&M

## Slide 4: KI#1: ENs for LADN service area
ENs:
  （23501）Editor’s Note: If there is no overlapping between the LADN service area configured in AMF and service area received from UDM, how to handle this case is FFS.
Way Forward：
  OPTION 1 (open): LADN service area received from UDM takes precedence over local configured LADN service area
  OPTION 2【out】: in case of no overlapping, AMF can send the failure result and rejection code to AF via UDM/NEF
  OPTION 3【out】: AMF sends a blank LADN Information to UE
  OPTION 4 (open)：depends on operator policy for which one to take precedence
ENs:
  （23501）Editor’s Note: The SMF does not need to know whether there is a LADN Service Area for a DNN/S-NSSAI, SMF does not need to know the content of the LADN Service Area. Whether this should be reflected in the data provided by UDM is FFS..
Way Forward：
  OPTION 1 : the subscribed LADN service area delivered to the SMF is treated an indication for SMF to activate the LADN per DNN and S-NSSAI, i.e. subscription to "UE mobility event notification" event per DNN and S-NSSAI to receive the notification about the UE presence in the LADN service area
  OPTION 2【out】:UDM sends an indication that LADN service area per DNN and S-NSSAI is activated to the SMF, instead of sending the content of the subscribed LADN service area
  OPTION 3 (preferred, suggested) : AMF sends the an indication that LADN service area per DNN and S-NSSAI is activated to the SMF

## Slide 5: KI#1: ENs for parameters rather other 5G VN group data
ENs:
  （23501）Whether parameters other 5G VN group data (e.g. Expected UE Behavior parameters, Network Configuration parameters, ECS Address Configuration Information etc.) can be used when defining/updating a 5GVN group is FFS.
Way Forward(suggested, texts are open)：
  All the parameters that can be used for the generic groups can also be provisioned for the 5G VN group when establishing or updating a 5G VN group
  AF providing 5V VN group configuration together with those parameters in a single NEF PP service request is one way to achieve this
  As part of dynamic management of the 5G VN group, an AF may also configure and update the service area, QoS or Group-MBR for the 5G VN group as described in clause 5.20b as well as other parameters (e.g. Expected UE Behavior parameters, Network Configuration parameters, ECS Address Configuration Information, etc.) for a 5G VN group as described in clause 4.15.6.2 of TS 23.502

## Slide 6: KI#3: ENs about structure and scenario without TSCTSF
ENs:
  （23501） Editor’s note: It is FFS whether this should be captured in TS 23.503 instead.
Way Forward(suggested)：
  Keep the specification on PCF behavior and AF request information in 503, keep the specification on TSCTSF in 501
ENs:
  （23501） Editor’s note: Further description is FFS, to be done if this option is selected
  （23502） Editor's note: The scenario without TSCTSF can be revisited based on the progress of other work items. Whether an additional signaling route for the direct PCF case is to be supported is FFS.
  （23503） Editor’s note: Further description of the scenario without TSCTSF is FFS
Way Forward：
  Option 1【A potential compromise?】: AF->NEF->UDR->PCF (for non-TSC case, follow the TR conclusion)
    PCF maintains the status of the AF request information for a group, e. g. whether the group member is activated, de-activated, failed, whether to retry in case of failure of GBR QoS, AF request change due to group membership changes
    UDR stores the AF requested QoS
    NEF or PCF: manages the time validity condition?
  Option 2 (open): AF->NEF->TSCTSF->PCF ( same as the case for TSC)
    TSCTSF stores the AF requested QoS, maintains the status of the AF request information for a group, e. g. whether the group member is activated, de-activated, failed, whether to retry in case of failure of GBR QoS, AF request change due to group membership changes, manages the time validity condition
  Option 3 (open): NEF determines based on operator configuration whether TSCTSF is needed

## Slide 7: KI#4: cross-SMF VN group communication
23.501 Clauses Affected:
  4.4.6 5G LAN-type Services
    user plane architecture to support 5G LAN-type service across different SMFs
  5.8.2.13 Support for 5G VN group communication
    Remove the single SMF limitation
    Add support for routing towards “border UPF” or routing between “border UPF”s
  5.29.3 PDU Session management
    Clarify that single SMF is one deployment option, and add support for multiple SMFs or SMF Sets
    Clarify the selection of SMF for a group
  5.29.4 User Plane handling
    Add user plane handling for UPFs served by a single SMF Set
    Add user plane handling for UPFs controlled by different SMF sets
    Clarify that SMF sets/instances share contextual information associated with the 5G VN group (e.g. SMF ID of the SMFs that serve the 5G VN group, UPF ID/Address of the UPFs that serve the 5G VN group, N19 tunnel endpoint for each UPF, UE addresses anchored at each UPF for PDU Sessions established by 5G VN group members) using Network Function/NF Service Context Transfer Procedures described in clause 5.21.4.
  6.2.2 SMF
    Add support functionality for 5G VN group communications across SMFs
  6.3.2 SMF discovery and selection
    Clarify the SMF discovery and selection for a 5G VN group needs to consider Service Area for the 5G VN group
  Annex to how to configure the connection between UPFs of different SMF sets 【open】

## Slide 8: AoB: GMEC-AIMLSys API - KI#5: Allowing UE to simultaneously send data to different groups using different QoS Policy
KI#5 Problem:
  KI#5 intents to achieve Allowing UE to simultaneously send data to different groups with different QoS policy. For the case that A PDU Session targeting a predefined group formed of multiple sub-groups, the UE sends a single packet destined to a multicast address of the combined group which is formed of multiple sub-groups, this can indeed reach multiple destinations and also multiple groups. However, it is not able to support different QoS when forwarding the single multicast packet to different groups in this case, because the QoS policy configured by AF for the combined group using mechanism defined for KI#3 should apply identically for each UE member in the combined group.
Way Forward(open):
  Option 1: enhance mechanism specified for KI#3
    When provisioning the QoS parameters for the combined group, AF indicates the 5GC to select the strictest QoS policy among other sub-groups the group member belongs to
    For example, UE1 belongs to sub-group A and sub-group B, UE2 belongs to sub-group A, UE3 belongs to sub-group B. sub-group A and sub-group B form the combined group. With the new AF indication for the QoS policy of the combined group, then the 5GC sets the max QoS between sub-group A and sub-group B for the UE1 traffic destined to combined group, sets the QoS of sub-group A for UE2 traffic destined to combined group, sets the QoS for sub-group B for UE3 traffic destined to combined group
  Option 2: reuse the AF Session with QoS mechanism
    After construction of the combined group, e.g. DNN, S-NSSAI, group member, PDU type, etc. The AF invokes AFSessionwithQoS service to set individual QoS for the traffic destined to the combined group respectively for each UE member within the combined group.
    Refer to the example in option 1, in this case, the AF invoke AFSessionwithQoS to configure UE1 in order set max QoS for between sub-group A and sub-group B for UE traffic destined to the combined group, then again invokes AFSessionwithQoS to configure UE2 in order to set QoS of sub-group A for UE2 traffic destined to combined group, again for UE3, etc.
  Option 3: Follow the mechanism specified for KI#3, but clarify that this case allows the UE to send packets to different groups but with the same QoS treatment

## Slide 9: AoB： GMEC-AIMLSys API
LS-API enhancement- GMEC-AIMLSys
  GMEC: Nnef_AFRequestForQoS
  AIMLSys: Nnef_MultiMemberAFsessionWithQoS
CT3 Questions:
  Whether SA2 is planning to merge these two APIs into a single one?
  What is the common part and/or difference between the Nnef_AFRequestForQoS service API and the Nnef_MultiMemberAFsessionWithQoS service API?
Way Forward: consider to finish the GMEC API procedure and AIMLSys API procedure respectively in this meeting to make them stable first. Whether to merge or separate is FFS.
  Merge
  Separate

## Slide 10: AoB： GMEC-AIMLSys API
  GMEC: Nnef_AFRequestForQoS
  AIMLSys: Nnef_MultiMemberAFsessionWithQoS