## Slide 1: PIN vs 5G VN
Huawei

## Slide 2: 2. Enable PIN management by PEMC UE when PEMC UE has no direct connection with PEGC and AF is not deployed
The PMEC is a UE for which the PEMC client present is unknow by 5Gc
The PMEC has no PDU session dedicated to PIN since it has no PIN subscription
The PMEC is reachable or can be reached as follow:
  Mechanism outside the 3GPP scope left to implementation, e.g. DynDNS or a server NOT-3GPP AF over UP. There are nothing different for any mutual reachability issue between 2 UEs with 2 dynamic IP addresses from a “pool of addresses” or 2 MAC address
  PMEC/UE and PEGC are members of the same 5G VN group. This solution has the implication described in the discussion to answer to questions Q3 & Q4
The approach 1) is proposed as way out to be specified, i.e. let to implementation outside the SA2 scope.
If SA6 defines some P2P discovery mechanism transparent to 5GC, i.e. without any interaction with 5GC, is up to SA6.

## Slide 3: 3. Differences between PIN and 5G VN
Two PDU sessions connect to the same UPF.
  Based on the 5G VN group feature, the UPF support a local switch mechanism, the UPF should identify the packets belong to the same 5G VN group based on the same "5G VN internal" interface and the network instance, i.e. the same DNN and slice information (crf TS 23.501 clause 5.8.2.13.0 “If more than one 5G VN group has to be supported in the PLMN, the N4 rule attribute Network Instance is used in addition to the UPF internal interface and set to a value representing the 5G VN group.”).
  for the PIN case, the PIN group cannot be identified by the DNN and slice, since this means millions of couple of DNNs and slices or the 5G VN feature need to be extended adding the PIN ID
Two PDU sessions connect to the different UPFs, then there is the existing solution to establish the N19 tunnel between the two UPFs as defined in 5G VN group feature
  the N19 tunnel is established per 5G VN group granularity, so in the PIN case it will be per PIN granularity, which results in much more number of N19 tunnels established for PIN than for 5G VN group.
  the N19 tunnel is shared by the group members. But for the PIN, there is not so much PIN members than 5G VN group members to apply this N19 tunnel, then it can be foreseen the N19 tunnel for PIN will be created and released frequently than for 5G VN group.

## Slide 4: 3. Differences between PIN and 5G VN
Support of 5G VN group management
  5G VN group feature specifies how the group membership and related information is management via OAM (see TS 23.501 clause 5.25.2) or via NEF exposure capability (see TS 23.501 clause 5.29.2).
  The above mechanism are not consistent with the current assumption of PIN creation management by PMEC.
  The management procedures has impact on traffic for the management of USRP, PDU session, etc
PDU session management
  The PDU session for the 5G VN requires that (see TS 23.502 clause 5.29.3): a) A PDU Session provides access to one and only one 5G VN group. The PDU Sessions accessing to a certain 5G VN group should all anchor at the same network, i.e. the common home network of 5G VN group members b) A dedicated SMF is responsible for all the PDU Sessions for communication of a certain 5G VN group. SMF selection is described in TS 23.501 clause 6.3.2. c) A DNN and S-NSSAI is associated with a 5G VN group. d) a dedicated SMF shall be selected Therefore
    The requirement in bullet a) is compatible with PDU session for PIN only if the PDU session is dedicated for a single PIN and not shared.
    The requirement on a DNN and S-NSSAI associated to a 5G VN group clash with the requirement to be associated to a PIN , unless we identify the PIN as a special kind of 5G VN group or the 5G VN group feature specification is extended to support a group of PEGCs and PMEC as 5G VN in a way that has not been proposed and discussed during the study phase The existing 5G VN mechanism

## Slide 5: 3. Differences between PIN and 5G VN
Considering
  The 5G VN as currently defined and PIN as per TR outcome are not 100% compatible (as for previous slides), therefore or
    5G VN is modified to support some of PIN requirement or
    PIN is modified to include some of 5G VN mechanism or
    they are kept separate
    NOTE : GMEC is changing the 5G VN feature, so which 5G VN feature we intend to use , R17 or R18?
  Limited TUs for finish the work in due time
  We should avoid to perform the study in normative phase since we had claimed that the study is completed
  The normative phase shall always fix the holes and gaps that are identified following the direction identified by the study conclusions
The PIN and 5G VN features are considered as separate features
Whether a UE or group of UEs can support multiple features is up to implementation per usual business, unless is demonstrate that is technically NOT possible. In this later case we clearly state in the specification that they are not compatible, as per usual business

## Slide 6: 4. PIN ID usage, including two scenarios of “5G VN mechanism is used for a PIN” and “5G VN is not used for a PIN”
4.