## Slide 1: Solution proposal for PEMC communicating PEGC via 5GC local switch to enable PEMC managing PIN without AF
vivo

## Slide 2: Why PEMC needs to communicate with PEGC via 5GC local switch
PEMC APP can be installed on any UE as well as on devices
The UE with PEMC APP (called PEMC UE) may not have direct connection with any PEGC
The communication of a PIN is fully controlled by PEMC/AF, in case AF is not deployed, the PEMC UE shall be able to communicate with PEGC to enable the management of the PIN via 5GC local switch
When AF is deployed, the PEMC can register and communicate with the AF, but the PEMC may still not allow PEGCs to communicate with the AF for the sake of Permission control

## Slide 3: The principle for PEMC communicating with PEGC via 5GC local switch
Anchor the PDU Sessions of PEGCs and PEMC UE at same SMF
The anchoring method could be according to same <DNN, S-NSSAI> combination, which does not have impact on SMF selection
Different PIN may use same <DNN, S-NSSAI> combination, the SMF sets Network Instance in PDRs and FARs according to the PIN ID to isolate traffic data between different PINs, which has less impact on SMF functionality (SMF functionality anyway needs to be enhanced to support the new feature - PIN)
The PEMC can be provisioned with URSP rule with same <DNN, S-NSSAI> combination for anchoring the corresponding PDU Session at the same SMF, and SMF sets Packet Filter Set in PDRs for the PDU Sessions to isolate management data between different PINs
The Internal Group ID corresponding to the PIN ID that the PEMC UE is able to be managed can be configured in Internal-Group-ID-list in AM and SM subscription, which does not have 5GC impact (e.g., pre-configured, or using 5G VN procedure that the External GID=PIN ID and membership only includes PEMC UE(s))
The conclusion that “PEMC UE does not have PIN subscription” does not mean “5GC is not aware of PEMC UE”, any UE can act as PEMC but only PEGC-capable UE with PIN subscription can act as PEGC, the above principle does not require PEMC UE has PIN subscription

## Slide 4: An example that is aligned with the principle – PEMC UE is able to manage PIN#1 and PIN#2
In order to enable the management data handling by PEGC APP, the URSP for PEGC includes two URSP rules use same RSD that one with PIN ID as TD and the other with PEGC IP or PEGC APP ID as TD .
PDRs and FARs for PDU Session#1 (PEGC#1) |  | PDRs and FARs for PDU Session#3 (PEGC#3) |  | PDRs and FARs for PDU Session#0 (PEMC UE) | 
PDR#11 for management UL |  | PDR#31 for management UL |  | PDR#01 for management UL | 
Source interface | "access side" | Source interface | "access side" | Source interface | "access side"
CN tunnel info | N3 TEID for PDU Session#1 | CN tunnel info | N3 TEID for PDU Session#2 | CN tunnel info | N3 TEID for PDU Session#0
Packet Filter Set | src: PEGC IP#1 | Packet Filter Set | src: PEGC IP#3 | Packet Filter Set | dst: IP ranges for PIN#1
FAR#11 for management UL |  | FAR#31 for management UL |  | FAR#01 for management UL | 
Network instance | PIN#1 | Network instance | PIN#2 | Network instance | PIN#1
Destination interface | "5G VN internal" | Destination interface | "5G VN internal" | Destination interface | "5G VN internal"
PDR#12 for management and traffic DL |  | PDR#32 for management and traffic DL |  | PDR#02 for management DL | 
Source interface | "5G VN internal" | Source interface | "5G VN internal" | Source interface | "5G VN internal"
Network instance | PIN#1 | Network instance | PIN#2 | Network instance | PIN#1
Packet Filter Set | dst: PEGC IP#1 ¦¦ PINE IP#11 | Packet Filter Set | dst: PEGC IP#3¦¦ PINE IP#31 | Packet Filter Set | dst: PEMC IP#0
FAR#12 for management and traffic DL |  | FAR#32 for management and traffic DL |  | FAR#02 for management DL | 
Destination interface | "access side" | Destination interface | "access side" | Destination interface | "access side"
Outer header creation | N3 TEID for PDU Session#1 | Outer header creation | N3 TEID for PDU Session#3 | Outer header creation | N3 TEID for PDU Session#0
NOTE: The DL PDR and FARs are common for both management and traffic data |  |  |  |  | 
PDR#13 for traffic UL |  | PDR#33 for traffic UL |  | PDR#03 for management UL | 
Source interface | "access side" | Source interface | "access side" | Source interface | "access side"
CN tunnel info | N3 TEID for PDU Session#1 | CN tunnel info | N3 TEID for PDU Session#2 | CN tunnel info | N3 TEID for PDU Session#0
Packet Filter Set | src: PINE IP#11 dst: PINE IP#21 | Packet Filter Set | src: PINE IP#31 dst: PINE IP#41 | Packet Filter Set | dst: IP ranges for PIN#2
FAR#13 for traffic UL |  | FAR#33 for traffic UL |  | FAR#03 for management UL | 
Network instance | PIN#1 | Network instance | PIN#2 | Network instance | PIN#2
Destination interface | "5G VN internal" | Destination interface | "5G VN internal" | Destination interface | "5G VN internal"
 |  |  |  | PDR#04 for management DL | 
 |  |  |  | Source interface | "5G VN internal"
 |  |  |  | Network instance | PIN#2
 |  |  |  | Packet Filter Set | dst: PEMC IP#0
 |  |  |  | FAR#04 for management DL | 
 |  |  |  | Destination interface | "access side"
 |  |  |  | Outer header creation | N3 TEID for PDU Session#0