## Slide 1: Way Forward for CT1 LS - S2-2303916/ C1-227197 (Samsung)

## Slide 2: Background
CT1 sent an LS to SA2 in S2-2303916/ C1-227197. Below are the details:
“At CT1#139e, CT1 discussed certain requirements related to the UE behaviour in a non-allowed service area. CT1 would like to ask SA2 for guidance on an issue. The scenario is as follows:
The UE is registered to an AMF both via 3GPP and non-3GPP access. The UE is currently in a non-allowed area. The registration area (TAI list) for 3GPP access includes both TAs from the UE's non-allowed area and TAs from the allowed area. The UE is currently in a non-allowed area.
The UE has at least 1 PDU session activated via non-3GPP access which cannot be transferred to 3GPP access.
The UE is in IDLE mode both for 3GPP and non-3GPP access, when it receives a paging via 3GPP access indicating non-3GPP access and responds with a Service Request.CT1 understands that if the UE responds to the paging when it is in a TA belonging to the allowed area, then the UE needs to include the Allowed PDU session status IE (in 23.502 terminology: "List Of Allowed PDU Sessions") indicating which of the PDU sessions associated with non-3GPP access can be transferred to 3GPP access and may include the Uplink data status IE if it has uplink data pending.
Question 1: Does the UE need to include the Allowed PDU session status IE also if it responds to the paging when it is in a non-allowed area?
Question 2: Is the UE allowed to include the Uplink data status IE if it has uplink data pending if it responds to the paging when it is in a non-allowed area?”

## Slide 3
SA2 could not reach consensus in last 2 meetings on CT1 LS, SA2 agrees that UE shall include the Allowed PDU session status IE (List of Allowed PDU Sessions in SA2 terminology) when it responds to the paging with non-3GPP access type in a non-allowed area. But SA2 has not reached consensus on which PDU session(s) UE should include as part of Allowed PDU session status IE. Below questions will help determine which PDU sessions UE can indicate as part of Allowed PDU session status IE.
SoH question:
  Q1) The UE as part of Allowed PDU session status IE(CT1 terminology)/List Of Allowed PDU Sessions(SA2 terminology) will indicate which PDU session(s) for the scenario described in CT1 LS:
  The UE shall include empty PDU session list (decision on emergency PDU session/MCS/MPX will be made as part of Q2).
  The UE is allowed to include any PDU session based on its policy ignoring service area restrictions. Same behaviour is applied for List Of PDU Sessions To Be Activated in the specific scenario described in CT1 LS .
  Q2) If there is an active emergency PDU session/MCS/MPX PDU session over non-3GPP access, should UE be allowed to include them in Allowed PDU session status IE ?
  Yes
  No
  NOTE: Q2 is applicable only if option-1 is chosen as way forward in Q1.
Notes: SA2 agrees that UE needs to also include the Allowed PDU session status IE (List of Allowed PDU Sessions in SA2 terminology) when it responds to the paging in a non-allowed area. But SA2 has not reached consensus if MCS/MPX session should be included as part of Allowed PDU session status. Currently, the List of Allowed PDU Sessions is provided by the UE according to UE policies and whether the S-NSSAIs of these PDU Sessions are within the Allowed NSSAI for 3GPP access as specified in TS 23.502.
SoH question:
Should SA2 further specify that MCX/MPX session shall be include as part of Allowed PDU session?
Yes
No

## Slide 4: End