## Slide 1: PIN: Way Forward for Open Issues
SA2#157

## Slide 2: Mapping between PIN and PDU Session of a PEGC
Option 1: 5GC is aware of PIN member and PIN ID, PIN ID is used alone in URSP TD, External Group ID is an alias of PIN ID, which is associated with only one (DNN, S-NSSAI) combination (support 1:1 mapping) (S2-2306834)
Option 2: 5GC is aware of PIN member and PIN ID, External/Internal Group ID used in URSP TD, each Group ID maps to a sub-group of PEGCs for a PIN and is associated with only one (DNN , S-NSSAI) combination (support 1:* mapping) (S2-2306385, S2-2306384, S2-2306386, S2-2306387)
Option 3: 5GC is aware of PIN member and PIN ID, PIN ID is used together with IP/non-IP descriptors in URSP TD (support 1:* mapping) (S2-2306412)
Option 4 (DEFAULT): Based on option 1 with exception that 5GC is not aware of PIN member and PIN ID, PIN Traffic ID instead of PIN ID is used alone in URSP TD, External Group ID maps to a sub-group of PEGCs for a PIN, which is associated with only one (DNN, S-NSSAI) combination (support 1:* mapping) (S2-2306712, S2-2306713)
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
    Option 3: Yes: No:
    Option 4: If no preference for options 1-3, option 4 is selected

## Slide 3: Subscription data
Option 1: Enhance existing subscription data
  Option 1.1: Indication in one place: in Group Data for both SMF handling PDU Session for PIN and AM-PCF handling URSP for PIN (S2-2306718, S2-2306719)
  Option 1.2: Indication in multiple places (imply un-manipulable by AF): One indication in SM subscription data for SMF handling PDU Session for PIN, one indication in UE context policy control data for AM-PCF handling URSP for PIN (S2-2306652, S2-2307415)
  Option 1.3: Indication in multiple places (imply un-manipulable by AF): Tow indications in SM subscription data for SMF handling PDU Session, one for non-3GPP delay budget and the other for N3QAI, one indication in UE context policy control data for AM-PCF handling URSP for PIN (S2-2306715, S2-2307415)
Option 2: New subscription data: PIN subscription data (new) and new service operations used (S2-2306413, S2-2306414)
Q1: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
Q2: In case Option 1 is selected in Q1, which sub-option is preferred?
    Option 1.1: Yes: No:
    Option 1.2: Yes: No:
    Option 1.3: Yes: No:

## Slide 4: Categorization of PIN traffic
Option 1: Generally categorized by PINE traffic with boundary consideration (S2-2306716)
  PINE direct communication (within PEGC), PINE indirect communication (within PIN), PINE-DN communication (outside PIN)
Option 2: Generally categorized only by boundary without PIN element type consideration (S2-2306411)
  PIN direct communication (within PEGC), PIN indirect communication (within PIN), PIN-DN communication (outside PIN)
If discussed without consensus, SoH needed and the SoH question is as following
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:

## Slide 5: End