## Slide 1: PIN: Way Forward for Open Issues
SA2#157

## Slide 2: Mapping between PIN and PDU Session of a PEGC
Option 1: 5GC is aware of PIN member and PIN ID is not transparent to 5GC. PIN ID is used alone in URSP TD), a PIN may be associated with only one Group ID in 5GC, the Group ID maps to full-group of PEGCs for a PIN and is an alias of PIN ID. The Group ID is associated with only one (DNN, S-NSSAI) combination (Do not support 1:* mapping)
Option 2: 5GC is aware of PIN member and PIN ID is not transparent to 5GC. Group ID is used alone in URSP TD, a PIN can be associated with multiple Group IDs in 5GC, each Group ID maps to a sub-group of PEGCs for a PIN. The Group ID is associated with only one (DNN , S-NSSAI) combination (support 1:* mapping)
Option 3: 5GC is aware of PIN member and PIN ID is not transparent to 5GC. PIN ID is used together with IP/non-IP descriptors in URSP TD (support 1:* mapping)
Option 4 (DEFAULT): Based on option 1 with exception that PIN ID is transparent to 5GC. An ID (not necessary to be PIN ID) is used alone in URSP TD (support 1:* mapping) In this option, PIN is an application layer concept, which may be associated with multiple Group IDs over application layer, each Group ID maps to a sub-group of PEGCs for a PIN.
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
    Option 3: Yes: No:
    Option 4: If no preference for options 1-3, option 4 is selected

## Slide 3: Subscription data
Option 1: Enhancing subscription data for PIN
  Option 1.1: New indication in existing subscription data: in Group Data (in case Group Data supported and used) for both SMF handling PDU Session for PIN and AM-PCF handling URSP for PIN, as well as optionally (e.g., when Group Data not supported) in SM subscription data for SMF handling PDU Session for PIN and in UE context policy control data for AM-PCF handling URSP for PIN
    Alternative: Two Indications in SM subscription data for SMF handling non-3GPP delay budget and for N3QAI separately
  Option 1.2: New subscription data: New PIN subscription data and new service operations used
Option 2: No enhancement for subscription data, (DNN, S-NSSAI) specific for PIN as subscription indication for PIN
Q1: Which option is preferred?
    Option 1: YES: NO:
    Option 2: YES: NO:
Q2: In case Option 1 is selected in Q1, which sub-option is preferred?
    Option 1.1: YES: NO:
    Option 1.2: YES: NO:
Q3: In case Option 1.1 is selected in Q2, whether the alternative of option 1.1 is preferred?
    YES: NO:
    (Default of option 1.1 is one indication in SM subscription data)

## Slide 4: End