## Slide 1: PIN: Way Forward for Open Issues
SA2#157

## Slide 2: Mapping between PIN and PDU Session of a PEGC
Option 1: 5GC is aware of PIN member and PIN ID, PIN ID is used alone in URSP TD, External Group ID is an alias of PIN ID, which is associated with only one (DNN, S-NSSAI) combination (support 1:1 mapping) (S2-2306834)
Option 2: 5GC is aware of PIN member and PIN ID, External/Internal Group ID used in URSP TD, each Group ID maps to a sub-group of PEGCs for a PIN and is associated with only one (DNN , S-NSSAI) combination (support 1:* mapping) (S2-2306385, S2-2306384, S2-2306386, S2-2306387)
Option 3: 5GC is aware of PIN member and PIN ID, PIN ID is used together with IP/non-IP descriptors in URSP TD (support 1:* mapping) (S2-2306412)
Option 4 (DEFAULT): Based on option 1 with exception that 5GC is not aware of PIN member and PIN ID, PIN Traffic ID instead of PIN ID is used alone in URSP TD, External Group ID maps to a sub-group of PEGCs for a PIN, which is associated with only one (DNN, S-NSSAI) combination (support 1:* mapping) (S2-2306712, S2-2306713)
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
    Option 3: Yes: No:
    Option 4: If no preference for options 1-3, option 4 is selected

## Slide 3: Local switch for PINE-2-PINE communication via 5GS
Option 1: Considering PINE IP, and full-mesh is used (imply no AF influence) (S2-2306406)
Option 2: Considering PINE IP, and configured by SMF when receiving input, e.g., from AF (S2-2306715)
Option 3: Not considering PINE IP (imply NAPT is mandatory in PEGC for routing PINE traffic via 5GS), and full-mesh is used (imply no AF influence) (S2-2306836)
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
    Option 3: Yes: No:

## Slide 4: Subscription data
Option 1: Enhance existing subscription data
  Option 1.1: Indication in one place: in Group Data for both SMF handling PDU Session for PIN and AM-PCF handling URSP for PIN (S2-2306718, S2-2306719)
  Option 1.2: Indication in multiple places (imply un-manipulable by AF): One indication in SM subscription data for SMF handling both non-3GPP delay budget and N3QAI, one indication in UE context policy control data for AM-PCF handling URSP for PIN (S2-2306652, S2-2307415)
  Option 1.3: Indication in multiple places (imply un-manipulable by AF): Tow indications in SM subscription data, one for SMF handling non-3GPP delay budget and the other for handling N3QAI, one indication in UE context policy control data for AM-PCF handling URSP for PIN (S2-2306715, S2-2307415)
Option 2: New subscription data: PIN subscription data (new) and new service operations used (S2-2306413, S2-2306414)
Q1: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
Q2: In case Option 1 is selected in Q1, which sub-option is preferred?
    Option 1.1: Yes: No:
    Option 1.2: Yes: No:
    Option 1.3: Yes: No:

## Slide 5: PEGC indication to CN and CN indication to PEGC
Option 1: PEGC sends capability indication to PCF (S2-2306855, S2-2307342)
Option 2: PEGC sends capability indication to AMF, and AMF sends support indication(s) to UE (S2-2306724, S2-2306718)
Option 3: No indications
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
    Option 3: If no preference for options 1-2, option 3 is selected

## Slide 6: Categorization of PIN traffic
Option 1: Generally based on management traffic and data traffic (controlled by PEMC/AF) (S2-2306716)
Option 2: Generally based on destination (within PIN or outside PIN) and mix with management and data traffic (S2-2306411)
If discussed without consensus, SoH needed and the SoH question is as following
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:

## Slide 7: End