## Slide 1: Preparation before SA2#161 meeting
Dan Wang(China Mobile), Yixue Lei (Tencent)

## Slide 2: 1) PDU set QoS Parameters
How the SMF sends the PDU Set QoS Parameters to NG-RAN:
[Alternative 1]: At least one PDU Set QoS Parameter shall be sent to the NG-RAN to enable PDU Set based QoS handling. If the NG-RAN receives only PSER and not PSDB, the RAN uses PSER and PDB for PDU Set based QoS, and if the RAN receives only PSDB and not PSER, the RAN uses PSDB and PER for PDU Set QoS.
[Alternative 2:] Both PSDB and PSER PDU Set QoS Parameters shall be sent to the NG-RAN to enable PDU Set based QoS handling.
9.12.2 | S2-2402426 | CR | Approval | 23.501 CR5331 (Rel-18, 'F'): Clarification on support of PDU Set based QoS | Nokia, Nokia Shanghai Bell | Rel-18 | XRM
9.12.2 | S2-2401946 | CR | Approval | 23.501 CR5309 (Rel-18, 'F'): Clarifications of PDU Set QoS parameters | China Mobile | Rel-18 | XRM

## Slide 3: 2) PDU set QoS Parameters supersede the PDU QoS Parameters
Whether it needs to update the specification as following:
When the PSDB is available, the PSDB supersedes the PDB per direction for the given QoS Flow in the NG-RAN
If the PSER is available, the PSER supersedes the PER per direction in the NG-RAN
9.12.2 | S2-2402639 | CR | Approval | 23.501 CR5224R1 (Rel-18, 'F'): PSER and PSDB supersede the PER and PDB per direction | CATT | Rel-18 | XRM | Revision of S2-2400242 from S2#160AH-e | 

## Slide 4: 3) The activation of the DL/UL PDU set QoS handling
1) For DL, whether it is needed to define the activation for DL PDU set QoS handling in NG-RAN, and when NG-RAN receives the DL PDU set QoS Parameters but do not activate the handling, NG-RAN should notify 5GC.
2) For UL,whether it enables the UL PDU Set based QoS handling and activates UL PDU Set QoS Parameters (e.g. based on UAI) are as described in TS 38.300 [27]
9.12.2 | S2-2402032 | CR | Approval | 23.501 CR5314 (Rel-18, 'F'): Correction on how to apply the DL and UL PDU Set QoS | vivo | Rel-18 | XRM

## Slide 5: 4) Others?