## Slide 1: Input questions for DualSteer NWM discussion
ETRI

## Slide 2: Question for KI#1.3
Observations:
  The PDU Session establishment for DualSteer is applicable to specific DNNs/S-NSSAIs.
  There are two types of steering/switching modes, i.e. Active-Standby and the Smallest Delay.
  The DualSteer Device should include an indication in the PDU Session establishment whether the PDU session is applicable for potential DualSteer switching.
Question1: Can we assume that
  DualSteer Device’s PDU Session establishment to DNNs/S-NSSAIs not specified as DualSteer in DualSteer rule can be treated as a Local Breakout session.
Question2: Can we assume that
  DualSteer Device’s PDU Session establishment without indication of potential DualSteer switching can be treated as a Local Breakout session.
Question3: Can we assume that
  Multiple PDU sessions with potential DualSteer switching indication to different DNNs/S-NSSAIs specified as DualSteer in DualSteer rule can be switched altogether to the other access under Smallest Delay switching mode of simultaneous DualSteer Device.