## Slide 1: Topology 1 architecture options
Huawei
November 7, 2024
Security Level: Confidential

## Slide 2
T1 Direct & Indirect Architecture Options
Deployment consideration:
Local deployment (e.g. in enterprise campus), standalone use
Deployment consideration:
Centralized deployment (e.g. add-on OP public network), shared by enterprises
Benefit (for enterprise):
  AIoT data security
  Service efficiency
Benefit (for operator):
  Low capex of first stage investment, only deploy very few AIOTF.
  Easier AIOTF maintenance. Interfaces with AMF, are less than BS reader interfaces
Two architecture options aim for different deployment, propose to conclude both in TR
T1 Indirect via AMF
T1 Direct

## Slide 3
The protocol stacks show the interface between the AIOT RAN and the AMF/AIOTF.
In the Indirect via AMF case, N2 is used between the AIOT RAN and AMF and a new reference point (Ny) is used between the AMF and AIOTF.
In the direct case, a new reference point Nx is used between the AIOTF and the AIOT RAN.
T1 Protocol Stacks
T1 Indirect via AMF
T1 Direct
From AIoT RAN point of view, same protocol stack towards the CN and AIOT Reader Control is common

## Slide 4
Example Flow for T1
(common) Service Operation request from AF via NEF, and initial reader selection at 5GC
(Direct/Indirect specific) Service Operation request sent to BS Reader.
In T1 Indirect case:
AIoTF determines the AMF based on the stored mapping of AMF and BS Reader
AIoTF includes BS Reader ID in the request to AMF
AMF includes AIoTF ID in the request to BS Reader
(Direct/Indirect specific) Service Operation report to AIoTF
In T1 Indirect case:
BS Reader includes AIoTF ID the response to AMF
Response msg includes BS Reader ID
(common) Interaction with Device
(common) Service Operation report to AF via NEF
Indirect interface option, reuse AMF “non-UE N2 message transfer” operation between BS reader and AIOTF