## Slide 1: User consent and LCS privacy profile checks for LMF models to determine location
Thomas Belling
Nokia

## Slide 2: Status Quo in TS 23.273
For UE positioning calculation (using any method, also for AIML method), GMLC checks LCS privacy profile retrieved from UDM
In addition, Clause 5.18 states:
  Editor's note: Whether user consent for UE positioning calculation is needed apart from the existing GMLC check of the LCS privacy profile is FFS.
  For ML model training, performance monitoring and UE positioning calculation using LMF-based AI/ML Positioning, the LMF checks with UDM the user consent status before collecting UE related data, see clause 6.22.3 and clause 6.22.4.

## Slide 3: LS S2-2412940 to SA3 and SA3 answer in S3-251788
S2-2412940
SA2 is currently finalizing Rel-19 normative work on AIML_CN and would like to request input from SA3 in the context of user privacy for LMF-based AI/ML positioning (KI#1).
SA2 would like to ask SA3 whether, when the LCS privacy profile is checked, user consent check is required or not.
S3-251788
SA3 agrees that LCS privacy profile defined in TS 23.273 and user consent in Annex V of TS 33.501 are independent procedures. SA3 cannot reach consensus on other aspects. SA3 will continue the discussion and keep SA2 updated.

## Slide 4: LCS Profile definition in TS 23.273
3.1 Definitions
LCS Client: entity that interacts with GMLC for the purpose of obtaining location information for one or more UEs. The LCS Client may reside in the UE.
5.4 UE LCS privacy
5.4.1 General
An LCS client or AF may or may not be authorised to retrieve the UE location, e.g. for commercial use. UE LCS privacy is a feature which allows a UE and/or AF to control which LCS clients and AFs are and are not allowed access to UE location information. UE LCS privacy can be supported via subscription and via UE LCS privacy profile handling.

## Slide 5: Findings and Proposals
UE LCS Privacy Profile
UE LCS Privacy Profile is defined by SA2
UE LCS Privacy Profile is focusing on authorization of LCS clients (e.g. external AFs) to obtain location information related to a UE
UE location information is not exposed outside the 3GPP CN for ML model training and accuracy monitoring
Proposal 1: The UE LCS profile does not need to be checked for ML model training and accuracy monitoring (No related need to update the agreed procedures)

## Slide 6: Findings and Proposals
User consent
User consent is defined by SA3 (with purpose values “data collection” and “analytics” defined by SA2)
User consent purpose value “data collection” seems appropriate for data collection and performance monitoring, but not for location inference.
SA3 did not yet conclude whether (and for which use cases) User consent needs to be checked
Proposal 2: Wait for SA3 conclusions before agreeing any changes related to User Consent (No related need to update the agreed procedures and ENs before SA3 concludes)

## Slide 7
Annex: Proposals from at SA2#168

## Slide 8: Proposals for training at SA2#168
Status Quo: Only user consent check
LMF checks user consent and LCS privacy profile for all cases
LMF checks LCS privacy profile for all cases
LMF checks user consent only when it trains the model. LMF checks user consent and LCS privacy profile when NWDAF trains model

## Slide 9: Proposals for performance monitoring at SA2#168
Status Quo: Only user consent check
LMF checks user consent and LCS privacy profile for all cases
LMF checks LCS privacy profile for all cases
LMF checks user consent only when it trains the model. LMF checks user consent and LCS privacy profile when NWDAF trains model

## Slide 10: Proposals for Inference at SA2#168
Status Quo: LMF checks user consent. GMLC checks LCS privacy profile
GMLC checks LCS profile for all cases. (no user consent check)