## Slide 1: User Consent vs. LCS Privacy Profile for LMF-based AI/ML Positioning
NTT DOCOMO
SA WG2 Meeting #169
S2-2504831

## Slide 2: Background
SA2 Question (LS Out S2-2412940)
  SA2 would like to ask SA3 whether, when the LCS privacy profile is checked, user consent check is required or not.
SA3 Response (LS In S2-2504530):
  SA3 agrees that LCS privacy profile defined in TS 23.273 and user consent in Annex V of TS 33.501 are independent procedures. SA3 cannot reach consensus on other aspects
SA2 should decide based on its own understanding
DCM view based on separation between model training and model inference steps

## Slide 3: For ML Model Training (& Performance Monitoring)
Model training by NWDAF:
User Consent: According to TS 23.288, NWDAF checks user consent before UE data (including location) collection for model training (independent of LMF).
LCS Privacy Profile: According to TS 23.273, if UE location data is collected from LCS via GMLC, the LCS privacy profile is checked by the GMLC automatically. But in the case of LMF-based AI/ML Positioning, NWDAF collects data directly from LMF (not via GMLC); so, to keep the semantics of the LCS privacy profile consistent, the check should also be done—but now the enforcement point is the LMF.
Summary: (following the same logic as the existing specifications in TS 23.288 and TS 23.273) Both user consent and LCS privacy profile must be checked for ML model training by NWDAF
  NWDAF checks the User Consent
  LMF checks the LCS privacy profile

## Slide 4: For ML Model Training (& Performance Monitoring)
Model training by LMF:
User Consent: In this case, LMF a ML model training entity (similar to MTLF), following the same logic of ML model training specified in TS 23.288 that mandates user consent checking by NWDAF, the user consent must also be checked in this case as well by the LMF.
LCS Privacy Profile: According to the current definition in TS 23.273, this profile is checked when the UE location data is exposed to an LCS client. LMF is not an LCS client. So, LCS privacy profile checking is not needed.
  Alternative compromise: “According to regulatory requirements and/or operator’s policy, LMF may also check the LCS privacy profile.”
Summary: For ML model training by LMF, user consent checking is mandatory, and LCS privacy profile checking is based on regulatory requirements and/or operator’s policy.

## Slide 5: For ML Model Inference
Model inference by NWDAF: Not applicable in this case
Model inference by LMF:
User Consent: According to TS 23.288, user consent must be checked to provide analytics (i.e., to perform ML model inference) by the NWDAF. Following the same logic, LMF must also check user consent to perform ML model inference for UE positioning.
LCS Privacy Profile: According to TS 23.273, the profile is always checked by GMLC when there is a request for UE location by a LCS client. So, the LCS privacy profile will be checked automatically by the GMLC when there is a request for UE location that triggers ML model inference by LMF. So, there is no need to check the LCS privacy profile again in LMF.
Summary: For ML model inference, LMF must check user consent (and the LCS privacy profile will be checked by GMLC according to existing specification).

## Slide 6
Thank you.