## Slide 1: Discussion on call setup estimation
vivo Mobile Communication Co., Ltd.

## Slide 2: Formula for call setup time calculation
: the size of call setup IMS signalling (SIP or I1) or EPS signalling (e.g., for bearer resource reservation)
: the size of protocol overhead for carrying IMS or EPS signalling, e.g. UDP/IP/AS is around 32 (IPv4) -72 (IPv6) bytes
: the transmission rate, as SA1 (TR22.887) defined, [1-3] kbps
: the propagation delay considering GEO, 280ms is assumed (SA1)
: the transmission and propgation delay considering terristrial side, half of VoLTE (4-5s based on experience), 2.5s is assumed
: the number of UL IMS or EPS messages
: the number of DL IMS or EPS messages
NOTE: It needs to be multiplied by 3 to account for 2 additional signaling for uplink resource scheduling

## Slide 3: SIP message size for TN
SN | Message | Direction | Message size (proportional) | Counting in Call Setup Time
1 | INVITE | UL | 2,564 | YES
2 | 100 Trying | DL | 445 | YES
3 | 183 Progressing | DL | 1,705 | YES
4 | PRACK | UL | 1,054 | YES
5 | 200 OK | DL | 726 | YES
6 | UPDATE | UL | 1,929 | YES
7 | 200 OK | DL | 1,494 | YES
8 | 180 Ringing | DL | 983 | YES
9 | 200 OK | DL | 1,365 | 
10 | ACK | UL | 840 | 
If is 1000bps, typical header size (IPv6 used) is 52 bytes: