## Slide 1: Support of Ethernet BH PDU Sessions for MWAB
Qualcomm Incorporated
S2-2505350

## Slide 2: Issues of the existing system
In Rel-19, the Backhaul (BH) PDU Session type was limited to be IP (i.e. IPv4 or v6):
5.49.1.1 Principles and functional entities
Mobile gNB with Wireless Access Backhauling (MWAB) provides an NR access link to UEs in proximity and connects to the 5GC serving the UE through an IP connectivity provided by a Backhaul PDU session(s), as illustrated in figure 5.49.1.1-1. The MWAB consists of a gNB component (MWAB-gNB) and a UE component (MWAB-UE). The MWAB-gNB is based on the gNB functionality specified in TS 38.300 [27] and TS 38.401 [42]. The MWAB may be mounted on a moving vehicle and may serve UEs inside or outside the vehicle.
However, there is no technical reason for such limitation, as BH PDU session follows normal PDU session management schemes.
Actually, in deployment, it may be beneficial to use Ethernet PDU Session type in some cases. (next slide)

## Slide 3: The use case & requirement for Ethernet BH PDU Sessions
Some deployment may use Ethernet for the fixed RAN management.
  Therefore, it is desirable to provide the same connection type to the MWAB-gNB as well (via the BH PDU Session), so that the same RAN OAM system can be used without enhancements.
Additionally, when the BH PDU Session is of Ethernet type, the MWAB-UE may be able to independently use redundant PDU sessions for traffic duplication to improve reliability.
  As described in TS 23.501 clause 5.33.2.1, the UE can implement TSN (Time Sensitive Networking) FRER (Frame Replication and Elimination for Reliability) to decide on setting RSN and PDU Session Pair ID.

## Slide 4: Impacts to the system
All the procedures for supporting BH Ethernet PDU sessions are in place.
MWAB-UE can use existing configurations, and URSP rules, to decide how to establish the BH PDU Session with the appropriate PDU Session type.
Only stage 2 descriptions for MWAB in TS 23.501 clause 5.49.1 needs to be updated.

## Slide 5: Changes required for specification
TS 23.501 clause 5.49.1, to add "Ethernet" to the BH PDU Session description besides the "IP".
Further provide reference to clause 5.33.2.1 on the possibility of using redundant PDU sessions for the BH.
To clarify the MWAB-UE configuration with the explicit mentioning of "PDU Session Type"
The WID proposal is in S2-2505333;
The corresponding CR is in S2-2505349.