## Slide 1: Analysis on Call Setup Time for IMS Voice over GEO Satellite
2025. 05. 09

## Slide 2
3GPP TSG SA WG2#169
19-23 May 2025, Fukuoka, Japan
Source: | Samsung
Title: | Analysis on Call Setup Time for IMS Voice over GEO Satellite
Document for: | Discussion
Agenda Item: | 20.1.1
Work Item / Release | FS_5GSAT_Ph4_ARC / Rel-20
Abstract of the contribution: This document includes an analysis on Call Setup Time for IMS Voice over Satellite
S2-2505310

## Slide 3: Introduction
Requirements for IMS voice using GEO satellite access (TS 22.261 6.46.11)
  The 5G system with GEO satellite access shall be able to support IMS voice communication as defined in TS 22.228.
  The 5G system with GEO satellite access shall be able to provide mechanisms to optimize IMS voice (e.g., call setup, transmission overhead) and support a codec for the transfer of the voice considering the transmission data rate, latency and packet size.
KPI for a 5G system with satellite access (TS 22.261 Table 7.4.2-1)
For IMS voice call over NB-IoT (GEO), the following architecture assumptions and principles are applied (as in the current TR 23.700-19 clause 4):
  The EPC architecture with GEO satellite access for NB-IoT, as defined in TS 23.401 is used as baseline.
  There will be no mobility enhancements developed for the NB-IoT NTN in this study.
  Enhancements to NB-IoT (GEO), EPC, and IMS for supporting voice call via GEO shall be minimized.
  Only architecture options with data via SGi will be considered in the study. SCEF/T8 will not be considered.
Scenario | UE type | Transmission data rate |  | Others
 |  | UL | DL | 
IMS voice call using GEO [NOTE 7] | Handheld | [1-3] kbit/s | [1-3] kbit/s | Call set up time (note 8) ≤30 s (note 9)
Note 7: All the values defined for IMS voice call using GEO satellite access are generic for both regular and emergency calls. Note 8: call set up time refers to [56]; Note 9: 30s is the upper bound that is derived based on the user’s patience suggestions (30s) in [57]; |  |  |  | 
[56] ITU-T E.800: "Definitions of terms related to quality of service" [57] https://www.ncbi.nlm.nih.gov/pmc/articles/PMC8177735/ |  |  |  | 

## Slide 4: Assumptions
In addition to the architecture assumptions and principles are agreed as in TR 23.700-19 clause 4, this paper also assumes following aspects for analysis
  IMS client is implemented in the UE and IMS network is in the operator network.
  Use the existing IMS compliant SIP exchanges are assumed among the UE and IMS network
  Voice transmission is transferred over IP with potential header compression (e.g., ROHC)
IMS
35,786 km distance from the earth
285ms signal delays
SGi
MME
S/P-GW
CP transport option
UP transport option
UE

## Slide 5: Call Setup Time Estimation: Definition
Definition of Call Setup Time
  Call Setup time refers the time interval between the moment a call attempt is initiated and the moment the called party begins to receive a ringing signal or is otherwise alerted of the incoming call. It is a key metric for evaluating user experience and network performance in both circuit-switched (CS) and packet-switched (PS) voice services. For example of VoLTE, it starts when the caller initiates the call (e.g., sends a SIP INVITE message) and ends when the called party is alerted (e.g., receives SIP 180 Ringing) for VoLTE.
Estimating Call Setup Time
  Components affecting the call setup time can include UE processing delay, transmission time over the radio, RAN processing, Core network signaling delays (e.g., IMS servers) and the delay in alerting the called device.
  In order to estimate the call setup time, it takes the fully optimized Mobile Originated call procedure for VoLTE (as shown in the figure) that is a useful practice of the current deployment in one of Korean Operators. It is also assumed that the user originates a call when the UE1 is in idle state and the UE2 is in connected state.
MO Call Procedure for Call Setup Time Estimation
Call Setup Time
EPC
IMS
eNB
UE2
UE1
Service Request
1. Random Access Preamble
2. Random Access Response
3. RRC Connection Request
4. RRC Connection Setup
5. Service Request
6. Initial UE Message
7. Initial UE Context Setup Request
8. Service Response
8. SIP INVITE (SDP offer)
EPS bearer setup
Originating network
Terminating network
SIP 180 Ringing: UE can make a ringing tone. It can be considered as the end of Call Setup Time
SIP 183 Progressing: If the early media is used for voice announcement or ring back tone (e.g., voice coloring), the call setup time finishes after an initial part of voice media delivery has been completed.
The full SIP exchanges in IMS-based Mobile Originated Call is explained in Appendix slide
EPS bearer setup can be established, simultaneously
9. SIP 180
10. Bearer Modification Command
11. Bearer Modification Complete
Notes:   FYI. The agreement on the requirements for IMS voice call using GEO satellite is
    Experience data rate (UL/DL): [1-3] kbps
    Call Setup Time ≤30 s

## Slide 6: Call Setup Time Decomposition: Overview
Call Setup Time Decomposition
  To estimate total call setup time efficiently and compare proposed potential optimization techniques fairly, this paper proposes to decompose the call setup time based on the MO call procedure as shown in the figure.
  Since transparent payload is assumed, all messages between the UE1 and eNB are transferred over service link and feeder link.
  In summary, Call Setup Time can be decomposed as follows:
  Call Setup Time = Service Request Delay + SIP exchange Delay + EPS Bearer Setup Delay
IMS
UE1
UE2
EPC
D1 (R, S) = P + S / R
where P = Propagation (e.g. 285 ms)
R = Data rate (e.g., 1,2,3 kbps)
S = Size of Message
D2: S1 Delay
D3: EPC Delay
D4: Delay of IMS
D5: Delay between EPC and UE2
An architecture diagram for calculating the Call Setup Time
  D1: over-the-air delay between the UE1 to eNB over service link and feeder link. This delay is calculated as the propagation delay plus transmission delay that is message size divided by physical layer rate: D1 (R, S) = P + S / R
  D2: S1 delay between the eNB and EPC
  D3: EPC delay includes the delays within EPC such as MME to/from S/P-GW, S/P-GW to/from PCRF, etc
  D4: IMS delay includes the delays within IMS networks such as P-CSCF, S-CSCF in originating/terminating network.
  D5: Delay between EPC and UE2

## Slide 7: Call Setup Time Decomposition: Service Request Time
Service Request Time
  When the user press a call button, the UE1 starts the MO call procedure. It is assumed that UE1 is in idle state, therefore, the Service Request Time also considers the RRC setup time including random access.
  First round: When the UE1 is sending the first random access preamble over service link and reaches the satellite, the satellite forwards the signal to the eNB in the ground. The eNB performs Timing Adjustment and UL resource allocation and sends Random Access Response back to the UE.
  Second round: The UE1 sends RRC connection Request and eNB responds with RRC Connection Setup.
  Third round: The UE1 sends Service Request with RRC Connection Setup Complete and the eNB sends the Initial UE Message to MME and Initial UE Context setup procedures are performed between the eNB and MME. The messages that do not impact the overall call setup time are not shown in the flow diagram such as Initial UE Context Setup Response from eNB to MME.
  After completing service request, the UE1 is ready to send SIP INVITE message.
UE
eNB
MME
1. RA Preamble
6. Initial UE Message
TA, UL grant
2. RAR
3. RRC Connection Request
4. RRC Connection Setup
5. Service Request
8. Service Accept
7. Initial Context Setup Request
Service Request Delay
Calculation: Service Request Delay

## Slide 8: Call Setup Time Estimation: SIP Message Exchange Time
SIP Messages Exchange Time: From SIP INVITE to SIP 180/SIP 183
  Although there are various types of SIP exchanges can be performed among the UE1, the UE2 and the C-CSCF in IMS network, the example flow diagram assumes one round of SIP negotiation, that is an usual procedure for VoLTE in one of Korean Operators.
  The UE1 provides SDP offers to the UE2. In this flow diagram, it is assumed that the UE2 is in connected state, therefore no paging delay has been considered in this scenario. If we assume the UE2 is in idle state, an usual configuration of DRX cycle (e.g., 2.4 seconds) should be further added to the Call Setup Time.
  UE2 can accept the offer without further negotiation. It is assumed that one operator can manage mobile profile for IMS voice deployed in their network. It is also assumed that operators manages small number of profiles due to GSMA efforts to minimize the number of exchanges for SDP negotiation. One typical example of SDP negotiation can follows:
  1) UE1 offers low bit rate codec(s) as well as VoLTE voice codec added by P-CSCF in UE1 side when the transcoding is supported.
  2) If UE2 also supports one of low bit rate code(s) offered by the UE1, the UE2 can accept it. Otherwise, the UE2 can accept one provided by the P-CSCF in UE1 side.
  NOTE: Scenarios for SIP 183 Progress for early media. There also can be the cases when the UE1 receives SIP 183 Progress instead of receiving SIP 180 for the early media transmission e.g. voice announcement by IMS network or ring back tone by UE2. For those cases, the UE1 can receive the voice data either from the IMS network or UE2 almost right after receiving SIP 183 Progress. Therefore, from the call setup time perspective, it is not much different from the case that the UE1 receives SIP 180. One additional delay of transmitting the early media data over the satellite should be added for this case
**SIP Message Size [S2-2503486]
Calculation: SIP Exchange Delay
SIP INVITE
EPC
IMS
UE2
UE1
eNB
T2 = Tsip (1kbps, 2512B**) = 9.6 sec
Tsip (R,S) = D1 (R+S) + D2 + D3 + D4 + D5
SIP Exchange Delay = T2 + T4 + T5 + T6 + T7 + T8 + T9
SIP Exchange Delay
(for SIP INVITE)
Direction | SIP Message | size
UE1 --> UE2 | INVITE [CSeq: 1 INVITE] | 1703
UE1 <-- Network | 100 Trying [CSeq: 1 INVITE] | 333
UE1 <-- UE2 | 180 Ringing [CSeq: 1 INVITE] | 560
UE1 <-- UE2 | 200 OK [CSeq: 1 INVITE] | 1377
UE1 --> UE2 | ACK [CSeq: 1 ACK] | 569
SIP message size are based on the log file of SIP message exchanges captured in the device connecting one of Korean operators |  | 
SIP 180 Ringing
Trying

## Slide 9: Call Setup Time Estimation: SIP Message Exchange Time
CSCF
CSCF
EPS
UE1
EPS
UE2
4. SIP 180 Ringing
5. SIP 200 OK
6. SIP ACK
3. SIP PRACK
Call Setup Time
One round of SIP exchanges
IR.92 based basic call procedures
UE2 responds SIP INVITE by SIP 180 Ringing
P-CSCF triggers QoS authorization simultaneously
CSCF
CSCF
EPS
UE1
EPS
UE2
Two round SIP exchanges
For early media, UE2 responds INVITE by SIP 183 in step 2
UE1 responds SIP 183 by SIP PRACK in step 3
One round of SIP negotiation (i.e. INVITE/RINGING) is a basic procedure to be analyzed. This is also a basic procedure for VoLTE (GSMA IR.92)
Two round of SIP negotiation (i.e. INVITE/SIP183/PRACK/RINGING) can be used by operators for some use cases, e.g., early media
IR.92 does not recommend to use pre-condition confirmation procedure (i.e. SIP UPDATE/SIP UPDATE OK)
Bearer setup
2. SIP 183
Bearer setup
1. SIP INVITE
Bearer setup
2. SIP 183
Bearer setup
1. SIP INVITE
5. SIP 200 OK
6. SIP ACK
Call Setup Time

## Slide 10: Call Setup Time Estimation: EPS bearer setup time
EPS bearer setup time
  Triggering: When the SIP 180 or SIP 183 message arrives P-CSCF in UE1 side, The P-CSCF triggers the EPS bearer modification procedure by sending Policy authorization procedure to the PCRF. The PCRF authorizes the policy and QoS and initiates the EPS bearer modification procedure as in the step 10 and step 11 in the flow diagram. The message flows from the P-CSCF, PCRF, P-GW, S-GW and MME are now shown in this diagram, but is considered as EPC delay in Call Setup Time calculation.
  Bearer Modification Command is transferred from eNB to the UE1 over the satellite link in step 10. Therefore the message size is also important. Bearer Modification Command message includes the NAS message including mandatory fields such as NAS header, EBI, QoS with one TFT with 1 packet filter. The NAS message is delivered in RRC Connection Reconfiguration over PDCP/RLC AM/MAC. When calculating the call setup time, we assume this message size is 60 Bytes in total.
  Bearer Modification Complete is transferred from the UE1 to eNB over the satellite link in step 11. The message includes NAS message including NAS header, Message Type, PTI, EPS Bearer Identity. The NAS message is carried in RRC UL information transfer over PDCP/RLC AM/MAC. When calculating the call setup time, we assume this message size is 30 Bytes in total.
  Note that the EPS bearer setup can be established, simultaneously with transferring the SIP 180 or SIP 183. In calculating the call setup time, we added transferring bearer modification command with RRC Connection Reconfiguration and RRC Connection Reconfiguration Complete and Bearer Modification Complete.
EPS bearer setup time
P-CSCF triggers QoS authorization and PCRF sends a PCC decision provisioning (QoS policy) to S/P-GW
UE receives RRC Connection Reconfiguration with Bearer Modification Command
UE sends RRC Connection Reconfiguration Complete and Bearer Modification Complete over Direct NAS transfer
UE
eNB
MME
IMS
UE2
S/P-GW
PCRF
2. SIP 180
Provisioning PCC rule
IP-CAN Session Modification
Update Bearer Request
Bearer Modification Request
RRC Connection Reconfiguration
(Bearer Modification Command
RRC Connection Reconfiguration
Complete
Bearer Modification Response
Bearer Modification Complete
Update Bearer Response
IP-CAN Session Modification
Notification of Bearer Event
Notes: Bearer Modification Command (over-the-air)
  NAS Message (45-60B: one IPv4 TFT)
    Mandatory fields (EBI, QoS)
    One Traffic Flow Template (TFT) with 1 packet filter
  RRC Connection Reconfiguration (10~20B)
  PDCP(2) + RLC AM(2~4) + MAC(2)
Total at least 60B~ Bearer Modification Complete (over-the-air)
  NAS Message (8~10B)
    NAS Header: ~6B
    Message Type: 1B
    PTI: 1B
    EPS Bearer Identity: 1B
  RRC (carried in RRC UL Information Transfer): ~15B
  PDCP: 2B
  RLC (AM): ~4B
  MAC: 2B
  Total 30~35B

## Slide 11: Call Setup Time Estimation: Summary
We showed the decomposition of the Call Setup Time that includes
  Service Request Time
  SIP Exchanges (SIP INVITE and SIP 180)
  EPS Bearer Setup Time
Without any optimization, the Call Setup Time requires at least 24.7 seconds for 1kbps data rate from the moment when UE starts wake-up until the UE receives SIP 180.
 | Procedure | Delay in sec (no optimization) |  | 
 |  | 1kbps | 2kbps | 3kbps
1 | Service Request | 2.3 | 2.0 | 1.9
2 | SIP INVITE | 15.7 | 8.9 | 6.6
3 | Bearer Setup | 1.4 | 1.0 | 0.9
4 | SIP 180 | 5.4 | 3.2 | 2.4
Call Setup Time |  | 24.7 | 15.0 | 11.8
Call Setup Time Decomposition
Call Setup Time
EPC
IMS
eNB
UE1
1. Service Request
2. SIP INVITE
3. EPS bearer setup
4. SIP 180
Notes: Call Setup Time refers to the time interval between the moment a call attempt is initiated and the moment the called party begins to receive a ringing signal or is otherwise alerted of the incoming call. It is a key metric for evaluating user experience and network performance in both circuit-switched (CS) and packet-switched (PS) voice services. For example of VoLTE, it starts when the caller initiates the call (e.g., sends a SIP INVITE or CS SETUP message) and ends when the called party is alerted (e.g., receives SIP 180 Ringing) for VoLTE. Components affecting the call setup time can include UE (User Equipment) processing delay, transmission time over the radio, RAN (Radio Access Network) processing, Core network signaling delays (e.g., IMS servers) and the delay in alerting the called device.

## Slide 12: Observation #1. Call Setup Time Reduction on SIP exchanges (1/2)
Several large (i.e. more than thousands of bytes) SIP messages need to be exchanged over low rate (e.g. 1 ~ 3 kbps) during call setup procedure. One of potential enhancements to reduce the transmission delay of those large SIP messages is using SIGCOMP. SIGCOMP is a text-based compression mechanism to compress SIP signaling messages with pre-configured dictionary between the UE and the P-CSCF. Its compression ratio is known as 20% ~ 35%
When it is used, the UE and P-CSCF behavior for supporting SIGCOMP is specified in 3GPP TS 24.229 clause 8, while GSMA IR.92 prohibits using of SIGCOMP when the initial IMS registration is performed in E-UTRAN access.
As shown in the table 1, the Call Setup Time can be significantly reduced, e.g., 6.8~14.2 seconds
Table 2 shows the Call Setup Times depending on the compression ratio
 | Procedure | Delay in sec (compression ratio: 30%) |  | 
 |  | 1kbps | 2kbps | 3kbps
1 | Service Request | 2.3 | 2.0 | 1.9
2 | SIP INVITE | 5.0 | 2.9 | 2.2
3 | Bearer Setup | 1.4 | 1.0 | 0.9
4 | SIP 183 or SIP 180 | 1.9 | 1.2 | 1.0
 |  | 10.5 | 7.1 | 6.0
Compression Ratio | Call Setup Time (sec) |  | 
 | 1kbps | 2kbps | 3kbps
35% | 11.5 | 7.7 | 6.4
30% | 10.5 | 7.1 | 6.0
25% | 9.4 | 6.6 | 5.6
20% | 8.4 | 6.0 | 5.2
Notes: The UE must not use SIGCOMP when the initial IMS registration is performed in E-UTRAN access as specified in Release 10 3GPP TS 24.229 [15].
For the case of GEO satellite (i.e., P-Access-Network-Info header field includes a value of e.g., “3GPP-NBIOT-GEO-SAT” (newly defined value)

## Slide 13: Observation #2. Call Setup Time Reduction on SIP exchanges (2/2)
The protocol overhead of SIP message over NAS is slightly higher than the UP-based transmission.
IMS SIP signaling over NAS
IMS SIP signaling over UP
IMS SIP signaling messages are transmitted over SRB/NAS
MME relays IP messages between the UE and S/P-GW
IMS call setup time
IMS SIP MSG | 
UDP | 
IP | 
NAS | 7B
RRC | 2B
PDCP | 0B
RLC | 2B
MAC | 2B
IMS SIP signaling messages are transmitted over DRB/UP
A-GW
S/P-GW
UE1
UE2
DRB
GTP-U
A-GW
UE1
UE2
MME
S/P-GW
SRB
S1-AP
IMS SIP MSG | 
UDP | 
IP | 
PDCP | 2B
RLC | 2B
MAC | 2B
SIP over NAS | 1kbps | 2kbps | 3kbps
Call Setup | 10.6 | 7.2 | 6.1
Compression ratio: 30% No EDT/CP opt is used |  |  | 
SIP over UP | 1kbps | 2kbps | 3kbps
Call Setup | 10.5 | 7.1 | 6.0
Compression ratio: 30% No EDT/CP opt is used. |  |  | 
IMS call setup time
Notes: Ptim

## Slide 14: Observation #3. Call Setup Time Reduction on Service Request Time
A user can place a call when the UE is in idle state. CIoT EPS Optimization can reduce Service Request Time
Service Request Delay can be reduced for (1kbps for radio)
  CP CIoT EPS optimization: 0.7 sec
  UP CIoT EPS optimization: 1.0 sec
A. CP CIoT EPS Optimization
UE
eNB
MME
1. RA Preamble
4. Initial UE Message
TA, UL grant
2. RAR
3. RRCEarlyDataRequest
(Service Request)
8. RRCEarlyDataComplete
(Service Accept)
RRC Connection Request can include data (e.g. Service Request)
One round of propagation can be reduced
B. UP CIoT EPS Optimization
RRC Connection Suspend/Resume mechanism can be used
One round of propagation can be reduced
UE
eNB
MME
5. UE Context Resume Request
2. RAR
1. Random Access Preamble
S/P-GW
IMS
6. UE Context Resume Response
SIP INVITE
4. RRC Connection Setup
3. RRC Connection Resume
SIP INVITE
S/P-GW
5. Modify Bearer
6. Response
7. Service Accept
[36.300 7.3b-1 MO-EDT for CP Ciot EPS Opt]
 | Service Request Time |  |  | 
 |  | 1kbps | 2kbps | 3kbps
 | No optimization | 2.3 | 2.0 | 1.9
A | CP CIoT EPS Opt | 1.6 | 1.4 | 1.3
B | UP CIoT EPS Opt | 1.3 | 1.2 | 1.2
Notes: The UE must not use SIGCOMP when the initial IMS registration is performed in E-UTRAN access as specified in Release 10 3GPP TS 24.229 [15].

## Slide 15: Observation #4. Call Setup Time Reduction on EPS Bearer Setup
EPS bearer setup procedure from the perspective of reducing the Call Setup Time
  The analysis also shows additional 1.4 seconds (for 1.0 kbps physical rate) is added to the Call Setup Time.
  If EPS bearer setup is skipped, then we can reduce the call setup time
  However, we might compensate the following aspects:
    The main motivation of using GBR bearer for voice transmission is to guarantee QoS based on the required bandwidth.
    Due to long propagation delay and low transmission rate of satellite radio, it is not possible to meet the delay requirements. Packet Delay Budget for current QCI-1 and QCI-5 are 100 milliseconds.
    In addition, due to the limitation of NB-IoT UE, GBR is not supported.
    The number of DRBs is limited up to 2
    Call Admission Control over the satellite link is required in order not to establish voice call over the same satellite link
    Differentiation of voice transmission traffic from others may help a situation when the same service link and feeder link are used by large number of the UEs

## Slide 16: Summary
An analysis introduces a Call Setup Time and its decomposition and applies known optimization techniques to each step.
Fully optimized SIP procedure should be applied, e.g., one round SIP exchange.
If the following optimization techniques are applied, the call setup time can be significantly reduced.
  EPS CIoT CP or UP Optimization can reduce “Service Request Time” by 0.6~1.3 seconds.
  SIP compression can reduce “SIP message exchange Time” by 6.8~14.2 seconds.
  The protocol overhead of SIP message over NAS is slightly higher (e.g., 9 Bytes per message) than the UP-based transmission and it increases 0.1 second to the call setup time.
  EPS bearer setup time can be reduced. If skipped, it can also reduce 0.9~1.4. However, QoS aspects should be carefully considered.
 | Call Setup Time Decomposition | No optimization |  |  | Potential Optimization Techniques | Call Setup Time when the known techniques are applied |  | 
 |  | 1kbps | 2kbps | 3kbps |  | 1kbps | 2kbps | 3kbps
1 | Service Request | 2.3 | 2.0 | 1.9 | EPS CIoT CP (UP) Optimization | 1.6 (1.3) | 1.4 (1.2) | 1.3 (1.2)
2 | SIP INVITE | 15.7 | 8.9 | 6.6 | SIGCOMP (30% compression ratio) | 5.0 | 2.9 | 2.2
3 | Bearer Setup | 1.4 | 1.0 | 0.9 | - | 1.4 | 1.0 | 0.9
4 | SIP 180 | 5.4 | 3.2 | 2.4 | SIGCOMP (30% compression ratio) | 1.9 | 1.2 | 1.0
Call Setup Time |  | 24.7 | 15.0 | 11.8 |  | 9.8 (9.5) | 6.5(6.3) | 5.4 (5.3)
Notes:     SIP compression procedures at the UE (TS 24.229 clause 8)
      SIGCOMP negotiation during IMS registration procedure.
      RFC 3486, SIP dictionary in RFC 3485/RFC 4896