## Slide 1: SA2#86 SIMTC Drafting
SIMTC Rapporteur
(Puneet Jain, Intel)
S2-113643

## Slide 2: Device Trigger - Requirements
Need convergence on the Device Trigger requirements. (3289 as baseline for discussion)
  What parameters are transferred (transparently vs. un-transparent) between MTC Server and 3GPP PLMN over MTCsp?
    External ID (e.g. MTC device ID, App ID, TBD) & Trigger Validity seem to be common agreeable parameters. For other parameters there is no consensus.
    Revised to 3639.
  Shall MTC Server indicate Trigger delivery mechanism (CP/UP/SMS etc.) to 3GPP systems over MTCsp? Or, it’s selected by MTC-IWF? (3305, 3175)
    No consensus. 2 views
      MTC server should be able to dictate/control which trigger mechanism (e.g. CP, UP, SMS etc) is used by how 3GPP system.
      MTC server sends trigger request to MTC-IWF and MTC-IWF decide the appropriate trigger delivery mechanism.
    Trigger Delivery mechanisms needs to be agreed first?
  Batch triggering. Can MTC server trigger multiple UEs using single trigger? (3445)
    Already possible over MTCsms – Not standardized
    For MTCsp? – No consensus.
  Triggering synchronization needed? (3045)
    Not needed
  Overload control for Device Trigger needed?(3217)
    It may be needed but not clear if this is high priority item for Rel-11.
  Urgent/Immediate Device Trigger needed?(3350)
    Where is corresponding SA1 requirement?
Way Forward on device Trigger Requirement
  3289  3639. Work offline on agreeable parameters.
  Contributions proposing new requirements should have considerable support (especially from operators) before they can be added and solutions can be evaluated.
  Proponents were asked to work offline to gather more support

## Slide 3: Device Trigger – Interim Conclusions
Submission of Device Trigger from MTC Server to 3GPP system (3288, 3392 as baseline for discussion)
  Standardize Control Protocol between MTC Server and 3GPP system (MTCsp CP)?
  MTC-IWF to select the Device Delivery mechanism, authorization of trigger, mapping, protocol translation etc.?
  Structuring of Device trigger evaluation/conclusions in 3 buckets (i.e. submission of trigger, delivery of trigger, Internal handling of trigger) is agreeable.
  Need to capture what all aspects of MTCsp should be standardized.
Deliver of Device Trigger from 3GPP system to UE
  We already agreed on Pre Rel-11 SMS?
  NAS signalling based trigger solutions? (3393, 3269, 3040, 3082)
  Service layer triggering ? (3420)
  SMSoIP based triggering? (3207)
  Device trigger delivery solutions should be discussed in Plenary session to derive further conclusions.
Way forward for Device Trigger Interim conclusions
  3288 3641, Merge 3392 to 3641

## Slide 4: Identifier
Definition of External and internal identifier (3308 as baseline for discussion)
  External Identifier – FQDN, ICCID, MTC Application ID (?), …
  Internal Identifier – IMSI, New Internal Identifier needed?
  No new Internal identifier needed
  No consensus on what external identifier should be defined by 3GPP. Is 3GPP system transparent to external identifier format? ETSI LS response need to taken into account.
Mapping between external and internal identifier (3129)
  Not discussed
Can IMSI be used on external interface (i.e. MTCsp)? (3046, 3176)
  No consensus. Proponents need to work offline to get more support.
Do we need MTC group identity or can we batch individual identity together? (3382)
  MTC Group is not priority as per SA Guidance. Putting the requirement back will not be helpful. This relates to batch triggering and requirements needs to be worded with that scenario in mind.
Should IMSI & IMEI structure be expanded or they are sufficiently big ? (3522)
  No changes to IMSI/IMEI structure for Rel-11. Should be document as working assumption.
MTC devices using MSISDN-based identifiers shall communicate with MTC devices using non-MSISDN-based identifiers? (3408)
  This scenario is not needed for Rel-11
Way forward for Identifier
  3308 3642. Need to discuss ETSI LS response.
  Capture working principle (possibly in TR 23.888 clause 4.1A)

## Slide 5: Small Data Transmission
Focus for Small Data Transmission in Rel-11? (3339 as baseline for discussion)
  SMS Optimizations
  NAS based small data transfer.
  Other mechanisms ..