## Slide 1: Discussion on UE-to-UE Multi-hop Relay, use cases, and requirements
Mark Lipford
FirstNet, SyncTechno Inc., Erillisverkot , Netherlands Police, Ministere De L’Interieur, AT&T, Norwegian Communications Authority, ASTRID, Telus, Apple, Qualcomm

## Slide 2: Background – What is multi-hop Relay
Multi-hop relay is a UE connected via more than a single UE relay to either the network, or to another UE.
Here are two examples of Multi-hop.
  UE-to-UE multi-up relay (off network)
  UE-to-Network multi-hop relay (on network)
Multi-Hop UE-to-UE Relay
Relay UE
Relay UE
Remote UE
Remote UE
Multi-Hop UE-to-Network Relay
Relay UE
Relay UE
Remote UE

## Slide 3
Why do we need UE-to-UE multi-hop Relay? Here are three Use Cases Supporting UE-to-UE Multi-hop Relay

## Slide 4: Use Case 1 – Remote wilderness
In this scenario there is a group of fire jumpers that parachute into a remote mountainous wilderness to fight a forest fire.
The fire jumpers spread out across the fire line that spreads over several mountains.
Due to the location, there is no network coverage but the need to communicate is high so they can keep each other informed to the conditions.
The ability to support both private 1-to-1 calling, and group calling is critical to the fire jumpers' safety and for them to do their job.

## Slide 5: Use Case 2 – In-building no coverage
Consider a situation where a fireman is in the back corner of a basement and has not connection to the network and needs to communicate with the on-scene commander at the street.
There could be a second fireman as the base of the steps and a third fireman at the top of the steps by the exterior door.
Multi-hop relay could allow the fireman in the back of the basement to have a mission critical communications with the onsite commander using multi-hop relay, even without network access.
Basement Area 1
Basement Area 2

## Slide 6: Use Case 3 – Search and Rescue
This is a use case that blends UE-to-Network and UE to UE multi-hop together.
In locations where only minimal coverage is available, public safety operators can consider deploying Rapid Deploy Temporary Network (RDTN) consisting of a local private core, edge compute and RAN features such as advanced antenna beamforming techniques supported in NR to increase signal strength and Integrated access and backhaul (IAB).
In this use case a multi-hop wireless relaying feature with RDTN enables an unmanned aerial vehicles (UAV) to provide extended coverage performing both search and rescue video analytics and MC communication hosted on the local edge compute.
RDTN
Drone as UE
Satellite
UE-to-Network
Relay
UE-to-UE
Multi-Hop
Relay

## Slide 7: Current Status of Requirements

## Slide 8: Background – Current Status of Requirements (TS22.261)
In TS22.261 UE-to-Network Relay is defined and includes support for multi-hop.
  6.9.1 Description
    The UE (remote UE) can connect to the network directly (direct network connection), connect using another UE as a relay UE (indirect network connection), or connect using both direct and indirect connections. Relay UEs can be used in many different scenarios and verticals (inHome, SmartFarming, SmartFactories, Public Safety and others). In these cases, the use of relays UEs can be used to improve the energy efficiency and coverage of the system.
    Remote UEs can be anything from simple wearables, such as sensors embedded in clothing, to a more sophisticated wearable UE monitoring biometrics. They can also be non-wearable UEs that communicate in a Personal Area Network such as a set of home appliances (e.g. smart thermostat and entry key), or the electronic UEs in an office setting (e.g. smart printers), or a smart flower pot that can be remotely activated to water the plant.
    When a remote UE is attempting to establish an indirect network connection, there might be several relay UEs that are available in proximity and supporting selection procedures of an appropriate relay UE among the available relay UEs is needed.
    Indirect network connection covers the use of relay UEs for connecting a remote UE to the 3GPP network. There can be one or more relay UE(s) (more than one hop) between the network and the remote UE.
There are currently no requirements in TS22.261 that include UE-to-UE multi-hop relay

## Slide 9: Background – Current Status of Requirements (TS22.280)
In TS22.280 There are UE-to-UE requirements for a single relay
  7.15 Off-network UE-to-UE Relay
    7.15.1 Private Communications
      [R-7.15.1-001] The Off-Network MCX Service shall provide a means by which the MCX User of a (source) UE can make a Private Communication to the MCX User of a (target) UE via a ProSe UE-to-UE Relay.
      [R-7.15.1-002] The Off-Network MCX Service shall provide a mechanism for a source MCX User to query whether a particular target MCX User is within ProSe direct communication range.
      [R-7.15.1-003] An MCX UE shall be able to:
      - discover whether the UE of the target MCX User is itself within direct communication range of the source UE; and if not;
      - instead discover whether the UE of the target MCX User is within communication range of a ProSe UE-to-UE Relay that is within direct communication range of the source UE.
    7.15.2 Group Communications
      [R-7.15.2-001] An MCX Service Administrator or authorized user shall be able to configure a ProSe-enabled UE, authorized to act as a ProSe UE-to-UE Relay, to relay any received MCX Service transmissions for one (or more) specified MCX Service Groups.
      [R-7.15.2-002] An MCX UE receiving both the original MCX Service Group transmission and a relayed transmission shall be able to associate the two transmissions, correctly order a mixture of packets (received directly and indirectly) and identify duplicate packets.
  7.16 Off-network Ad hoc Group Communication
    [R-7.16-001] The off-network MCX Service shall provide a mechanism to combine an ad hoc multiplicity of MCX Users within communication range into a group communication.

## Slide 10: Proposal

## Slide 11: Proposed Change 1
Considering these use cases, and the lack of requirements to support these use cases there is a need to update the requirements in TS22.280 for Off-network UE-to-UE to include multi-hop capability.
Proposed changes to TS22.280 are:
7.15.1 Private Communications
[R-7.15.1-001] The Off-Network MCX Service shall provide a means by which the MCX User of a (source) UE can make a Private Communication to the MCX User of a (target) UE via one or more a ProSe UE-to-UE Relays.
7.15.2 Group Communications
[R-7.15.2-001] An MCX Service Administrator or authorized user shall be able to configure one or more a ProSe-enabled UEs, authorized to act as a ProSe UE-to-UE Relay, to relay any received MCX Service transmissions for one (or more) specified MCX Service Groups via one or more ProSe UE-to-UE Relay.

## Slide 12: Proposed Change 2
To stay aligned with current working processes, update TS22.261 to include the changes in Proposal 1 in TS22.280
Changes to TS22.261
6.9.1 Description
The UE (remote UE) can connect to the network directly (direct network connection), connect using another UE as a relay UE (indirect network connection), or connect using both direct and indirect connections. Relay UEs can be used in many different scenarios and verticals (inHome, SmartFarming, SmartFactories, Public Safety and others). In these cases, the use of relays UEs can be used to improve the energy efficiency and coverage of the system.
Remote UEs can be anything from simple wearables, such as sensors embedded in clothing, to a more sophisticated wearable UE monitoring biometrics. They can also be non-wearable UEs that communicate in a Personal Area Network such as a set of home appliances (e.g. smart thermostat and entry key), or the electronic UEs in an office setting (e.g. smart printers), or a smart flower pot that can be remotely activated to water the plant.
When a remote UE is attempting to establish an indirect network connection, there might be several relay UEs that are available in proximity and supporting selection procedures of an appropriate relay UE among the available relay UEs is needed.
Indirect network connection covers the use of relay UEs for connecting a remote UE to the 3GPP network. There can be one or more relay UE(s) (more than one hop) between the network and the remote UE.
A relay UE can also be used to connect two remote UEs using direct connection. There can be one or more relay UE(s) (more than one hop) between the two remote UEs.
6.9.2 Requirements on indirect network connection
The following set of requirements complement the requirements listed in 3GPP TS 22.278 [5], clauses 7B and 7C and in 3GPP TS22.280 [x], clauses 7.15.1 and 7.15.2.
6.9.3 Requirements on direct device communications
The following set of requirements complement the requirements listed in 3GPP TS22.278 [5], clause 7A.
The 5G system shall support the relaying of traffic between two remote UEs using direct device connection via one or more relay UE(s) (one or more hops, assuming single path), while in coverage, out-of-coverage, or partial coverage.

## Slide 13: Thank You