## Slide 1
3GPP TSG-SA WG1 Meeting #106, Jeju, Korea, 27-31 May 2024
Discussion on Collaboration of Dual 3GPP Access (FS_ColDualAccess)
Source： CATT
Agenda item: 4
Document for: Discussion
S1 – 241157

## Slide 2: Motivation
IoT devices are normally deployed with a combination of autonomous movement and remote control. For some critical tasks, e.g. path planning, control command transmission, there are stringent requirement on network availability and reliability for the connectivity between remote IoT platform and IoT devices, especially in critical IoT applications (e.g. factory robot, critical medical instrument).
“Suning” Unmanned Automated Warehouse
Dual access or even triple access based on multiple RATs is widely used to cater for different use cases e.g. ensure the reliability, extend the network bandwidth.
High Throughput
Reliability or Latency

## Slide 3: Gap Analysis
Rel-15 - SMARTER, multiple access technologies
Rel-15 - EDCE5, E-UTRA-NR Dual Connectivity
Rel-19 - DualSteer， traffic steering and switching over dual 3GPP access
Existing Requirements/Functions
Gap and Benefit to be suppported
Current:
The transmission is coordinated by RAN or CN.
Gap:
Neglect the use cases related to the application-initiated collaboration of dual 3GPP access
Benefit:
- More practical policy for network switching or selection considering the need of IoT application
- Help to improve network efficiency (e.g. energy consumption, congestion status)

## Slide 4: UC#1 AGV Control via dual 3GPP Access
Service Flow
1. In regular patrol task, AGV will connect to both NR#1 and NR#2, and send photos and sensor data via NR#1 to AGV control application.
2. The platform also initiates 5G positioning service via NR#1 for AGV navigation and path planning.
3. The platform is authorized to get the radio capability and performance of NR#1 and NR#2 when AGV moves.
4. Before AGV moves to the shadow corner of NR#1, the platform requests the network to handoff AGV to NR#2 to avoid the connection lost.

## Slide 5: Other Use Cases
The IoT platform requests the network to deliver MT message with critical billing information via both 3GPP access duplicated for high reliability.
MT Message incl. for Smart Meter
Sharing Positioning Data
The location info. of the same device is allowed to be reused by different applications in the specific policy defined by 3rd party e.g. when QoS fulfills, when one network is unavailable.

## Slide 6
Study the use cases and potential service requirements for 3rd party involved collaboration of dual 3GPP access of one device, regarding the following aspects:
Network capability exposure about the information related to dual 3GPP access (e.g. reachability, radio characteristics, etc)
Policy control for different services(e.g. positioning, messaging service)
Gap analysis between potential new service requirements and existing 3GPP requirements and functionalities
Proposed Objectives

## Slide 7
Thank You!