## Slide 1: Views on 6G Use Cases
Sharp
S1-241184

## Slide 2: Sharp’s topics of Interest
ISAC
AI/ML
Green Communications
Security
Overview

## Slide 3: Integrated Sensing and Communications
Sharp’s interested use cases
One of the issues of V2X is that among a group of cars in proximity, one or more of the cars may not be capable of V2X, then efforts to enhance safety by way of “group situational awareness” may be futile... Thus “sensing” functionality used by a 6G BS that is serving the group of cars (and in fact, there may be multiple 6G BS serving one or more of the cars in the group) may be very useful to an ITS (intelligent transportation system) to enhance safety without requiring every car on the road to be V2X capable.
Enhance the performance of the network by providing optimized input for network operations. For example, the sensing function would be able to detect objects that (temporarily) obstruct the direct propagation path between a transmission node and a device enabling enhanced mobility decisions, beam management configurations, Secondary Cell configuration.
Potential enhancement direction in one sentence
  Break down the barriers between “Uu” (uplink/downlink) and “PC5” (sidelink) such that
    ISAC “sensing data” can be shared over sidelink among V2X UEs and non-ISAC capable V2X UE; and
    Data to be shared via sidelink can also be shared via downlink by broadcast from a BS to non-sidelink-capable UEs.
ISAC

## Slide 4: Artificial Intelligence and Machine Learning
Sharp’s interested use cases
Potential examples include:
  Automation of Network wide resource scheduling, e.g., coordinated scheduling among gNBs
  AI enabled mobility.
  AI enabled Sensing.
  AI enabled MAC (e.g., AI enhanced scheduling considering at least: time, frequency, and spatial domain)
  AI enabled device level and NW component level power control.
Potential enhancement direction in one sentence
Native support for the acquisition of AI related data and the use of system computation resource for model operation and management that can result in optimized system configuration(s) and enhanced user experience while minimizing the use of network resource (e.g., Energy, RF, Time)
AI/ML

## Slide 5: Green Communications
Sharp’s interested use cases
  Our commitment to avoiding climate catastrophe includes the promotion of Green Communications, such as reduced network/device energy usage by employing a holistic approach to the design of next generations networks (i.e., a native E2E energy savings design).
  Energy consumption estimation frameworks for more precise and timely measurement of energy consumption
Potential enhancement direction in one sentence
  Energy saving via a reduction in communication channel usage (e.g. overhead due to the transmission of periodic control information) for both the network and UE perspective should be pursued.
Green Comm.

## Slide 6: Security
Sharp’s interested use cases
  AI/ML and ISAC will test societies concept of an individuals (and corporate) public and private information, in both a static configuration and a dynamic one.
Potential enhancement direction in one sentence
  Native security and privacy protection by design.
Security.

## Slide 7
Thank you