## Slide 1: Discussion on on enhanced support for Multi-USIM (MUSIM) UE
CableLabs
3GPP SA WG1 Meeting #106
Jeju Island, Korea, 27-31 May 2024
S1-241188, 3GPP TSG-SA WG1 Meeting #106, 27-31 May 2024

## Slide 2: Motivations
Lack of coordination between networks operated by the same operator and MUSIM device, supporting multi-SIM UE for efficient UE and network resource management, efficient power consumption.
Achieving Near-zero interruption on active connection for Multi-SIM UEs with single Tx/Rx capability
Enhancing UE and network energy savings by enabling co-ordination between networks and multi-SIM UE needs to be studied.
Limitation with dual steer requirements
  There’s no support for traffic splitting across networks.
Lack of support for various deployment scenarios and features of multi-SIM UEs.
  Simultaneous access of PLMN+PLMN over 4G/5G
  Simultaneous access of PLMN+SNPN over 4G/5G.
S1-241188, 3GPP TSG-SA WG1 Meeting #106, 27-31 May 2024

## Slide 3: Use Cases
Efficient UE Resource Utilization
  Signaling, procedures like RA/TA updates can be unified between networks serving a MUSIM UE and radio resources can be utilized efficiently.
  Paging Optimizations like sending paging frames for idle SIM through active connection of SIM2.
UE network energy saving
  When a network wants to offload traffic for energy efficiency, network along with MUSIM capable UEs can perform traffic switching more efficiently.
Traffic steering and splitting
  When MUSIM device connects to two networks simultaneously and services provisioned on these networks can be switched between networks based on the network and UE conditions (like load, energy savings) by interacting between UE and Network.
  Application traffic can be split between two simultaneous connections to provide more bandwidth if needed.
S1-241188, 3GPP TSG-SA WG1 Meeting #106, 27-31 May 2024

## Slide 4: Use case: Paging & RA/TA update Optimization
A Multi-SIM UE can maintain “active” and “idle” connections without having to interrupt ‘active’ connection for periodic messages with the following optimizations.
  Paging Optimization
  TA/RA update Optimization
Paging optimizations studied for MUSIM UEs can be further optimized. When downstream data is to be sent over idle SIM (PLMN2), PLMN2 core can inform PLMN1 core which in turn notifies MUSIM UE about the buffered downstream data.
Once MUSIM UE receives the DL data notification, UE will start service request procedure to establish RRC Connection with gNB in PLMN2 and receive the buffered downstream data.
UE is allowed to skip/avoid TA/RA updates within PLMN2 and can update location based on PLMN1 updates.
S1-241188, 3GPP TSG-SA WG1 Meeting #106, 27-31 May 2024

## Slide 5: Use Case: Network/UE Energy Efficiency
A MUSIM device is connected to two networks PLMN1 & PLMN2. PLMN2 operator has a capacity booster cell and MUSIM device is simultaneously connects to both the operators.
When capacity booster cell is active, MUSIM device use PLMN2 for high throughput services while other best of effort services offered by PLMN1.
S1-241188, 3GPP TSG-SA WG1 Meeting #106, 27-31 May 2024
When capacity booster cell (PLMN2) goes in energy saving state, it may not handover the traffic right cell because current traffic handover mechanism tend to pick a random neighboring cell (using Xn interface).
If networks knows that UE is a MUSIM device, network can work with other SIM UE and find the optimal target node for handing over the data session.
Solutions may inform MUSIM UE to initiate the traffic handover procedure, network functions across PLMNs may not interact directly.

## Slide 6: Use Case: Differentiated Services PLMN + NPN or PLMN+PLMN
Operator has two PLMNs or PLMN and NPN with overlapping cells, a MUSIM device can connect to both the networks simultaneously.
Subscribers opted for platinum tier like UE2 can can get better quality of service by splitting the application session on both the RATs and achieve better user experience, while other users like UE1 can only use single session for one service.
Traffic can be selectively switched from PLMN2 to PLMN1 if the network load changes or capabilities of network changes by switching specific services can be moved between networks.
Dynamic change of capabilities of network and UE can be handled optimally if the networks know that two UEs belong to the same MUSIM device.
S1-241188, 3GPP TSG-SA WG1 Meeting #106, 27-31 May 2024

## Slide 7: Proposal
The objective of the proposed work item is:
Study and identify use cases for supporting different multi-USIM scenarios
  Identify potential requirements to overcome challenges of lack of coordination between networks and MUSIM UE to support multi-USIM scenarios;
  For identified use cases, perform a gap analysis between newly identified requirements and existing 3GPP requirements
To specify service requirements for supporting simultaneous Multi-SIM (MUSIM) UE.
The service requirements will cover the following aspects:
Co-ordination across 3GPP access networks and the associated MUSIM UE
  Network awareness of two USIMs (UEs) belonging to one simultaneous MUSIM device
  Provide unified coverage, service capabilities as well as resource optimizations
UE/network energy saving via paging optimizations with networks and MUSIM UE interaction.
S1-241188, 3GPP TSG-SA WG1 Meeting #106, 27-31 May 2024