## Slide 1
SA (1 or more SFNs)
target area
Only SFN coverage:
1 - No announcement received; broadcast of MBSP message here, but no reception outside target area
Only CB coverage:
1 - no announcement, because it would suppress the PWS message;
2 - only PWS message displayed.
CB and SFN coverage:
1 – announcement via CB;
2 – PWS message ignored;
3 – MBSP message displayed
CB
Message broadcast:
1 – announcement via CB with SN+MI of PWS message in overlapping area
2 – PWS message via CB in target area
3 – MBSP message via MBMS in SA
Displayed:
1 - SA outside overlapping area: nothing, because no announcement and no PWS message was sent here
2 - Target Area outside overlapping area: PWS message; is not suppressed because no announcement was sent here
3 – Overlapping area: MBSP message; PWS message is suppressed

## Slide 2: PWS+MBSP
Message 1: An announcement is broadcasted via CB in the overlapping area
The announcement contains the Message Identifier (MI) and Serial Number (SN) of the PWS Warning notification that will follow soon.
The UE stores the MI+SN in its CB message store, which will result in even the very first PWS Warning Notification to be ignored as a duplicate message.
Message 2: The MBSP message is broadcasted via MBMS in the entire Service Area (SA)
Only the UEs in the overlapping area which have received the announcement will receive and display the message.
Message 3: The PWS Warning Notification message is broadcasted via CB in the target area
UEs in the overlapping area will ignore the PWS Warning Notification
The order of message 2 and 3 is not relevant.
If a UE in the overlapping area receives the announcement, but is unable to receive the MBSP message correctly, then it will have to rely on a repetition, because it will ignore the PWS Warning Notification.
If a UE in the overlapping area cannot receive the announcement correctly, it will not be able to receive the MBSP message, but it should receive and display the PWS Warning notification, since this message will not be ignored.

## Slide 3: MBSP only
Message 1: An announcement is sent to the UEs in the overlapping area, or to all UEs in the entire Service Area (SA)
Note that the overlapping area may not be a close approximation of the target area
Note that the SA may not be a close approximation of the target area
Message 2: The MBSP message is broadcasted via MBMS in the entire SA
The UEs which have received the announcement will receive and display the message.
If a UE cannot receive the MBSP message correctly it will have to rely on a repetition.