## Slide 1: “elastic core” further enhancement of virtualization
Agenda Item: 5
Source: NTT DOCOMO
Contact: Atsushi Minokuchi
<minokuchi (at) nttdocomo (dot) co (dot) jp>
3GPP TSG-SA WG1 Meeting #68 S1-144359
San Francisco, USA, 17-21 November 2014

## Slide 2: introduction/proposal
This document addresses #1 among two streams below for future work for core network:
  EPC evolution based on virtualization
  Disruptive approach.
This document explains an concept to further enhance the benefit of virtualization.
This document is for information.
If we get sufficient support, we propose a Rel-14 study item around this topic at the next SA1 meeting.

## Slide 3: overview of “elastic core”
Problem: resource rebalancing takes time.
  That prevents flexible, efficient resource usage that virtualization promises from being realized.
Cause of the problem: “state”
  The state information needs to be transferred.
Solution: to separate processing and state.
= “elastic core” concept

## Slide 4: challenge of virtualization
End-user
Peer node
state
APL
state
APL
ACT
SBY
Node A(node ID A)
sync
Capacity
Resource Pool
②Apply configuration changes to
distribute sessions
Network
①Instantiate a new virtual node in a
couple of minutes
③Overall load is shared among two nodes
⑤Apply configuration changes to remove
Node B
④Moving sessions from Node B to Node A
Via A
Via B
Scale OUT
Scale IN
Time to complete takes longer
②
③
⑤
④
state
APL
state
APL
ACT
SBY
Node B(node ID B)
sync
Capacity
①

## Slide 5: “elastic core”
NW
State DB
State DB
State DB
#1
#3
#5
#2
#4
#6
End-user
Peer node
APL
APL
ACT
Node A(node ID A)
DC1(Resource Pool)
SDN
ACT
①Add IMSI hash
②Routing and load Balancing by IMSI hash※
※IMSISDN ,etc can be used in addition to IMSI
⑦IMSI hash routing is changed by
NW Manager
⑤IMSI hash routing is changed by
NW Manager
DC2(Resource Pool)
NW manager
Add “IMSI hash”
Header
IMSI
hash
data
Routing by
“IMSI Hash”
IMSI Group #1,#3,#5
IMSI Group #2,#4,#6
APL
ACT
③Store State information in Distributed DB
Scale OUT
Scale IN
④Instantiate a new virtual node in a
couple of minutes
IMSI Group #1,#3,#5
IMSI Group #2,#4,#6
IMSI Group #5,#6
⑥Load Balancing is completed in an
instant.
⑧VM is deleted.
#5
#6
Quick ,Wide and easy scaling
#1,2,3,4,5,6
Replica
#1,2,3,4,5,6
Replica
#1,2,3,4,5,6
#1,2,3,4
Replica#5.6
#5,6
Replica
#1,2,3,4

## Slide 6: from virtualization to “elastic core”
 |  | Use case examples | Requirements |  | Potential benefits
 |  |  | Time to complete (resource adjustment) | Resource sharing range Geographical/node-wise | 
1st Ph. | Easy operation | Pre-planned node deployment/ reduction |  |  | Ease of infrastructure resource prediction
2nd Ph. | Efficiency | Fluctuation between day/night |  |  | CAPEX reduction
 | Elasticity | Congestion control |  |  | Improved service continuity
Final | Resiliency | Resiliency against disasters No SBY |  |  | Further service availability Further CAPEX reduction
～30 min
～5min
・nation-wide
・all nodes
・node building
・multiple nodes of
the same type
・node building
・1 node
～week/day
Type2. ELASTIC CORE (Scaling by the nodes) (slide 5)
Type1. ELASTIC CORE (Scaling internal components in a node)
Virtualization (slide 4)