## Slide 1: Motivation for Study on enhancing 5G system with satellite backhaul
CATT,China Telecom,InterDigital

## Slide 2: Backhaul technology in 5G
optical fiber network
wireless terrestrial networks
This backhaul technology has deployed for the cellular network many years, and it is out of 3GPP scope.
This backhaul technology had studied in RAN in REL 16.

## Slide 3: Satellite backhaul scenarios（1）
gNB deployed in aircraft；
Satellite backhaul between the gNB and 5GC；
When aircraft and satellite move, the backhaul link will change between the satellites
Untrusted non 3GPP access network (e.g. WLAN) is deployed on the cargo ship；
Satellite backhaul between the untrusted non 3gpp access network and N3IWF；

## Slide 4: Satellite backhaul scenarios（2）
When the fiber network break off under calamity scenario( e.g. earthquake etc), gNB can access the 5GC through satellite backhaul;
gNB can connect different backhaul link over different satellite because the satellite keeps moving
gNB can connect two backhaul links over two satellites to ensure the reliable transmission
Access to 5GC through the fiber and satellite simultaneously

## Slide 5: Motivation of the study
Latency of the Backhaul= User link latency （10ms）+Feeder Link latency（10ms） + ISL latency（if available）（100ms * ISL number）
The service experience will be impacted with the latency of the backhaul, e.g. whether IMS voice can be supported when satellite backhaul is used considering the maximum latency
The capacity of gNB is restricted by the bandwidth of the satellite backhaul
The service experience will be impacted with the bandwidth of the backhaul, e.g. whether UE-AMBR need to be adjusted based on the bandwidth of the satellite backhaul.
A gNB connect to a moving satellite may subject to backhaul connections change, and then may cause service interruption, so whether the requirement to the network deployment is required, e.g. a gNB shall be able to simultaneous connect to two satellites

## Slide 6: Objective
To identify and to study new use cases whether satellite components (e.g. satellite GEO, LEO, with or without inter satellite links, etc.) can be used as transport / backhaul in a 5G system.
Investigating potential requirements on 5G systems identified in the above new use cases, e.g. the requirements on QoS control, requirements for management and charging, regulatory requirements and do a gap analysis with existing 3GPP 5G system functionalities.

## Slide 7
THANK YOU
www.datangmobile.cn