## Slide 1: Resident Terminology
Discussion for CC
Toon Norp, FS_Resident Rapporteur
3GPP TSG-SA WG1 Meeting #92e S1-204302
Electronic Meeting, 11-20 November, 2020 (revision of S1-204xxx)

## Slide 2: Input to this meeting
 | KPN | Nokia S1-204081 | Huawei S1-204173
Indoor small basestation: | S1-204268 An indoor small base station is a customer-premises equipment that connects a 3GPP UE over NR wireless air interface. The indoor small base station connects to a 5G Residential Gateway which is connected to the 5GC via either fixed broadband access or NG-RAN | Premises radio access node: a small basestation primarily for use in a small indoor facility such as a residence or storefront. | is a base station that provides better cellular coverage for UEs in the indoor environment. For backhaul connection to the 5GC, the indoor small base station connects to the 5GC via the residential gateway, while the residential gateway could connect to the 5GC via a macro base station or fixed network.
Residential gateway | S1-204269 The Residential Gateway (RG) is a device providing, for example voice, data, broadcast video, video on demand, to other devices in customer premises. The residential gateway separates customer premises equipment from the equipment in the public network. | Premises radio access node aggregator: aggregates signalling from multiple premises radio access nodes to provide a single entity look and feel to the core network. | 
5G Residential Gateway | A 5G-Residential Gateway (5G-RG) is a Residential Gateway capable of connecting to the 5GC, via either fixed broadband access, cable access, or NG-RAN. |  | 
CPE | a customer-premises equipment or customer-provided equipment (CPE) is any device located at a subscriber's premises and connected with a public network via a residential gateway. |  | 

## Slide 3: Observations made online
We should not use architecture concept in definitions (e.g. a X is defined as something that connects to Y)
We should keep close to terminology that was adopted in WWC work between SA2 and BBF, on the other hand indicating that new functionality is added
Important that we are talking about ‘customer premises equipment’, i.e. different from fully operator owned and controlled network environments
Words like “small” are not well defined and not very helpful
FS_Resident definitions should also be applicable to PINs

## Slide 4: Suggested new terms
The following terms seem to get support online
  Premises Radio Access Station – PRAS
  Evolved Residential Gateway - eRG
Proposal is to use these terms and create definitions for them

## Slide 5: Suggested definition PRAS
Premises Radio Access Station: a small basestation primarily for use in a small indoor facility such as a residence, office, or shop storefront.

## Slide 6: Suggested definition eRG
Evolved Residential Gateway: the evolved residential gateway is a gateway between the public operator network (fixed/mobile/cable) and a Customer Premises network within a residence, office or shop.

## Slide 7: Pictorial view
CPE Function
Direct Network
Connection
Direct Device
Connection
Direct Network
Connection
5GS