## Slide 1
China Telecom
Minimization of Service Interruption Phase 2
Motivations, Use Cases and Proposal

## Slide 2
  Motivations
Ensuring the availability of the 5G core network service is critical, because the number of the users that are impacted by the core network is large. If the 5G core network fails, the communication service for millions of users would be interrupted.
The scope of Rel-17 MINT feature is restricted to RAN failure, and we propose to lift this limitation to include failures of the core network. It is noted that the scope of this study excludes any network failure that includes the UDR/UDM and AUSF network functionality.
In addition to Disaster Roaming provided in MINT, there could be other solutions to minimize service interruption when considering different failure scenarios.
For example: in TS 23.501, the 5G Multi Operator Core Network (5G MOCN) network sharing architecture is supported, in which only the RAN is shared in 5G System. Operators with 5G MOCN architecture could utilize the cooperation in network sharing to minimize communication service interruption. When a network cannot provide communication service to its users due to core network failures, its users may be switched to one of the cooperative operators serving as the backup core network. Thus, 5G MOCN can be considered as an example scenario to be studied.

## Slide 3
  Use Cases
#1 Core network failure due to failed network control
Failed upgrade of NF/NE(s), computer virus, software bugs, incorrect network configurations or malfunctions may cause abnormal behavior of the core network and put the entire network out of service. Many operators have reported network service outage due to the above problems in recent years.
#2 Core network failure due to natural disasters
Natural disasters such as storms, floods and fires may lead to extreme and sudden damage to core network NF/NE(s) in a particular region. Such events have led to lots of network service disruptions in the past few years.
For example:
In the 5G MOCN scenario, when a natural disaster (e.g. fire) happens in Location A, the core network of Operator A is severely damaged and unable to serve its users (shown in red). Its users may be switched to the core network of one of its cooperative operators (e.g. Operator B in Location B).
Meanwhile, to minimize the impact to the home users of Operator B, it might be possible that only part of the users or services are switched.

## Slide 4
  Proposal
The aim of this study is to gather and analyse scenarios where interruption to communication service occurs and to derive potential service requirements out of the scenarios, while meeting applicable regional regulatory requirements. The following areas will be studied:
Identifying the potential service requirements of mitigations that go beyond those defined in MINT.
Identifying use cases and potential service requirements to support minimization of service interruption for core network failures, which goes beyond the scope of MINT which was constrained to scenarios triggered by failure of the radio access network.
Other aspects, including regulatory, security and privacy requirements.
This study discusses different scenarios in which interruption could occur and interruption minimized, including e.g. network sharing.
This study considers core network failures and RAN failures, though any network failure that includes the UDR/UDM and AUSF network functionality is excluded.
This study has no backwards incompatibility with Rel-17 MINT.

## Slide 5
THANKS
感 谢 聆 听