## Slide 1
Mobile Terminated call optimization in case of Ultra-Flash CSFB(SRVCC based CSFB)
Source Company: China Unicom, Huawei, Hisilicon
SA WG2 Meeting #100  S2-134171
11 - 15 November 2013, San Francisco, USA

## Slide 2: Caller Line Identification optimization for normal CSFB
23272-8b0
7.3 Mobile Terminating call in Active Mode - PS HO supported
1a. The MSC receives an incoming voice call and responds by sending a Paging Request (IMSI or TMSI, optional Caller Line Identification and Connection Management information, CS call indicator) to the MME over a SGs interface.
The eNodeB forwards the paging message to the UE. The message contains CN Domain indicator and, if received from the MSC, the Caller Line Identification.
1b. UE sends an Extended Service Request (Reject or Accept) message to the MME for mobile terminating CS fallback. The Extended Service Request message is encapsulated in RRC and S1‑AP messages. The UE may decide to reject CSFB based on Caller Line Identification.
Background
For Mobile terminated call, UE has to fall back to 2/3G to enter in Alerting and the CLI will be displayed to user at this time. This means UE will always fall back to 2/3G for MT call even the user does not want to accept the MT call that results in following issues:
  The data calls in LTE will be interrupted that results in bad user experience.
  UE return back to LTE could take a longer time and user cannot enjoy the high speed of LTE
  Unnecessary inter-mobility between LTE and 2/3G that results in signaling burden in operator networks
In Rel-8, MME indicates CLI (if available/allowed) to the terminated user in order to have a chance to decide whether or not accept the call.

## Slide 3: Caller Line Identification optimization for normal CSFB(Cont)
Problem for current mechanism
How to display CLI in UE
  For legacy 2/3G call, the UE will enter into Alerting state when displaying CLI to user.
  But this is nor possible for CSFB MT UE as the UE will fall back to 2/3G and enter into Altering sate after a normal MT call procedure.
User experience
  Assuming the UE is able to display CLI to user and the user is decided to answer the call.
  After that, the user would like to communicate with the peer side but cannot hear anything for several seconds.
  However, the UE still need to fallback to 2/3G and finish MT call procedure that will take a long time.
Due to these two problems, this feature is not implemented as the time being.

## Slide 4: Caller Line Identification & Ultra Flash CSFB
Upon receiving CSFB page with CLI, UE enters into Alerting State.
(1) MSC/UE create MT call (TI=0,TI Flag=1) during SRVCC HO
(2) As MSC/UE reuse the MT call, there is no need of MT call procedure.
According to the testing in Huawei lab, it takes about 1 seconds to have active CS Bearer

## Slide 5: Caller Line Identification & Ultra Flash CSFB(Cont)
Call flows description
  Regarding MT call for Ultra-Flash CSFB, upon receiving CSFB page with CLI, the UE enters into Alerting State and wait for user’s decision in LTE.
    If the user decides to pick up the call, the UE sends Extended Service Request(Accept) to MME and trigger Ultra-Flash CSFB. The MSC/UE will reuse the MT call created during SRVCC HO and therefore there is no need of MT call procedure.
    If choosing to reject , the UE sends Extended Service Request(Reject) to terminate the CSFB.
Open Discussion
  After discussion with Huawei and according to the testing in Huawei lab, it takes about 1 seconds to make active CS bearer ready after UE accept the CSFB call and send Extended Service Request.
  It looks acceptable for user experience as it will takes 1 or 2 seconds for user to accept the MT call and put the phone to the ears. Further, it looks similar to the legacy CS call with late assignment
Advantages and proposal
(1) For MT call, the UE can be in Alerting state in LTE and does not impact the high-speed data in LTE.
(2) The UE will enter into Alerting State upon receiving CSFB page that further reduce the call setup time e.g. the E2E call setup time could be less than 3 seconds.
(3)Propose to discuss this and have this feature in Rel-12.

## Slide 6
Thank You !