## Slide 1: Discussion on 5G Control Plane Protocol Stacks
LG Electronics Inc.
SA WG2 Meeting #121
15 - 19 May 2017, Hangzhou, P. R. China

## Slide 2: Issue 1. UE-5GC (NAS) protocol stack
There are two alternative proposals for UE-5GC protocol stack (NAS)
  Alt 1-1. Generic NAS layer between UE and AMF, and additional NAS protocol on top of Generic NAS layer for both UE-AMF and UE-SMF NAS protocol.
  Alt 1-2. Single UE-AMF NAS protocol layer, and UE-SMF NAS protocol on the top of the UE-AMF NAS protocol.

## Slide 3: Issue 1. UE-5GC (NAS) protocol stack
This issue is related to what is discussed in CT1, how to design 5G NAS protocol.
In the last CT1 meeting, the following was agreed (TR 24.890 v0.1.0)
  5G NAS consists of two main functions: 5GMM and 5GSM
  5GMM procedure can be specific procedures (e.g. registration/deregistration), CM procedures (e.g. service request / paging) and common procedure (e.g. transport of SM NAS/SMS/etc.)
  A 5G SM message can be piggybacked in a 5G MM message. To this purpose, the 5G SM messages can be transmitted in an information element in the 5G MM messages.
So it seems that Alt 1-2 is more aligned with CT1 agreement.
  Even in S2-172649, alt 1-2 is adopted, only with a difference of the name of the protocol between UE and AMF (N1-NAS-Transport)
  It will be better to be aligned with stage 3 for the name, so “NAS-MM” would be a good choice.
Proposal 1: There is a single NAS protocol layer between the UE and the AMF. This NAS protocol is responsible for 5GMM functionalities, including transport of non-MM messages between UE and AMF. This layer can be referred as “NAS-MM”

## Slide 4: Issue 2. AN-5GC (N2) protocol stack
Regarding the protocol stack between the AN and the AMF, RAN3 agreed as follows according to TS 38.300 (R3-171329)
  The application layer signalling protocol is referred as NG-AP
  The transport network layer is built on IP transport
  SCTP is added on top of IP for the reliable transport of signalling messages
For the protocol stack between the AN and the SMF, it is desired to achieve decoupling of AMF and SMF in terms of each N2 information.
  This is already reflected in 502, while the SMF sends “N2 SM information” to the AMF and AMF just relays this information to the AN via NG-AP message.
  In S2-172649, it is proposed to introduce “N2-AP-SM” (sub)layer between the AN and the SMF, which seems transparent to the AMF.
  Whether there is needs for additional sublayer on the top of NG-AP and N11 is FFS for now..
SCTP
IP
Data link layer
NG-AP
Physical layer
Are these layer needed?

## Slide 5: Issue 2. AN-5GC (N2) protocol stack
While the purpose of this layer is for decoupling of AMF and SMF, it seems not necessary to introduce new layer for this purpose.
  For example, current procedure only refers “N2 SM information” between the AN and the SMF. Even though it is a kind of Information Element in N11-AP and N2 (or NG-C), it is okay if the AMF does not refer or manipulate the information, but just relay the field to the other protocol message.
This has a huge impact on N2/N3 (or NG) protocols, which needs to be analysed and studied for the impact to other procedures, as well as the impact in RAN WG3. So it will be beneficial to wait until RAN3 decide how to design NG-AP regarding SM related information.
Proposal 2: Whether an additional (sub)layers above NG-AP in the AN and N11 in the SMF is needed for AN-SMF interaction transparent to the AMF will be determined in RAN WG3
  It may be beneficial to ask RAN3 about this issue and request for their feedback.

## Slide 6: Summary
For UE-5GC (AMF/SMF) CP protocols stacks,
  Proposal 1: There is a single NAS protocol layer between the UE and the AMF. This NAS protocol is responsible for 5GMM functionalities, including transport of non-MM messages between UE and AMF. This layer can be referred as “NAS-MM”
For AN-5GC (AMF/SMF) CP protocol stacks,
  Proposal 2: Whether an additional (sub)layers above NG-AP in the AN and N11 in the SMF is needed for AN-SMF interaction transparent to the AMF will be determined in RAN WG3
Companion p-CR S2-173245 proposes changes and new protocol stacks.