## Slide 1
Summary on Slice IWK
© 3GPP 2018 SA2-184944 TSG SA2#127bis Newport Beach, USA, May 28 – June 1
Huawei, Hisilicon

## Slide 2: 6.5.1 Slice IWK Related Contribution
6.5.1 | S2-184716 | CR | Approval | 23.502 CR0383R8: EBI allocation and slicing interworking with EPS | Qualcomm Incorporated | Rel-15 | 5GS_Ph1 | Revision of (Agreed with objection from Huawei) S2-184563 fro S2#127 Slice IW
6.5.1 | S2-184813 | CR | Approval | 23.502 CR0369R2: Clarification on the EBI assignment, PDU session ID list in Registration and PDU session correlation. | Qualcomm Incorporated | Rel-15 | 5GS_Ph1 | Revision of (Agreed) S2-184074 from S2#127 Slice IW
6.5.1 | S2-184722 | CR | Approval | 23.501 CR0330: Clarifying slicing interworking principles | Qualcomm Incorporated, Intel | Rel-15 | 5GS_Ph1 | Slice IW
6.5.1 | S2-184723 | CR | Approval | 23.502 CR0387: Clarifying slicing interworking principles | Qualcomm Incorporated, Intel | Rel-15 | 5GS_Ph1 | Slice IW
6.5.1 | S2-184958 | CR | Approval | 23.501 CR0376: Correction to Network slicing and Interworking with EPS | China Telecom | Rel-15 | 5GS_Ph1 | Slice IW
6.5.1 | S2-184973 | CR | Approval | 23.501 CR0383: Clarification on usage of PLMN ID received via PCO during PDN connection establishment | LG Electronics | Rel-15 | 5GS_Ph1 | Slice IW
6.5.1 | S2-184693 | LS In | Action | LS from CT WG4: LS On SNSSAI During EPS to 5GS Mobility | CT WG4 (C4-183468) | Rel-15 | 5GS_Ph1 | Responses drafted in S2-184719 and S2-185095
6.5.1 | S2-185093 | CR | Approval | 23.501 CR0402: VPLMN S-NSSAI during mobility from EPS to 5GC with N26 | Huawei, Hisilicon | Rel-15 | 5GS_Ph1 | Slice IW
6.5.1 | S2-185094 | CR | Approval | 23.502 CR0449: VPLMN S-NSSAI during mobility from EPS to 5GC with N26 | Huawei, Hisilicon | Rel-15 | 5GS_Ph1 | Slice IW
6.5.1 | S2-185109 | CR | Approval | 23.502 CR0454: Subscription of supporting interworking with EPS | Huawei, HiSilicon | Rel-15 | 5GS_Ph1 | Slice-IWK
6.5.1 | S2-184719 | LS OUT | Approval | [DRAFT] Reply LS on SNSSAI During EPS to 5GS Mobility | Qualcomm Incorporated | Rel-15 | 5GS_Ph1 | Response to S2-184693
6.5.1 | S2-185095 | LS OUT | Approval | [DRAFT] LS response on SNSSAI During EPS to 5GS Mobility3 | Huawei, Hisilicon | Rel-15 | 5GS_Ph1 | Response to S2-184693

## Slide 3: Topic 1: V-S-NSSAI in the RAN/UE for HR case during IRAT mobility
S2-184693 LS from CT WG4: LS On SNSSAI During EPS to 5GS Mobility
S2-184719 [DRAFT] Reply LS on SNSSAI During EPS to 5GS Mobility
S2-185095 [DRAFT] LS response on SNSSAI During EPS to 5GS Mobility
S2-185094 23.502 CR0449: VPLMN S-NSSAI during mobility from EPS to 5GC with N26
V-SMF does not do the mapping between H-S-NSSAI and V-S-NSSAI.
Connected state mobility:
AMF provide the default V-S-NSSAI to the V-SMF, which is populated in the N2 container sent to RAN. During the Registration procedure, the AMF do the mapping or query the NSSF get the mapping value of the H-S-NSSAI and provided it to the UE, and update the V-SMF.
Per that updated value, V-SMF update the RAN with the mapped H-S-NSSAI value.

## Slide 4: Topic 1: V-S-NSSAI in the RAN/UE for HR case during IRAT mobility
Idle State mobility(with N26):
AMF provide the default V-S-NSSAI to the V-SMF and notify the V-SMF to activate the PDU Session at the same time in case registration with the activation flag.
AMF derive the V-S-NSSAI first based on the received H-S-NSSAI. AMF can update the V-SMF with the correct V-S-NSSAI.
If S-NSSAI is agreed to be added into registration request NAS message, the AMF can provide VPLMN S-NSSAI to V-SMF. By that it can avoid send the default V-S-NSSAI to the V-SMF and do the update later when the H-S-NSSAI is got.
Idle State mobility(without N26):
Similar if the UE can include the H-S-NSSAI in the PDU Session Establishment message, it can avoid send the default V-S-NSSAI to the V-SMF and do the update later when the H-S-NSSAI is got.
C1: Take S2-185094/5095 as base line.

## Slide 5: Topic 1: V-S-NSSAI in the RAN/UE for HR case during IRAT mobility
Open issue:
whether the Registration Accept message sent to the UE needs to include the PDU Session ID and S-NSSAI
Background
UE has (or receives) the mapping from HPLMN S-NSSAI to VPLMN S-NSSAI as part of the configured NSSAI
One company believes that we need to send the (PDU Session ID, S-NSSAI) to the UE in the Registration Accept in addition
Proposed way forward: Do not send the (PDU Session ID, S-NSSAI) to the UE again in the Registration Accept.

## Slide 6: Topic 2: IWK without N26 case
S2-184722 23.501 CR0330: Clarifying slicing interworking principles
S2-185093 23.501 CR0402: VPLMN S-NSSAI during mobility from EPS to 5GC with N26
S2-184723 23.502 CR0387: Clarifying slicing interworking principles
S2-185094 23.502 CR0449: VPLMN S-NSSAI during mobility from EPS to 5GC with N26
IWK Without N26 case, what is the UE behavior at 5G side:
  RRC layer, the S-NSSAI received from PGW-C+ SMF is included.
  NAS layer,
  Registration : the S-NSSAI is suggested to be sent to the AMF, which can provide corresponding VPLMN S-NSSAI to UE in registration accept message, hence UE can provide VPLMN S-NSSAI in PDU Session establishment request.
  PDU Session establishment: This is to make consistence of the UE behavior.
C2: Take S2-185093 as base line.

## Slide 7: Topic 3: EBI allocation
S2-184716 23.502 CR0383R8: EBI allocation and slicing interworking with EPS
  Multiple PDU sessions for the same DNN but different S-NSSAI scenario, Same PGW-C+SMF case
    Case 1: Served by one Common UPF, all PDU Session associated with this UPF are requested by SMF for EBI application.
    Case 2: Served by different UPF, only one UPF and its associated PDU Session is selected by SMF for EBI application.
C3: Take S2-184716 as base line.

## Slide 8: Topic 4 clarification
Remove “received from PGW-C/SMF” as PDU Session ID is not received from PGW-C/SMF
NAS layer the S-NSSAI deleted part is to be changed back.
C4: the S-NSSAI original deleted is to be recovered.
S2-184813, 23.502 CR0369R2: Clarification on the EBI assignment, PDU session ID list in Registration and PDU session correlation.

## Slide 9: Topic 5 IWK subscription
S2-185109 23.502 CR0454: Subscription of supporting interworking with EPS
Add the subscription parameter into the UDM subscription table.
Clarify the condition when the PGW-C+SMF do the EBI allocation, i.e. only if the subscription data for the DNN and S-NSSAI associated with this PDU session indicates support for interworking with EPS
There some UE granularity PDU Session subscription data, e.g. SSC mode, PDU type, which will impact the IWK. It is better to also introduce the Per UE granularity IWK subscription .
Suggestion, take S2-185109 as base line for alignment work.

## Slide 10: Summary of each topic
6.5.1 | S2-184716 | CR | Approval | 23.502 CR0383R8: EBI allocation and slicing interworking with EPS | Propose to handle this document, no revision is needed according drafting session
6.5.1 | S2-184813 | CR | Approval | 23.502 CR0369R2: Clarification on the EBI assignment, PDU session ID list in Registration and PDU session correlation. | Propose to handle this document, Revision is needed to change the S-NSSAI included in NAS back.
6.5.1 | S2-184722 | CR | Approval | 23.501 CR0330: Clarifying slicing interworking principles | 
6.5.1 | S2-184723 | CR | Approval | 23.502 CR0387: Clarifying slicing interworking principles | 
6.5.1 | S2-184693 | LS In | Action | LS from CT WG4: LS On SNSSAI During EPS to 5GS Mobility | 
6.5.1 | S2-185093 | CR | Approval | 23.501 CR0402: VPLMN S-NSSAI during mobility from EPS to 5GC with N26 | Propose to handle this document, no revision is needed according drafting session
6.5.1 | S2-185094 | CR | Approval | 23.502 CR0449: VPLMN S-NSSAI during mobility from EPS to 5GC with N26 | Propose to handle this document, no revision is needed according drafting session
6.5.1 | S2-185109 | CR | Approval | 23.502 CR0454: Subscription of supporting interworking with EPS | Propose to handle this document, no revision is needed according drafting session
6.5.1 | S2-184719 | LS OUT | Approval | [DRAFT] Reply LS on SNSSAI During EPS to 5GS Mobility | 
6.5.1 | S2-185095 | LS OUT | Approval | [DRAFT] LS response on SNSSAI During EPS to 5GS Mobility3 | Propose to handle this document, no revision is needed according drafting session