## Slide 1: MUSIM UE and Same PLMN discussion. (Samsung, NEC, Airtel) S2-1911891

## Slide 2: Contents
Issue discussion
What is available from release-15.
Solution
Conclusion

## Slide 3
USIM1 stack
USIM2 stack
AMF
N1 signalling connection is active for USIM 2.
MT data for USIM-1 stack
Issues:
Even though there is a direct N1 signalling connection to the UE(for USIM-2 stack). Network will end up doing paging broadcast consuming the RAN resources.
Worst is: The UE may decide not to respond to paging (e.g. due to a paging cause, the UE implementation deems ‘lower priority.’) This will lead to retransmission of the page by the PLMN. Based on paging strategy, the paging can get escalated. This will use significant network resources.
UE has to keep switching the RF on paging occasions to see if paging message is received to the UE for USIM-1 stack which will:
  Impact data throughput of the UE’s USIM-2 stack as data transfer is effected when UE tunes its RF to check for paging of USIM-1 stack.
  Battery is consumed when UE continuously switches the RF to just check if there is a paging message available for the UE’s USIM-1 stack.
Issue discussion:
UE
Paging message for USIM1 GUTI

## Slide 4
3GPP access
N3GPP access
AMF
NOTIFICATION message for 3GPPA over N1 signalling connection of N3GPPA
MT data for 3GPPA PDU session
AMF has a knowledge that 3GPP access MM context and N3GPP access MM context belongs to the same UE.
With the knowledge of AMF, if the UE is in IDLE mode over 3GPPA and in Connected mode over non-3GPP access, then AMF can send NOTIFICATION message to the UE instead of sending paging broadcast message.
If UE is able to respond it will send service request over 3GPP access otherwise UE will respond back with NOTIFICATION RESPONSE indicating its inability to respond with service request procedure.
Clearly there are benefits to the system from resource utilization perspective.
What is already available from release-15:
UE

## Slide 5
AMF
Step 1(Current spec):
Registration procedure is successfully executed and GUTI-1 allocated to USIM-1 stack.
Steps:
Registration procedure is successfully executed and GUTI-1 allocated to USIM-1 stack following current specification.
During registration procedure of USIM-2 stack indicate to AMF that GUTI-1(assigned to USIM-1) is part of same UE. Further, following current specification GUTI-2 is allocated to USIM-2 stack.
AMF knowledge is now enhanced that GUTI-1 MM context and GUTI-2 MM context belongs to the same UE.
Solution(slide-1)
Enhance AMF’s knowledge that both the USIM’s belongs to same UE:
UE
USIM1 stack
USIM2 stack
Step 2(proposed change):
As part of registration request message indicate GUTI-1(i.e. USIM-1) is part of same UE.

## Slide 6
AMF
NOTIFICATION message for USIM-1 stack over N1 signalling connection of USIM-2 stack.
MT data for USIM-1 stack
AMF has a knowledge that USIM-1 MM context and USIM-2 MM context belongs to the same UE.
With the knowledge of AMF, if the UE is in IDLE mode over USIM-1 stack and in Connected mode over USIM-2 stack, then AMF can send NOTIFICATION message for USIM-1 stack over N1 signalling connection of USIM-2 stack to the UE instead of sending paging broadcast message.
If UE is able to respond it will send service request over 3GPP access otherwise UE will respond back with NOTIFICATION RESPONSE indicating its inability to respond with service request procedure.
UE will not monitor the paging channel for USIM-1 stack and its expected to receive and DL information over USIM-2 stack.
Solution(Slide-2):
UE
USIM1 stack
USIM2 stack

## Slide 7: Conclusion:
With following proposed changes:
  Enhancing AMF’s knowledge that MUSIM’s belong to the same UE; and
  Instead of blindly sending paging using broadcast mechanism sending NOTIFICATION message over the connected mode N1 signalling connection;
The 3GPP system can:
  Save greater amount of network resources: As AMF can define a paging strategy to page the UE using existing NAS N1 signalling connection.
  Data throughput can be increased: As UE does not switch to read the paging channel for second USIM stack when data transmission is ongoing for the first USIM stack.
  UE’s battery consumption is reduced: As UE’s RF need not be tuned between two USIM’s stack to read the paging channel when one of the USIM is in connected mode.

## Slide 8: Thank You !!