## Slide 1: Security concern of option 2 and option 3b for Solution 22 in TR 23.748
Document for: LS out to SA3
Agenda Item: 8.3
Work Item / Release: FS_enh_EC / Rel-17
China Mobile, CATT,

## Slide 2: Background
Solution 22 in TR 23.748 introduces a “LDNSR” to receive DNS query from UE and insert ECS option, and then send it to DNS server with replacing DNS query target IP address to target DNS server if needed.
There are 3 options in Solution 22.
  Option1: LDNSR insert ECS option in DNS query to indicate UE location to C-DNS
  Option 2a: LDNSR forwards the DNS query to L-DNS; the forwarded DNS query targets the L-DNS address
  Option 2b: LDNSR request the SMF to forward the DNS query to L-DNS through 5G user plane also; the forwarded DNS query targets the L-DNS address
  Option 3a: DNS query is offloaded to local PSA and then a local LDNSR inserts ECS option for resolution.
  Option 3b: DNS query is offloaded to local PSA and then sent to a local DNS resolver, the local DNS resolver replace the DNS query target IP address to L-DNS address.
Observation
When UE is configured with C-DNS address, the LDNSR can change the DNS query target IP address to L-DNS address, while the DNS query is intent to be terminated in C-DNS.
LDNSR is a functionality which belong to 5GS,and act as a DNS resolver. Whether the LDNSR can be trusted by DNS system is FFS.

## Slide 3
Question: whether there is security risk for the option 2 and option 3b of solution 22, considering that the DNS query originated by the application client in the UE is handled by a DNS resolver in the MNO network, which can forward the DNS query to an Authoritative DNS Server outside the MNO network with changing the DNS query IP address; the Authoritative DNS Server belongs to the service provider of the application installed on the UE.
Proposal: A LS should be sent to SA3 to check whether there is security risk for option 2 and option 3b of solution 22.