## Slide 1
Discussion on LCS-UP binding issue
SA2#162
vivo

## Slide 2
CT1 LS raises two issues for LCS-UP connection between the UE and the LM. Summary:
  1. Whether and how to link one UE with one TLS connection by the LMF? (in case of creating a new connection)
  2. Whether and how to reuse the established TLS connection when the subsequent LCS request for the same UE comes? (in case of reusage of the existing connection)
  Excerpted from incoming LS C1-241722:
  1. After the TLS connection is established, the UE and the LMF initiate LPP or LCS-SS procedure. For the LMF-initiated case, given that multiple UEs are served by the LMF and multiple TLS connections are active, the LMF needs to determine a TLS connection for the target UE. However, it has not been specified how to link the association between the TLS connection and the UE, e.g., how the LMF knows which TLS connection is for the UE who has received the UPP-CM command message. If the TLS connection can be linked to the ‘wrong UE’ then there could be a risk of location related data from one UE which is sent to another UE.
  2. Once the binding of the TLS connection to the UE is done, if there is a new LCS service request (e.g., MT-LR) for the same UE, the AMF invokes Nlmf_location_determinelocation service operation to the LMF. However, it has not been specified how the LMF associates the LCS service request to the TLS connection of the UE. In this case, the LMF cannot determine which TLS connection can be used for the LCS service request. Therefore, the LMF cannot reuse the TLS connection of this UE for subsequent LCS service request(s).
Introduction

## Slide 3
1. In case of creating a new user plane connection:
LMF keeps multiple TLS connections with different UEs.
LMF needs to know who is using the specific TLS connection in order to accurately deliver LPP/LCS-SS messages.
Observation 1: The LCS-UP binding procedure is needed so that the LMF can link one TLS connection with one UE.
Discussion

## Slide 4
2. In case of subsequent location requests for the same UE:
During LMF selection, the following factor is considerable, but not crucial: Requested UE has maintained user plane connection with certain LMFs.
For MT-LR/deferred MT-LR and MO-LR cases, the correlation ID is included in Nlmf_Location_DetermineLocation request message, which is per LCS session/request granularity, not per UE granularity. Correlation ID has no relationship with LCS-UP connection, which may cause the LMF to reperform a ‘new’ LCS-UP connection establishment for this request.
Observation 2: Current information in Nlmf_Location_DetermineLocation service message could not enable LMF to reuse the same LCS-UP connection.
Observation 3: Redundant binding procedures may be performed if reusability is not supported.
Discussion

## Slide 5
Conclusions:
the LCS-UP binding over TLS needs to be supported so that the LMF can link one secured user plane connection with one UE.
the LMF also needs to be enabled to reuse the same secured user plane connection when receiving the subsequent location service for the same UE.
Proposal 1: The binding procedure using an LMF-locally unique ID is performed via TLS between the UE and LMF. The signaling detail of the procedure is left for CT1 design.
Proposal 2: LCS-UP connection ID is provided by LMF and stored in AMF after the LCS-UP connection is established successfully.
Proposal 3: The AMF selects the LMF that maintains an existing user plane connection with the requested UE when performing LMF selection. The Nlmf_Location_DetermineLocation service message is enhanced to include the LMF-locally unique ID, if exists, to the LMF.
LS (S2-2404044) and attached CR (S2-2404045) for TS 23.273 are proposed as the resolution.
Conclusions

## Slide 6
Thanks

## Slide 7
How SUPL achieves:
SUPL INIT message used to initialize the SUPL session includes a SET ID, which identifies one SET (e.g., IMSI, SUPI, MSISDN). the SLP can know which SET is using the SUPL session.
LCS-UPP now could not take the same action as SUPL since the LMF may be not aware of UE ID (e.g., SUPI, MSISDN) caused by that AMF does not indicate UE ID to the LMF.
SET: SUPL Location Platform
SLP: SUPL Enabled Terminal
MSISDN: Mobile Station International Subscriber Directory Number
Annex 1

## Slide 8
Potential solutions for binding discussed in stage 3:
IP address binding: UE IP address can be used during the TLS handshake procedure, but LMF could not distinguish which UE is handshaking with LMF since NAT issue exists.
UE ID binding: UE ID (e.g., SUPI) is sent to LMF via LCS-UPP messages to bind the UE and TLS connection, but LMF may be not aware of UE ID (see Annex 1).
LCS-UP connection ID binding: LMF allocates a connection ID to link one UE and one connection. The UE and LMF performs binding using this ID. But some enhancements in SA2 need to be agreed at first.
Annex 2