## Slide 1: Discussion on R19 AIML_CN KI#4: Signalling Storm Detection, Prediction, Mitigation and Prevention
SK Telecom, China Mobile, China Telecom, Dish Network, ETRI, KDDI, KPN N.V., NTT DOCOMO, Lenovo, LG Uplus, Rakuten Mobile, Samsung, TOYOTA MOTOR CORPORATION, vivo

## Slide 2: Discussion 1/2
NF abnormality resulting signaling storm
  KI#4 and its use-case was discussed in SA2#160AHE and SA2#161(S2-2403593) which the NF abnormality resulting signaling storm, can be analyzed and mitigated.
Dynamics of NF abnormality
  NFs can behave differently depending on 5GC topologies, dynamics of procedures, different UEs/Sessions, configurations and so on.
  Depending on the signalling storm use case some NFs may be impacted while other NFs may not.
Example illustration :
TSG SA Rel-19 Workshop (SA#100 SWS-230008)

## Slide 3: Discussion 2/2
Analytics-assist should be able to gather more information from NF dynamics on top of counting a certain number of message types, e.g., dive deeper into NF signaling information exchange.
  Accurately finding NF Abnormality could be quite complex and difficult. For example, Signaling storm should not happen often in the real-world operating environment with a thoroughly designed/verified system dimension.
  So, without more data input from NFs, we may not be able to find such NF abnormality potentially (and eventually) causing signal storms, with a reason if any.
  The data collection from each NF depends on the signaling storm scenario.
More fine-grained NF Input Data collection should increase better prediction accuracy!
Consumer NF
Producer NF
NWDAF

## Slide 4: Example of NF signaling information exchange
Service Consumer
Service Producer
Other Service
Producer(s)
Service Request
Service Response
Service Request
Service Response
Content Information
NWDAF
[Input Data]
Collected Data & Transfer
Service Producer NF example
Example illustrates the Producer NF※ procedures.
A communication between NFs in 5GC are processed as a ‘chained-procedures’, e.g., the Producer NF does not just receive service request/response from a peer NF, it can also act as the Consumer NF for secondary service request/response to other Producer NF(s).
Such NF signaling information between the Producer NF to Consumer NF can be important and improves accuracy of detecting NF abnormality.
For example, SMF (acting as producer) receiving a Service Request to create a Session from an AMF(and UE), requests (now acting as consumer) to create/get a SM Policy with PCF, which it completes the Session Management by using other services such as UDM, PCF, UPF, etc. to finally delivers the Response of Session Establishment procedure to the AMF.
※ For simplicity, we limit/focus on Producer NF, but if needed Consumer NF oriented focus can also work

## Slide 5
Service Consumer
Service Producer
Other Service
Producer(s)
Service Request
Service Response
Service Request
Service Response
Content Information
NWDAF
[Input Data]
Collected Data & Transfer
To be specific, within the ‘chained-procedures’, the Producer NF receives Service Request from Consumer NF. Depending on the Services types, message types processing, the Producer NF decides to act as a Consumer NF to further request/response other Producer NFs.
Such information from the Producer NF to a Consumer NF transition could be,
  Time (start/end), latency/jitter, processing states and causes/reasons
  Frequency/statistics related to those information
  Those information is per UE or per session.
A level of information collected to be sent to Analytics-assistance (e.g., NWDAF) can be adjusted depending on the operation policies (e.g., SBI message size, storage, system load)
※ For simplicity, we limit/focus on Producer NF, but if needed Consumer NF oriented focus can also work
Example of NF signaling information exchange - cnt
Service Producer NF example

## Slide 6: Input data collection from AMF
(Events can be obtained immediately)
  Attempt number of the request from UE/RAN such as “Initial Registration Request, Mobility and Periodic Registration Request, Service Request, etc.”
  Attempt number of the request from other NFs(such as SMF, PCF, SMSF, etc.) to occur Network Triggered Service Request procedure per UE (i.e., Paging message)
  Attempt number of UE CM state change
  Attempt number of UE AM Policy Update (URSP, Restriction Area, etc.)
  UE related state transition information (transition type and/or frequency, etc.)
  UE related timer information (type of timer, timer duration, etc.)
  Public Warning information (WRITE-REPLACE WARNING REQUEST, etc.)
(Events that may need some generations)
  Procedure event trend per certain Area of interest, slice, DNN, NSSAI, TAC(Type Allocation Code)
  Success and failure result trend (numbers within certain time interval, ratio, cause/error code etc.) per certain Area of interest, slice, DNN, NSSAI, TAC(Type Allocation Code)
  Expected (or unexpected) consequential event occur trend within a time-window (e.g., UE response after Paging)

## Slide 7: Input data collection from SMF
(Events can be obtained immediately)
  Attempt number of UE SM Policy Update (QoS, Rules, etc.)
  Attempt number of the Charging data request toward CHF
  Attempt number of the request from other NFs(such as SMF, PCF, SMSF, etc.) to occur Network Triggered Service Request procedure (i.e., N1N2Transfer via AMF for UP Deactive session)
  Load information of connected UPF(s); using PFCP Load Control Information IE
  Usage information of UE IP address resource(s)(dynamic and static, V4, V6, etc.) when CP allocation UE IP (total number, usage, number of UE IP(s) which prohibit to allocation during certain time interval, etc.)
  Usage information of UE IP address resource(s) (dynamic and static, V4, V6, etc.) when UP allocation UE IP (total number, usage, number of UE IP(s) which prohibit to allocation during certain time interval, etc.)
  UE related state transition type (transition type and/or frequency, etc.)
  UE/Session related timer information (type of timer, timer duration, etc.)
(Events that may need some generations)
  Procedure event trend per certain Area of interest, slice, DNN, NSSAI, TAC(Type Allocation Code)
  Success and failure result trend (numbers within certain time interval, ratio, cause/error code etc.) per certain Area of interest, slice, DNN, NSSAI, TAC(Type Allocation Code)
  Expected (or unexpected) consequential event occur trend within a time-window (e.g., Charging after Usage Report, Session Modification after SM Policy update)

## Slide 8: Input data collection from UPF
(Events can be obtained immediately)
  Attempt number of Session Report toward SMF occurred by DL packet
  DL pkt information; IP Packet Filter Set, Measurement period, Throughput DL(peak or not), Data volume
  UL pkt information; IP Packet Filter Set, Measurement period, Throughput UL(peak or not), Data volume
  End to End packet delay
  Usage information of UE IP address resource(s) (dynamic and static, V4, V6, etc.) when UP allocation UE IP
(Events that may need some generations)
  Procedure event trend per certain RAN(N3 Interface address), slice, DNN, NSSAI, TAC(Type Allocation Code)
  Success and failure result trend (numbers within certain time interval, ratio, cause/error code etc.) per certain Area of interest, slice, DNN, NSSAI, TAC(Type Allocation Code)
  Expected (or unexpected) consequential event occur trend within a time-window(e.g., Packet flows after Session Establishment)

## Slide 9: Input data collection from NRF/SCP
(Events can be obtained immediately)
  Load information of registered NF(s)/Service(s)
  Capability information of registered NF(s)
  Heart-beat related information (Whether to respond immediately, Number of retransmissions, heart-beat interval, etc.)
  (dynamic) network topology (per slice)
(Events that may need some generations)
  abnormal NF(s)/Service(s) status trend (transition freq. between registered vs. non-registered status)
  time internal of consumer NF receiving service response (per producer NF(s)/Service(s))
  (pre-configured) VIP's call processing latency (per call procedure)

## Slide 10: Input data collection from (common) NF
(Events can be obtained immediately)
  Kinds of connected peer Producer NF(s) and its/those number(s) (within certain time window, if needed)
  Requested service information per connected peer Producer NF(s) (within certain time window, if needed)
  SBI message/protocol handling information(retransmitted event/message count and towards which NF(s))

## Slide 11: Output examples
Detection output
  Target of the signaling storm, e.g. NF instance ID
  Anomality ID, e.g. massive UE/frequent access, NF abnormal signaling, etc..
  Source of the signaling storm, e.g. UE/NF list.
Prediction output
  Target of the signaling storm, e.g. NF instance ID
  Anomality ID, e.g. massive UE/frequent access, NF abnormal signaling, etc..
  Source of the signaling storm, e.g. UE/NF list.
  Confidence, e.g. confidence of this prediction.

## Slide 12: Mitigation or prevention examples
Handling UEs/Sessions
  Per UE/Session
    AMF sets back-off timer for MM NAS for a selected set of UEs
    SMF sets back-off timer for SM NAS for a selected set of Sessions
    PCF sets AM/SM policy control for a selected set of UEs/Sessions
  Per group
    AMF triggers RAN to initiate overload control for the UEs in specific slice, priority.
Handling NFs
  NRF configures the local policy to prevent the source NF from being discovered or discovering others.
  Source NF configures to reselect other target NFs and unsubscribes the existing abnormal NF.
  NRF configures the local policy to prevent the source NF from being discovered or discovering others or deprioritize the source NFs/Services from being select less.
  Source NF configures to reselect other target NFs and unsubscribes the existing abnormal NF or triggers UE Reregistration and/or Session Reestablishments, and reselects to other target NFs

## Slide 13
Thank you

## Slide 14
Tdoc | Title | 24.2 (SA2#161 / Athens, Greece) Solution (focusing for NF input to NWDAF) | Company
S2-2401925 | Solution to key issue 4: Signalling storm detection and mitigation based on O&M data | O&M based, MDA assistance | OPPO
S2-2402012 | New solution: NWDAF-assisted policy control for network abnormal behaviours mitigation | Use of PCF/NWDAF | KPN
S2-2402026 | Solution for KI#4: Flexible analytics design to support multiple "signalling storm" scenarios. | A.ID : SBI signalling NF -> NWDAF input data depends on the signalling storm scenario | Lenovo
S2-2402181 | KI#4: New Sol: NWDAF analytics for signalling storm prediction | ID : "Control Plane - Number of successful initial registrations, Number of mobility registration update requests, Mean time of Registration procedure, Total number of attempted service requests, Number of PDU session creation requests, Signalling Abnormality" - The service producer entity: Request throttling, Back-pressure, Connection Pooling, etc. The service consumer entity: Request throttling, NF reselection, etc. OAM: Horizontal/Vertical scaling, Proper configuration of the network entities, etc. SCP (in the case of using SCP for service communication between NFs): Request throttling, Back-pressure, Connection Pooling, etc. Max/mean/min number of request/response/ in a time window, the number of the timed-out requests, max/mean/min response time | NTT DOCOMO
S2-2402181 S2-2402762 | KI#4, New Sol: NWDAF Assisted Network Abnormal Behaviour Mitigation and Prevention | Number of NAS transactions, Number of successful NAS transactions, Number of reattempted NAS transactions, Number of registered UEs, Number of active UEs, Number of UEs with successful NAS transaction, Number of NG-RAN connections, NF service name(s)/ID(s), NF resource usage per service, NF resource capacity | Samsung
S2-2402226 | New Solution on NWDAF-assisted for 5GC handling of abnormal network behaviors | - The load of 5GC NFs. Total number of 5GC NFs interface messages. 5GC NFs interface message success rate. Current interface thresholds of the 5GC NFs, etc. | CMCC
S2-2402269 | (KI#4) Solution for NWDAF enhancements to support network abnormal behaviours (i.e. Signalling storm) mitigation and prevention | O&M based, NWDAF/MDAF assistance | Ericsson
S2-2402436 | New Solution for KI#4: Registration signalling analytics to support detection and prevention of signalling storm | Registration Signaling Information > Registration Type , > Number of registration request, > Number of registration failure UE group ID or a list of UE IDs (1..SUPImax) > Timer List >> Type of timer , >> Timestamp, >> Timer duration > Registration Type of the UE , > Number of UE registration request AMF resource usage | China Telecom
S2-2402462 | Solution (KI#4): New Analytics of NAS-Level Congestion Control for Network Abnormal Behaviour | UE ID , MMCC experience for UE >Start time of data collection , >End time of data collection, >MM NAS request (1..max) >>Type of MM NAS request , >>Timestamp >MM NAS message from network with backoff timer (1..max) >>Type of MM NAS message from network, >>Timestamp, >>Provided backoff timer | ETRI
S2-2402508 | KI#4, New Solution: NWDAF Assisted Detection and Mitigation of Signalling Storm | Timestamp , UE ID , Back-off timer, Service request statistics > Type, > Frequency, > Request result, NF load, NF status, Signalling statistics | Huawei
S2-2402732 | KI#4: New Solution – SBA signaling storm mitigation and prevention based on NWDAF detection and prediction | S-NSSAI, DNN, Source NF ID, SBA unhandled request message amount, SBA reject message amount, SBA redundant message amount, SBA message amount, Start/end time, Number of Ues, NF, Number of network context, NF load, NF resource usage | vivo
S2-2402733 | KI#4: New Solution – NAS signaling storm mitigation and prevention based on NWDAF detection and prediction | S-NSSAI , DNN, SUPI, NAS unhandled request message amount, NAS reject message amount, NAS message amount, Start/end time, Number of UEs,NF load, NF resource usage | vivo
S2-2402750 | KI#4, New Solution: NWDAF-assisted Network Abnormal Behaviour Mitigation and Prevention | NF transaction information, NF status information, NF context information | SK Telecom
  Appendix
  SA2#161
  For Information