## Slide 1: OPPO View on 6G SID WTs
OPPO

## Slide 2: Outline
List of WTs with key objectives and justification
Summary
System Architecture Evolution
Key Enabler#1: Coordinated Computing
Key Enabler#2: Unified Data Framework
MNO Service#1: AI
MNO Service#2: ISAC
Dual Steer for Migration

## Slide 3: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
WT#1 | System Architecture evolution | 1. NAS for basic functionality (i.e. RM, CM, MM, SM, UE Policy) routing over CP locally; 2. NAS for MNO services (e.g. LCS, AI, Sensing) routing over UP; 3. Related RM, CM, MM and UE Policy procedures . | Non-AMF related NAS (e.g. SM, UE Policy, LCS) messages are piggybacked in Access and Mobility Management NAS messages. As a consequence, the AMF may become a bottleneck for handling all NAS signalling in 5G design. The payload size of the NAS message for non-basic functionality (e.g. LCS, new MNO services) is increasing and conveying the according NAS messages over CP doesn't seem to be efficient. Beside that, the SRB is not designed to transfer big payload signaling/data. | RAN2/3, SA3
WT#2 | Evolved basic functionality based on 5G design | 1. QoS Model enhancement; 2. UE Policy enhancement; 3. Session Management enhancement; 4. Non-3GPP access support; 5. Network slicing simplification. | Some basic functionalities defined in 5GS can be evolved into 6GS design with proper enhancement or simplification. | RAN2/3, SA3
WT#3 | Key Enablers for new MNO services | 1. UE and network Coordinated Computing; 2. Unified Data Framework. | Following aspects are deemed as key enablers in 6GS to support new MNO services: (1) Proper management, control and allocation of computing resource, 5G EC design can be used as basis for solving the connectivity delay; (2) A Unified Data Framework enabling the data collection and management for different MNO services. | RAN2/3, SA3
WT#4 | MNO services | 1. AI; 2. ISAC; 3. Voice; 4. Emergence service. | Some critical MNO services should be supported in Day-1 design, there is no doubt on supporting voice and Emergence service, while AI and ISAC should also be supported in Day-1 design to attract customer's interest. | RAN2/3, SA3
WT#5 | Interworking and migration | 1. Inter-RAT mobility with N26 between 5GS and 6GS as default option; 2. Dual steer with dual registration based on single subscription as complementary option. | Inter-RAT mobility with N26 between 5GS and 6GS should be supported as an default option, but in early deployment, to avoid frequent Inter-RAT mobility due to ad-hoc coverage of 6G radio, Dual Steer can be supported as complementary option. Dual Steer can also be considered as an option to support migration from 4G to 6G directly if necessary. | RAN2/3

## Slide 4: Summary
6G Core Network should be designed with considering following aspects:
  System architecture is evolved to a new core network;
  Some basic functionalities can be evolved based on 5G design;
  Key Enablers are needed to accommodate new MNO services;
  Critical MNO services are supported in the beginning;
  Inter-RAT mobility with N26 between 5GS and is supported as default option, complementary option should be considered to solve the frequent early deployment issue.

## Slide 5: System Architecture Evolution
NAS messages for basic functionality (i.e. RM, CM, MM, SM, Security and UE Policy Provisioning) are still over CP;
E2E Service messages (e.g. between UE and LMF, etc.) for other functionality (e.g., LCS, other new services, etc.) are over UP.
Distributed NAS are supported for both CP and UP NAS messages, i.e. not always required to be routed via Access and Mobility Management function.

## Slide 6: Key Enabler#1: Coordinated Computing
Potential new functionality in 6GS:
Provide Computing Resource offloading to network as a service to UE under the control of MNO network;
Support the (re-)discovery of Computing Resource Offloading Function by the UE in 6GS;
Support Computing resource management with a new NF or Session Management Function in core network;
Support UP Function (e.g. PSA UPF, L-PSA UPF, etc.) (re)selection by leveraging Computing resource;
Allocate Computing resource as reserved resource to application during Session Management, which can be triggered by UE or AF during Session Manage Establishment or Modification procedure.
UE knows where, when and how to request Computing support from network.

## Slide 7: Key Enabler#2: Unified Data Framework
A common framework to support the data management including:
Data detection from various sources with the different data type (e.g., Sensing data, AI data);
Data collection;
Data processing;
Data exposure (e.g. UE, NF or 3rd party);
Data source and consumer identity validation;
Data traceability to record all the data related operation to support the trustworthy.

## Slide 8: MNO Service#1: AI
Potential new functionality in 6GS:
1. Each entity may support AI functionality natively to support the native AIML framework;
2. AI as a service to support the UE or 3rd party to perform AIML operation;
3. Network information exposure to UE/3rdparty to improve user experience;
4. AI Model Life Cycle Management (e.g. LCM components distribution in 6GS and the corresponding procedures);
5. Various AIML type supported in network (e.g. Federated learning, reinforcement learning, transfer learning, etc.).

## Slide 9: MNO Service#2: ISAC
Potential new functionality in 6GS:
Architecture and function enhancements to support sensing.
Service authorization and revocation. This includes investigating mechanisms for authorization and revocation sensing service requests from the service consumer.
Discovery and selection of sensing entities based on service requirements triggered by the service request and capability of the sensing entities.
Sensing data and the associated information collection and transport mechanisms for result calculation.
Mechanisms for providing sensing associated information and result (including sensing result and contextual information) exposure, for one time, periodic or event based reporting.
Configuration parameters/policy provisioning for the support of ISAC services.
Sensing assisted communication.
Non-UE Sensing object identification.
Non-3GPP sensing.
AI assisted Sensing.

## Slide 10: Dual Steer for Migration
Potential system impacts in 6GS:
Standalone CP and UP in both Systems, and packet convergence is done at a shared Anchor UPF and UE;
RM/CM/MM/SM need to be evolved to support Dual Steer based on Dual-registration with single USIM;
UE Policy for controlling Dual Steer operation needs to be defined;
Easy migration option from 4G to 6G.

## Slide 11
Thank you!