## Slide 1
Discussion for 6G study on Native AI
Agenda item: 30.7
Source: Samsung
Document for: Discussion
3GPP SA WG2 Meeting #168
07 – 11 April, 2025, Goteburg, Sweden
S2-2503716

## Slide 2
Each NF and RAN with native support of AI functionality
Federation or collaboration/interworking of AI functions at different NFs (e.g., MM, SM, Policy, etc.)
Cross-domain optimization across RAN, CN and OAM
Areas to be Studied
Native AI for 6G
Native support of AI functionality can contribute to achieve cost-efficient network management and optimize overall performance
Single AI-based local optimization cannot not guarantee the performance improvement of the overall system `
Motivation
Native support of AI functionalities across 6G network to improve the overall performance of 6G system and user experience by federation or collaboration of AI functions at heterogeneous NFs, RAN and OAM
AI/ML support in 5G
Native AI support in 6G
AMF
SMF
PCF
UDM
NWDAF
Analytics #A (statistics/prediction)
How to use analytics in making a decision ?
?
?
?
Undefined and unpredicted NF behaviour
(No interoperability & potential interference)
Analytics #B (statistics/prediction)
OAM (MDAF)
Reconfig. based on MDAF
Reconfig. based on MDAF
RAN AI Fn. (e.g.,NRT-RIC)
MM
SM
Policy
UDM
AIML
Native AI functionality
Federation and collaboration of AI functions to make a decision
OAM (MDAF)
RAN AI Fn. (e.g.,NRT-RIC)
Interworking between
different domains
Standard interface for distributed AI/ML
Data Mgmt. in Service Plane

## Slide 3
1. Identify impacts on system architecture and NF behaviors for embedding and supporting AI functionalities at the NFs.
2. Support of collaboration and/or interworking among AI functions at different NFs (e.g., MM, SM, Policy, etc.) in the control procedure.
3. Architecture and protocol design to support collaboration and/or interworking of AI functions across RAN, CN and OAM for, e.g., data collection, model training, inference, performance monitoring etc.
NOTE: “Service Plane” can be used for collaboration and/or interworking between AI functions.
Key Objectives
Native support of AI/ML functionalities across 6G network to improve the overall performance of 6G system and user experience by federation or collaboration of AI functions at heterogeneous NFs, RAN and OAM.
6G System Architecture Study Objectives
Notes: WT-1: Identify impacts on NF behaviours and system performance when embedding and supporting AI functionalities at the NFs
WT-2: Whether and how AI functions at different NFs (e.g., MM, SM, Policy, etc.) can collaborate and/or interwork in the control procedures
WT-3: Whether and how AI functions across RAN, CN and OAM can collaborate or interwork for, e.g., data collection, model training, inference, etc.

## Slide 4
Appendix. NF-embedded AI
Each NF has embedded AI functionalities that support to make its own decision based on its AI model and collected data
Each NF requests and uses the data received from homogeneous or heterogeneous NFs for its model training and decision making process
AI in an NF collaborates and interworks with AI functionalities in other NFs for global optimization of AI models and inferences
In order to not overload in the control plane, it may use different planes (e.g. Service Plane) to transfer the collected data and/or pre-trained AIML models
Common Data/AI Model repository can also be defined
Concept of Embedded AI
Each NF and RAN with native support of AI functionality together with centralized AI functionalities
NF-B
AI Model
Collected
Data
Internal AI Platform
(Proprietary)
Decision Logic
NF-A
AI
AI
Data and AI Model Delivery over, e.g., Service Plane
Each NF equipped with AI functionalities
Example for Embedded AI in 6G Core
Control Plane (SBI)