## Slide 1: Handling target DNAI provided by AF/PCF while I-SMF is inserted for Local Offloading Management
Nokia
Document for: Discussion Agenda Item: 19.9.2 Work Item / Release: eEDGE_5GC_Ph3 / Rel-19
SA WG2 Meeting #170 S2-2507382
25 – 29 August, 2025, Goteborg, Sweden

## Slide 2: Background
When I-SMF based Local Offloading Management is introduced (for Session Breakout connectivity model), it is noted that UE and AF are both unaware whether Local Offloading Management based I-SMF insertion is applied, see §6.10 of TS 23.548.
AF providing a target DNAI or SMF deciding a target DNAI from the (updated) list of DNAIs in PCC rule is defined in various clauses in TS 23.501 (§5.6.7, §5.13, §5.34), TS 23.502 (§4.3.6, §4.16.5, §4.23) and TS 23.548 (§6.3.7).
  AF provides a target DNAI via Nnef_TrafficInfluence > Potential Location of Applications
  PCF provides the list of DNAIs within the PCC rules via Npcf_PolicyAuthorization_Create/Update service. It is clarified in §5.2.5.3.2, §5.2.5.3.3, and §5.2.6.7.2 of TS 23.502 that when only one DNAI is provided as part of list of DNAIs, the presented DNAI is the target DNAI.
§4.3.6.1 of TS 23.502
If the AF interacts with 5GC via the NEF, the NEF performs the following mappings or determinations where needed:
  Map the AF-Service-Identifier into DNN and S-NSSAI combination, determined by local configuration.
  Map the AF-Service-Identifier into a list of DNAI(s) and Routing Profile ID(s) determined by local configuration.
The NEF can only provide this mapping when the DNAI(s) being used by the applications are statically defined. When the DNAI(s) where applications are instantiated may vary dynamically, the AF should provide the target DNAI(s) in its request together with either Routing Profile ID(s) or with N6 traffic routing information.

## Slide 3: Background
For the existing ETSUN scenario (§5.34 of TS 23.501 and §4.23 of TS 23.502), it is already defined that if a certain target DNAI requested by AF/PCC rule is not supported by the inserted I-SMF, the anchor SMF either issues:
  Nsmf_PDUSession_SMContextStatusNotify in order to send the target DNAI to AMF; or
  Nsmf_PDUSession_StatusNotify to I-SMF, and then the I-SMF invokes Nsmf_PDUSession_SMContextStatusNotify to send the target DNAI to AMF
  to trigger AMF to re-select a suitable I-SMF or remove the existing I-SMF depending on the scenarios defined in §5.34.3 of TS 23.501 and §4.23.5.4 of TS 23.502.
When I-SMF based Local Offloading Management applied, how 5GC (i.e., PCF, SMF, AF) handles the AF/PCF-provided target DNAI is not specified .

## Slide 4: Background
In case of Local Offloading Management, if UE is located in the Local Offloading Management service area, then AMF may select and insert an I-SMF.
In one of the proposed CRs (S2-2503404/S2-2503921) in April SA2 meeting, it was proposed that either:
  this I-SMF should be configured e.g. via OAM to be able to support all target DNAIs that would possibly be requested by AFs; or
  if the I-SMF for local offloading management has been selected by the AMF, the I-SMF reallocation is only triggered due to UE mobility, i.e., no SMF triggered I-SMF reallocation.
However, in practice, this is difficult to ensure as certain target DNAI(s) requested by AF may not be supported by already inserted I-SMF.
Moreover, AF-provided target DNAI or SMF-determined target DNAI (based on UE location etc.) being not supported by the anchor SMF was the motivation to introduce ETSUN mechanisms, namely I-SMF insertion/change.
Observation 1: In practice, it is likely that service area of an SMF does not include all target DNAIs.

## Slide 5: Background
In another proposed CR (S2-2502895) in April SA2 meeting, it was proposed that:
  handling of updated PCC rule(s) which may include target DNAI or DNAI(s) for the PDU session is executed same as the respective SMF triggered I-SMF selection or removal defined in clause 4.23.5.4 of TS 23.502.
This proposal was challenged by some companies with the assumption that the UE may have other applications running on the same PDU session to different DNAIs that might be still served by the existing I-SMF.
With this given assumption, these companies indicated that re-selection/removal of the existing I-SMF for only the given target DNAI may impact the user experience on the applications running to remaining DNAIs on the same PDU session.
However, the given assumption is not valid as if there are multiple applications running on the same PDU session towards different DNAIs, the SMF is the entity to decide whether it is required to send the target DNAI to AMF for triggering I-SMF re-selection or removal as defined in step 7 of §4.3.6.2 of TS 23.502.
Observation 2: For a given assumption that UE has multiple applications running on the same PDU session towards different DNAIs, the SMF may decide not to send target DNAI to AMF, hence, I-SMF re-selection/removal may not be triggered for the given assumption.

## Slide 6: Possible cases
Case #1: UE has multiple applications running on the same PDU session
  It is worth to note that Case #1 may be realized with multiple applications running on the same PDU session towards the same DNAI.
Case #2: UE has one application running on the PDU session

## Slide 7: Possible scenarios #1
SMF A
Service Area
SMF B
Service Area
SMF B supports | SMF C supports
DNAI#1 | DNAI#1
DNAI#2 | DNAI#4
DNAI#3 | DNAI#5
SMF C
Service Area
SMF A is selected as the anchor SMF, and SMF B and SMF C are candidate I-SMFs.
Case #1: UE PDU session towards | Case #2: UE PDU session towards
DNAI#1 | DNAI#1
DNAI#2 | 
Case #1: UE PDU session towards | Case #2: UE PDU session towards
DNAI#1->4? | DNAI#4
DNAI#2 | 
AF Traffic Influence with target DNAI
1) AMF has selected SMF B as the I-SMF for LOM.
2) AF has sent DNAI#4 as the target DNAI to change DNAI#1 to DNAI#4
3) SMF behavior on PCC rule update
Case | SMF behavior
Case #1 | SMF identifies that UE has another application running on the PDU session towards different DNAIs. Therefore, SMF decides not to send target DNAI to AMF to not to trigger I-SMF re-selection/removal. Instead SMF triggers failure/notification to AF/PCF.
Case #2 | SMF identifies that the target DNAI is not part of list of supported DNAIs provided by the I-SMF and there is no other application running on the same PDU session. Therefore, SMF decides to send target DNAI to AMF to trigger I-SMF re-selection/removal.
LOM service area

## Slide 8: Possible scenarios #2
SMF A
Service Area
SMF B
Service Area
SMF B supports
DNAI#1
DNAI#2
DNAI#3
SMF A is selected as the anchor SMF, and SMF B is the candidate I-SMF.
Case #1: UE PDU session towards | Case #2: UE PDU session towards
DNAI#1 | DNAI#1
DNAI#2 | 
Case #1: UE PDU session towards | Case #2: UE PDU session towards
DNAI#1->4? | DNAI#4
DNAI#2 | 
AF Traffic Influence with target DNAI
1) AMF has selected SMF B as the I-SMF for LOM.
2) AF has sent DNAI#4 as the target DNAI to change DNAI#1 to DNAI#4
3) SMF behavior on PCC rule update
Case | SMF behavior
Case #1 | SMF identifies that UE has another application running on the PDU session towards different DNAIs. Therefore, SMF decides not to send target DNAI to AMF to not to trigger I-SMF re-selection/removal. Instead SMF triggers failure/notification to AF/PCF.
Case #2 | SMF identifies that the target DNAI is not part of list of supported DNAIs provided by the I-SMF and there is no other application running on the same PDU session. Therefore, SMF decides to send target DNAI to AMF to trigger I-SMF re-selection/removal.
LOM service area

## Slide 9: Possible scenarios #3
SMF A
Service Area
SMF B
Service Area
SMF B supports
DNAI#1
DNAI#2
DNAI#3
SMF A is selected as the anchor SMF, and SMF B is the candidate I-SMF.
Case #1: UE PDU session towards | Case #2: UE PDU session towards
DNAI#1 | DNAI#1
DNAI#2 | 
Case #1: UE PDU session towards | Case #2: UE PDU session towards
DNAI#1->4? | DNAI#4
DNAI#2 | 
AF Traffic Influence with target DNAI
1) AMF has selected SMF B as the I-SMF for LOM but after UE moved out LOM service area, AMF de-activated LOM.
2) AF has sent DNAI#4 as the target DNAI to change DNAI#1 to DNAI#4
3) SMF behavior on PCC rule update
Case | SMF behavior
Case #1 | SMF identifies that UE has another application running on the PDU session towards different DNAIs. Therefore, SMF decides not to send target DNAI to AMF to not to trigger I-SMF re-selection/removal. Instead SMF triggers failure/notification to AF/PCF.
Case #2 | SMF identifies that the target DNAI is not part of list of supported DNAIs provided by the I-SMF and there is no other application running on the same PDU session. Therefore, SMF decides to send target DNAI to AMF to trigger I-SMF re-selection/removal.
LOM service area

## Slide 10: Scenario-related Observations
Observation 3: The anchor SMF is the only entity that can decide whether UE is running multiple applications on the same PDU session towards different DNAIs.
Observation 4: SMF may identify that UE has another application running on the PDU session towards different DNAI(s). Therefore, SMF decides not to send target DNAI to AMF to not to trigger I-SMF re-selection/removal. Instead SMF triggers failure/notification towards PCF/AF.
Observation 5: SMF may identify that the target DNAI is not part of list of supported DNAIs provided by the I-SMF and there is no other application running on the same PDU session. Therefore, SMF decides to send target DNAI to AMF to trigger I-SMF re-selection/removal.
Observation 6: SMF may identify that the target DNAI is not part of list of supported DNAIs provided by the I-SMF and that UE has another application running on the PDU session towards the same DNAI. Therefore, SMF decides to send target DNAI to AMF to trigger I-SMF re-selection/removal.

## Slide 11: SMF sends target DNAI to AMF
AF sends target DNAI
PCF updates PCC rule for the PDU session to indicate target DNAI
SMF determines that the target DNAI is not supported by the I-SMF
I-SMF
0a. AMF has inserted I-SMF for LOM
0b1. Nsmf_PDUSession_Create Request (list of supported DNAIs)
0b2. Nsmf_PDUSession_Create Response (list of DNAIs of interest to PDU Session)
SMF decides list of DNAIs of interest to PDU session and is aware DNAIs supported by the inserted I-SMF
SMF sends target DNAI to AMF
AMF performs I-SMF re-selection or removal

## Slide 12: SMF does not send target DNAI to AMF
AF sends target DNAI
PCF updates PCC rule for the PDU session to indicate target DNAI
SMF determines that the target DNAI is not supported by the I-SMF but there are other applications running towards other DNAIs on this PDU Session that are served by the I-SMF.
I-SMF
0a. AMF has inserted I-SMF for LOM
0b1. Nsmf_PDUSession_Create Request (list of supported DNAIs)
0b2. Nsmf_PDUSession_Create Response (list of DNAIs of interest to PDU Session)
SMF decides list of DNAIs of interest to PDU session and is aware DNAIs supported by the inserted I-SMF
Notification to PCF: SMF sends Npcf_SMPolicyControl_UpdateNotify response with “FAILURE: DNAI_STEERING_ERROR”
Notification to AF: SMF notifies AF with “TRAFF_ROUTE_REQ_OUTCOME” that includes “failedTrafficFlows”
5b. Nsmf_EventExposure_Notif (TRAFF_ROUTE_REQ_OUTCOME)

## Slide 13: Failed enforcement of target DNAI
In clause 4.2.6.2.6.2 of TS 29.512, DNAI_STEERING_ERROR is defined as follows:
In clause 5.6.3.3 of TS 29.508, TRAFF_ROUTE_REQ_OUTCOME is defined in Table 5.6.3.3-1 as follows:
TraffRouteReqOutcome is described as a subscribed event in clause 4.2.2.2 of TS 29.508, and has the following data definition:
If routing of traffic to a local access to a data network policy provided in the "routeToLocs" attribute is invalid, unknown or not applicable, or the enforcement of the steering of the traffic to the indicated DNAI failed, the SMF shall return a PCC Rule Error Report, as specified in clauses 4.2.3.16 and 4.2.4.15, and set the "failureCode" attribute to "DNAI_STEERING_ERROR".
Enumeration value | Description | Applicability
TRAFF_ROUTE_REQ_OUTCOME | Indicates the report of the installation outcome of the requested traffic routing requirements. | TraffRouteReqOutcome
Attribute name | Data type | P | Cardinality | Description | Applicability
succTrafficFlows | array(FlowDescription) | O | 1..N | Contains the descriptor(s) of the IP traffic for which the requested traffic routing requirements were successfully installed. (NOTE 1) | 
succEthTrafficFlows | array(EthFlowDescription) | O | 1..N | Contains the descriptor(s) of Ethernet traffic for which the requested traffic routing requirements were successfully installed. (NOTE 1) | 
failedTrafficFlows | array(FlowDescription) | O | 1..N | Contains the descriptor(s) of IP traffic for which the requested traffic routing requirements failed to be installed. (NOTE 2) | 
failedEthTrafficFlows | array(EthFlowDescription) | O | 1..N | Contains the descriptor(s) of Ethernet traffic for which the requested traffic routing requirements failed to be installed. (NOTE 2) | 
NOTE 1: These attributes are mutually exclusive and only one of them may be present. NOTE 2: These attributes are mutually exclusive and only one of them may be present. |  |  |  |  | 

## Slide 14: Failure/notification Observations
Observation 7: “DNAI_STEERING_ERROR” can be used as it is to inform PCF as it is specified for a case the enforcement of the steering of the traffic to the indicated DNAI failed within the provided Traffic Control Data policy decision to which the PCC rule refers.
Observation 8: “TRAFF_ROUTE_REQ_OUTCOME” together with “failedTrafficFlows” can be used to notify the AF regarding the SMF decision to not to proceed with the given target DNAI as it is defined to support of the subscription to the traffic routing requirements installation outcome event reporting of SMF.

## Slide 15: Observations (summary)
Observation 1: In practice, it is likely that service area of an SMF does not include all target DNAIs.
Observation 2: For a given assumption that UE has multiple applications running on the same PDU session towards different DNAIs, the SMF may decide not to send target DNAI to AMF, hence, I-SMF re-selection/removal may not be triggered for the given assumption.
Observation 3: The anchor SMF is the only entity that can decide whether UE is running multiple applications on the same PDU session towards different DNAIs.
Observation 4: SMF may identify that UE has another application running on the PDU session towards different DNAI. Therefore, SMF decides not to send target DNAI to AMF to not to trigger I-SMF re-selection/removal. Instead SMF triggers failure towards PCF/AF.
Observation 5: SMF may identify that the target DNAI is not part of list of supported DNAIs provided by the I-SMF and there is no other application running on the same PDU session. Therefore, SMF decides to send target DNAI to AMF to trigger I-SMF re-selection/removal.
Observation 6: SMF may identify that the target DNAI is not part of list of supported DNAIs provided by the I-SMF and that UE has another application running on the PDU session towards the same DNAI. Therefore, SMF decides to send target DNAI to AMF to trigger I-SMF re-selection/removal.
Observation 7: “DNAI_STEERING_ERROR” can be used as it is to inform PCF as it is specified for a case the enforcement of the steering of the traffic to the indicated DNAI failed within the provided Traffic Control Data policy decision to which the PCC rule refers.
Observation 8: “TRAFF_ROUTE_REQ_OUTCOME” together with “failedTrafficFlows” can be used to notify the AF regarding the SMF decision to not to proceed with the given target DNAI as it is defined to support of the subscription to the traffic routing requirements installation outcome event reporting of SMF.

## Slide 16: Proposal
Proposal 1: SMF-triggered I-SMF insertion/change/removal was defined as part of ETSUN. The procedures that are introduced to enable I-SMF based Local Offloading Management should not interfere with the existing procedures.
Proposal 2: Define SMF-triggered I-SMF insertion/change/removal for Local Offloading Management scenario in TS 23.548 as proposed in S2-250xxxx.
Proposal 3: Include a note in TS 23.502 and TS 23.501 on handling AF Traffic Influence to clarify that SMF takes into account whether I-SMF is inserted for Local Offloading Management to decide on sending/not sending the target DNAI provided by AF (via PCF, PCC rules) as in S2-250yyyy and S2-250zzzz, respectively.
Proposal 4: When SMF decides not to proceed with the given target DNAI in PCC rule due to I-SMF based Local Offloading Management, SMF may notify PCF as part of Npcf_SMPolicyControl_UpdateNotify Response including failure as “DNAI_STEERING_ERROR”. If needed, further confirmation from Stage 3 can be requested.