## Slide 1: Discussion on IP vs. Non-IP
ZTE
(RoHC) (reduced RTP)
3GPP TSG SA WG2#170
Stor-Göteborg, Sweden, Aug 25 – 29, 2025
S2-2507102

## Slide 2: IP with RoHC
In SA2#169, several assumptions regarding IP/UDP/RTP header with RoHC are outlined in document S2-2504678:
Assumption 1.1: In RoHC SO state, the packet type is type 2 (UOR-2) ⇒ 3B
Assumption 1.2: At the transition from silence periods to talk spurts, the compressor sends UOR-2EXT packets⇒ 10-12B
However, according to field log, we have the following observations:
Observation 1.1: In RoHC SO state, the packet type used can be Type 0 (UO-0) with UDP checksum disabled⇒ 1B
  Note: This is based on field log from GEO voice scenarios, where, under extremely limited channel resources, it is possible to select the packet format with the smallest header overhead.
Observation 1.2: At the transition from silence periods to talk spurts, the compressor switches from UO-0 to UO-1⇒ 2B
  Note: Talk and silent packets share the same SN space (incremented by 1 per packet) but use different TS_STRIDE values (e.g., 20 ms vs. 160 ms). The UO-1 format can represent this TS_STRIDE change to the decompressor. Therefore, UO-1 is sufficient and UOR-2EXT is unnecessary.
Header Length Clarification
Observation1.3: For GEO voice scenario, RoHC can achieve a 1B header(instead of 3B), with only 1B(instead of 7-9B) during talk-to-silence transitions.

## Slide 3: IP with RoHC
In SA2#169 , 4 issues about RoHC are proposed in document S2-2504678:
Observation2: RoHC issues are either minor or can be mitigated by implementation (e.g., sending silence frames in advance, applying UO-0/UO-1 format).
issue | description | Observation/analysis
call setup delay | Under worst-case assumptions (1 kbps, 80 ms ptime, 60B IR header), each initial IR packet introduces ~500 ms delay, potentially causing 6–7 voice packets to be lost. | Logs show only two IR packets sent, at an average-case assumption(2 kbps, 160 ms ptime (per SA4 emulation)) → the total delay is ~500 ms, resulting in only 3 lost voice packets. If even this loss is unacceptable, it can be mitigated by transmitting silence frames before the 200 OK response (INVITE), ensuring no or less voice packet loss.
call interruptions | Packet loss or decompression errors can force the compressor back to IR state, causing voice interruptions. | Based on our analysis, the probability of losing enough consecutive packets (around 16) to cause one time decompression failure is negligible.
over/under scheduling | Packet header size may increase: 3 B → 10–12 B during talk-to-silence transitions (UOR-2 → UOR-2-EXT) 3 B →20–30 B after NACK, due to fallback to IR-DYN Such abrupt jumps may cause resource over-scheduling or under-scheduling. | Logs show packet header increases only : 1 B → 2 B during talk-to-silence transitions (UO-0 → UO-1) (see details in page 2) The likelihood of receiving a NACK is theoretically very low. Both IP and non-IP bearers show consistent deltas between SID and voice packet sizes(unless the new ULBC talk packet size is the same as silent packet size).
ROHC overhead bit rate | Assumes 3 × (10–12B) packet size per transition → increases ROHC overhead from 300 bps to 540 bps. | Actual headers can be much smaller: 1 B (steady state), 2 B (after fallback) → 540 bps estimate is significantly overstated. (see details in page 2)
RoHC Issues Clarification

## Slide 4
In SA2#169, one assumption regarding reduced RTP header are outlined in solution3,5 of TR23.700-19:
Assumption3: the non-IP (reduced RTP) header only include short RTP SN ⇒ 1B
However, many aspects are overlooked, for example:
  if DTMF needs to be supported, extra 1 B (PayloadType) field may be added ⇒ 1 + 1 == 2 B
  if Multi-Call or FEC (Forward Error Correction) need to be supported, extra 4 B (SSRC) field may be added ⇒ 2 + 4 == 6 B
  if JBM (Jitter Buffer Mgmt) needs to be supported, extra 4 B (TimeStamp) field may be added ⇒ 6 + 4 == 10 B
  Additionally, SRTP (Secure RTP) cannot be supported, even if we want to support
  maybe more features will be found later….
Functionality wanted to be supported by non-IP (reduced RTP) | In order delivery | DTMF | MULTI-CALL/FEC | JBM | Encryption | Integrity protection | …
Cost | 1 octet (SN) | 1 octet (PayloadType) | 4 octets (SSRC) | 4 octets (TimeStamp) | Can’t support | Can’t support | 
Total Overhead | 1 octet | 1 + 1 == 2 octets | 2 + 4 == 6 octets | 6 + 4 == 10 octets | Infinite | Infinite | 
Observation3.1: In our view, at a minimum, DTMF support is essential for GEO voice, which already brings the non-IP (reduced RTP) overhead to 2B—comparable to RoHC (1–2 B).
Observation3.2: Furthermore, the strong dependencies on SA1, SA3, and SA4 make it unlikely that the non-IP solution can be completed within the Rel-20 timeline.
Non-IP (reduced RTP)
Header Length Clarification

## Slide 5
Given that IMS is an IP-based architecture, and satellite-access UE may need to communicate with legacy UE, the PGW or other network functions are required to reconstruct the reduced RTP headers into complete IP/UDP/RTP headers before forwarding them to IMS components.
However, several aspects of this mechanism, which may significantly affect the system, remain insufficiently discussed and evaluated.
These include, but are not limited to, the following concerns:
  concern1: UE may need to remove or insert specific fields in the IP, UDP, and RTP headers, which could require modifications to the modem/application.
  concern2: P-GW may need to remove or insert specific fields in the IP, UDP, and RTP headers, which could require modifications to the user plane processing module/protocol stack.
  concern3: P-CSCF may need to provide extra header information to P-GW, which could result in increased signaling load or necessitate interface enhancements.
  concern4: Without transmitting the RTP timestamp, it is not possible to accurately reconstruct it on the receiver side, which may affect media synchronization and playback quality.
  There may be additional aspects that have not yet been identified or listed.
Observation4: The feasibility and potential impact of sending non-IP voice packets require thorough evaluation and alignment among relevant working groups, given that it is considerably more complex than the IP-based solution.
Non-IP (reduced RTP)
Concerns in Reconstructing Full IP/UDP/RTP Packet

## Slide 6: Conclusion and proposal
Compared to Non-IP(Reduced RTP), The IP (RoHC) approach :
  achieves comparable or lower overhead (1–2 bytes)
  is significantly more future-proof(can support DTMF, MULTI-CALL/FEC, JBM, etc.)
  has fewer dependencies on SA1, SA3, and SA4
  requires fewer modifications to existing system
  and any issues with RoHC are minor or can be effectively addressed by implementation
Conclusion
Proposal
For IMS voice, it is proposed to tentatively reach consensus on selecting IP (with RoHC) at SA2#170.