## Slide 1: Handling IMS congestion from UEs in Connected Mode (LS from RAN2)
NTT DOCOMO
KDDI
SoftBank Mobile Corp.
S2-131767
TSG SA WG2 #97
Busan, Korea, 27-31 May 2013

## Slide 2: Introduction
RAN2 has sent LS (S2-130006) to SA2
  http://www.3gpp.org/ftp/tsg_sa/WG2_Arch/TSGS2_95_Prague/Docs/S2-130006.zip
Asks IMS (UNI) overload from UEs in connected mode needs any solution.
  SA1 created new set of requirements (PMOC)
This paper discusses the scenarios and solutions

## Slide 3: Questions from RAN2
Are there any requirements due to the fact that UEs stay in connected mode more often nowadays that may be taken into account with respect to access control mechanisms?
Is there already any CN based mechanism developed to solve especially the above problems (above (1) and (2)) discussed in this LS e.g. in case of disaster scenario which may cause signalling overload to IMS system?
SA2 hasn’t responded to these two questions yet.

## Slide 4: Status
SA2 haven’t responded this RAN2
SA1 have done their work (Rel-12 PMOC)
CT1 have sent us LS saying they’ll wait for further update from SA1.
It’s the right time SA2 looks at this issue.

## Slide 5: Problem described in RAN2 LS (S2-130006)
*Diagram is based on a record taken in a NTT DOCOMO RNC in Tohoku area
But similar behaviour was also observed in other areas in Japan e.g. Tokyo
CS Call attempt
Goes up to 60+ times
Earthquake at 14:46
Estimated CS Voice Call Attempt per Hour* on 11 March 2011
Expected NW capacity

## Slide 6: Current solution (for IMS)
SSAC (Service Specific Access Control)
  Only works in Idle mode.
  UEs in idle mode (when barring is enforced) do not send INVITE messages.
P-CSCF
PGW
SGW
MME
eNB
PCRF
BCCH (SIB2):
MMTel Barring
Rate

## Slide 7
UE: in RRC-Connected Mode
  i.e. SRB/DRB/EPS Bearers exist already for each UE.
  No NAS/GTP/PMIP/Diameter signalling involved
Creating DoS effect on P-CSCF
No congestion within a RAN U-Plane bearer is expected.
  Bearer resources are already allocated
  SIP INVITE doesn’t consume much bandwidth
  This is different from UPCON scenarios
P-CSCF
PGW
SGW
MME
eNB
INVITE of DEATH!
PCRF
Problem described in RAN2 LS (cont’d)

## Slide 8: The Requirements
Regulatory requirements
  Emergency call / priority call must not fail
    Includes Non-UE detectable emergency calls
Operator requirements
  Allow space for normal calls
    Very strong regulatory pressure on providing voice services as much as possible, which can save lives.
  Service shutdown must be avoided
    Solution with extra processing power / extra signalling in the RN/CN/IMS is NOT wanted!
      These can make the situation even worse

## Slide 9: The Requirements – cont’d
“Fair” barring
  Everybody gets fair chance of successful call setup
For example…. 80% barring rate
time
OK
OK
OK
OK
OK
OK
“Fair Barring”
Unfair barring  NOT THIS!

## Slide 10: The Requirements – cont’d
User Experience
  User is notified of being barred
  Same user experience is needed, when operator proactively bar call attempts.
            In other words, UE must know if the call is being barred / rejected.

## Slide 11: Proposal: SSAC in Connected Mode
MMTEL app
UE - RRC
RAN
BCCH
SSAC barring rate (existing)
Press “call”
Query
Return barring rate
SSAC enforcement
Return SSAC barring rate
regardless of RRC state
(In R9 only when idle mode)
No SA2/CT1 impact foreseen. Only one small CR in 36.331 required.

## Slide 12: Solutions – what else?
Existing Solutions?
IOC (IMS Overload Control)
SIP Reject (with Backoff timer)
QoS modification / PCC gating
Analysis:
Require a lot of processing, which doesn’t quite fit the earthquake/terrorist attack voice call burst scenarios.
The MMTel Call originations must gated in the RAN itself.

## Slide 13: Conclusion
  Solutions to stop voice call attempt using ACB.
  For CSFB/SSAC ACBs:
No SA2 specification impact foreseen
Reply LS to RAN2 to progress the work
  It’s business critical for the success of (Vo)LTE.