## Slide 1: Advanced Media Delivery
Thomas Stockhammer, Qualcomm Incorporated
Support from Jason Cloud, Frederic Gabin (Dolby) and Richard Bradbury (BBC)
October 17, 2025
5G-MAG Workshop: Release 19 - ready for implementation

## Slide 2
Introduction
Advanced Media Delivery – 5GMS
Common Media Client Data (CMCD)
Multi-access media delivery
Media delivery from multiple service endpoints/locations, including CMMF and Content Steering
Distributing DRM-encrypted and high-value content
Improved QoS support for Media Streaming services including ECN marking for L4S and QoS monitoring
Media Streaming aspects of Network Slicing
Advanced Media Delivery – MBS/MBMS-5GB
In-session unicast repair for MBS Object Distribution
Time Synchronization
Outlook Rel-20

## Slide 3: Selected Technologies for Media Services
Codecs and Formats
Content Delivery Protocols
Access and Distribution Technologies
Security, Content Protection and Provenance
Rendering and Presentation
Quality-of Service and Quality-of-Experience
Data collection and Intelligence
3GPP is addressing the issue to profile technologies for 3GPP Services and Media Service Enablers

## Slide 4: Rel-19 Advanced Media Delivery
Advanced Media Delivery
Common Client Metadata.
Common Server-and Network-Assisted Streaming.
Multi-Access Media Delivery.
Media Delivery from multiple service endpoints/location.
Modem Usage Optimized Media Streaming.
DASH/HLS Interoperability.
Further harmonization of RTC and Streaming for Advanced Media Delivery.
Improved QoS support for Media Streaming services.
QUIC-based segmented media delivery.
In-band signalling of QoS for 5G Media Streaming.
Dynamic content generation from multiple sources.
In-session Unicast Repair for MBS Object Distribution.
MBS User Service and Delivery Protocols for eMBMS.
Time Synchronization for MBS
Combined Unicast/Broadcast
FS_AMD
Study completed in Dec ‘25 (stage 2) and Mar ‘25
Identified normative work
AMD-ARCH-MED
Stage-2 work for Streaming and MBS/MBMS
Completed also in Mar 25
AMD_PRO-MED
Stage-3 Protocol work in SA4 and CT3/4
Completed Sep 25, open API Dec 25
Identified more study topics for future Releases
Enhance 5GMS and Broadcast to be fit for purpose for and benefit from modern streaming technologies

## Slide 7: Stage-2 Topics and CRs
Topic | Title | Lead | Latest Document and Status | Related spec and CR number | Clause in spec | Completion
1 | Common Client Metadata | Thomas Stockhammer, Qualcomm | S4aI250061 (n) | 26501-0101rev3 |  | 100%
2 | Media delivery from multiple service endpoints/locations | Jason Cloud, Dolby | S4aI250062 (e) | 26501-0103rev3 |  | 100%
3 | Multi-Access Media Delivery | Prakash Kolan, Samsung | S4aI250036 (e) | 26501-0107rev1 |  | 100%
4 | Distributing encrypted and high-value content | Thomas Stockhammer, Qualcomm | S4aI250062 (n) | 26501-0102rev3 |  | 100%
5 | In-session Unicast Repair for MBS Object Distribution | Thomas Stockhammer, Qualcomm | S4aI250068 (e) | 26502-0033rev4 |  | 100%
6 | MBS User Service and Delivery Protocols for eMBMS | Thomas Stockhammer, Qualcomm | S4aI250040 (e) | 26502-0034rev2 |  | 100%
7 | Selected MBMS Functionalities not supported in MBS | Thomas Stockhammer, Qualcomm | S4aI250057 (n) | 26502-0035rev2 |  | 100%
8 | Improved QoS support for Media Streaming services | Qi Pan, Huawei | S4aI250042 (e) | 26501-0104rev1 |  | 100%
9 | Media Streaming aspects of Network Slicing | Prakash Kolan, Samsung | S4-242016 (e) | 26501-0098rev2 | 2, 4.0.6, 5.8.1, 6.9.6, Annex X, Annex Y | 100%
All technologies are now integrated in the Rel—19 versions of TS 26.501 and TS 26.502

## Slide 8: Stage-3 Topics and CRs
Topic | ST | Title | Lead | Latest Document and Status | Related spec and CR number | Completion | Impact other WGs | 3GPP Forge branch name
1 | a | Common Media Client Data | Richard Bradbury, BBC | S4-251463(a) | 26510-0021r5 | 95% | None | cmcd
1 | b | Common Media Client Data | Richard Bradbury, BBC | S4aI250146(a) | 26512-0089r3 | 95% | None | cmcd
2 | a | Media delivery from multiple service endpoints/locations - General | Jason Cloud, Dolby | S4aI250158(a) | 26510-0016r7 | 95% | None | multi_service_location
2 | b | Media delivery from multiple service endpoints/locations - General | Jason Cloud, Dolby | S4aI250159(a) | 26512-0086r7 | 95% | None | multi_service_location
2 | c | Media delivery from multiple service endpoints/locations - CMMF | Jason Cloud, Dolby | S4aI250160(a) | 26512-0091r6 | 100% | None | N/A
2 | d | Media delivery from multiple service endpoints/locations - Content Steering | Thomas Stockhammer, Qualcomm | S4aI250171(a) | 26512-0099r2 | 100% | None | N/A
3 | a | Multi-Access Media Delivery | Prakash Kolan, Samsung | S4aI250150(a) | 26512-0087r8 | 95% |  | multiaccess
4 | b | DASH Instantiation and DRM Protocol Support | Thomas Stockhammer, Qualcomm | S4-251507(a) | 26512-0093r3 | 100% |  | N/A
4 | c | Distributing encrypted and high-value content | Thomas Stockhammer, Qualcomm | S4-250988 (e) | 26511-0015 | 100% |  | N/A
5 | a | In-session Unicast Repair for MBMS Object Distribution | Thomas Stockhammer, Qualcomm | S4aI250148(a) | 26346-0677r4 | 95% | None | in-session-repair
5 | b | In-session Unicast Repair for MBS Object Distribution | Thomas Stockhammer, Qualcomm | S4aI250149(a) | 26517-0031r3 | 95% | None | in-session-repair
7 | a | Time Synchronization | Thomas Stockhammer, Qualcomm | S4-251511(a) | 26517-0028r5 | 95% | CT3's TS 29.580. Bump up version of Nmbsf provisioning API | time-service-endpoints
8 | a | Improved QoS support for Media Streaming services | Qi Pan, Huawei | S4-251552(a) | 26510-0020r7 | 95% |  | AMD-PRO-MED-QoS
8 | b | Improved QoS support for Media Streaming services | Qi Pan, Huawei | S4-251485(a) | 26512-0090r3 | 100% |  | N/A
9 | a | Media Streaming aspects of Network Slicing | Prakash Kolan, Samsung | S4-251486(a) | 26510-0008r6 | 95% |  | slicing
All technologies are now integrated in the Rel—19 versions of TS 26.510, TS 26.512, TS 26.346 and TS 26.517

## Slide 9: 5G Media Streaming

## Slide 10: Rel-16 5G Media Streaming – The Idea
Collaboration of MNOs and Media Service Providers
Approach:
  Framework aligned with today‘s OTTmedia distribution practices
  Supplementing MNO and third-party media services to easily access 5GS and 5GMS features
  Concrete instantiation for subset of recommended technologies (e.g. codecs, formats, etc.)

## Slide 11
5G Content Provider UK
5G UE in China
5GMS-aware Application
Media Session Handler
Media Player
5GMS AS
5GMS AF
Select BBC
Access: http://5gms.bbc.uk/3gpp-m5/v2/service-access-information/d54a1fcc-d411-4e32-807b-2c60dbaeaf5f
JSON Response
{
"provisioningSessionId": "d54a1fcc-d411-4e32-807b-2c60dbaeaf5f",
"provisioningSessionType": "DOWNLINK",
"streamingAccess": {
"mediaPlayerEntry": "http://5gms.bbc.uk/m4d/provisioning-session-d54a1fcc-d411-4e32-807b-
2c60dbaeaf5f/Christmas-Greetings-to-5G-MAG.mpd"
}
}
Play BBC
GET X-MAS MPD
MPD Response
Notes: Hello, my name is Weiyu from Qualcomm China. I explain you the first handshake we did just a few days ago with the BBC 5GMS Network components you saw earlier.
We implemented initial functions of Media Session Handler and Media Player.
Here is our test app. Let us check the BBC Christmas Greetings.
[Click]
We send a 5GMS RESTful API call to the AF and get a 5G conforming JSON response.
The Media Session Handler instructs the media player to play the video and the Media Player gets the MPD from the AS.
[Click]

## Slide 12
5G Content Provider UK
5G UE in China
5GMS-aware Application
Media Session Handler
Media Player
5GMS AS
5GMS AF
MPD Response
<?xml version="1.0" ?>
<!-- MPD file BBC Christmas Greetings -->
<MPD xmlns="urn:mpeg:dash:schema:mpd:2011" minBufferTime="PT2S" type="static" mediaPresentationDuration="PT0H0M30S" maxSegmentDuration="PT0H0M2S" profiles="urn:mpeg:dash:profile:isoff-live:2011 ">
<Period duration="PT0H0M30.000S">
<AdaptationSet segmentAlignment="true" maxWidth="1920" maxHeight="1080" maxFrameRate="25" par="16:9" lang="und" startWithSAP="1" contentType="video" containerProfiles="'cmf2', 'cfhd'">
<SegmentTemplate media="1/$Time$.m4s" initialization="1/init.mp4" timescale="12800">
<SegmentTimeline>
<S t="0" d="25600" r="14"/>
</SegmentTimeline>
</SegmentTemplate>
<Representation id="1" mimeType="video/mp4" codecs="avc1.640028" width="1920" height="1080" frameRate="25" sar="1:1" bandwidth="5100000">
</Representation>
</AdaptationSet>
</Period>
</MPD>
GET X-MAS Segments
Segment Response
Monitor and Support
Notes: So let‘s unpack our Christmas present.
[Click]
We got a voucher for some Segments and we request those while 5GMS Control functions monitor the session.
[wait until the end of Richard‘s message]
Thank you Richard
[END]

## Slide 13: 5G Media Streaming Features
Primarily downlink features
Content Hosting
Network Assistance
Dynamic Policies
Consumption Reporting
Metrics Reporting
Data collection, reporting and exposure
Service URLs

## Slide 14: Topic #1: Common Client Metadata

## Slide 15: What is CMCD?
A defined set of structured key/value pairs communicating mutually beneficial media-related information from a player to a CDN via either
  A set of custom headers
  A query arg
  A JSON object
Common because the same data structure can be used across all players and all CDNs.
Resources
  Available for free at https://tinyurl.com/cta5004spec
  DASH-IF Special Session available from Will Law
Lot of discussion during MWS on version 2

## Slide 16: Selected Use Cases in 5G Media Streaming
The use cases which CMCD enables are broad – including robust pre-fetching of content, analytics solutions, forensic debugging, CDN delivery optimisation, alerting and monitoring systems, low latency optimisations, server-side switching, research analytics and content steering decision-making.
In the context of 5G Media Streaming, the CMCD information may be used for several purposes that are elaborated further in the remainder of this clause:
1) Operational optimisation of the 5GMSd AS: The Application Server uses CMCD information to optimise its operation. For example, the 5GMSd AS may choose to pre-fetch content from the 5GMSd Application Provider based on the value of the CMCD Next object request key signalled by the Media Player.
2) Operational optimisation of the 5GMSd AF and 5G Media Streaming: The Application Function uses CMCD information in order to configure the 5G System for optimised media delivery across the User Plane. For example, the 5GMSd AF may invoke service operations on the PCF in order to effect a delivery boost if the CMCD Buffer starvation flag is set by the Media Player.
3) UE data collection on media playback and 5GMS reception, reporting and event exposure by 5GMS System: The Application Function uses the data collection and reporting framework to provide CMCD information to the 5G System or to external 5GMS Application Providers. This could, for example, take the form of a time series event log for audit purposes. Such data could, for example, be useful to determine the quality of reception and to identify anomalies or errors that can occur on players.
Based on clause 5.16.

## Slide 17
Option 3: Out-of-band reporting of CMCD information at M11d and M5d
Option 1: In-band reporting of CMCD information via reference point M4d and M3d
The preferred solution is Option 1 "In-band reporting of CMCD information via reference points M4d and M3d", for the following reasons:
- In-band reporting reference point M4d is broadly implemented in common media clients nowadays.
- In-band reporting permits operational optimizations by the 5GMSd AS, which is not the case with Option 3 Out-of-band reporting of CMCD information via reference points M11d and M5d. Solely on the basis of this issue, Option 1 and Option 2 would remain valid candidates.
- Passing the CMCD information to the 5GMS AF at reference point M3d (Option 1) permits operational optimisations by the 5GMSd AF, which is not the case with Option 2 In-band reporting of CMCD information via reference points M5d and R4 where the CMCD information is handed directly to the Data Collection AF instantiated in the 5GMS AF, but is not visible to the latter.
All envisaged use cases can be supported by Option 1.
We may revisit this decision after the availability if v2 of CMCD

## Slide 18: Stage-3 Support
Combined with metrics reporting, but now referred to as in-band client data
In-band client reporting on M4 defined in TS 26.512, 10.5, for example
  Media Player shall include in every CMCD report the current media delivery session identifier in the sessionId property and content identifier of the media streaming asset being consumed in the contentId property of the MetricsSession
Client data reporting on M3 in TS 26.512, 11.4.3
  The syntax and MIME media type of metrics reports conveying client data to the 5GMSd AF shall comply with the JSON-based metrics reporting envelope specified in clause 9.5.3.2 of TS 26.510.
Configuration of Reporting via Service URL in TS 26.512, 12.4
Configurations and settings API for Media Player via M7d and M11d in clause 13.2.4 of TS 26.512
Event exposure on R5/R6 defined in clause 18.3.3 of TS 26.512
Inband client reporting in DASH, defined in TS 26.512, Annex G.5
  DASH content offering requirements and recommendations
  Media Player requirements and recommendations
Summarized in S4-251463 (26.510) and S4aI250146 (26.512)

## Slide 19: Implementation into 5G-MAG reference tools
In-band client reporting on M4 defined in TS 26.512, 10.5
  Small work for media clients that already support CMCD.
Client data reporting on M3 in TS 26.512, 11.4.3
  Some work as it requires to define M3 API
Configuration of Reporting via Service URL in TS 26.512, 12.4
  Some work as it requires updates for generation and processing
Configurations and settings API for Media Player via M7d and M11d in clause 13.2.4 of TS 26.512
  Small work for media clients that already support CMCD.
Event exposure on R5/R6 defined in clause 18.3.3 of TS 26.512
  Some work as it requires to create the report
Inband client reporting in DASH, defined in TS 26.512, Annex G.5
  Small work for media clients that already support CMCD.

## Slide 20: Topic #2: Multi-CDN (Service Location) Media Delivery

## Slide 21: Media Delivery from Multiple Service Locations
5GMS network provisioning and configuration extensions and APIs to:
Provision and expose multiple 5GMS AS service locations at reference point M4
Content Preparation to create/update Media Entry Points and/or prepare ingested media for delivery from multiple service locations (e.g., CMMF encoding)
5GMS AS service chaining at reference point M10

## Slide 22: Media Delivery from Multiple Service Locations
Media Entry Point (e.g., MPD, CMMF EFDT, MPD + CMMF EFDT, etc.) instantiated multiple service location delivery, i.e., information provided to 5GMS Clients via the Media Entry Point may include:
Service location URLs
Content Steering Information
CMMF Configuration Information
5GMS Client capabilities to support:
Service location switching (DASH client-side switching, Content Steering, SAND4M)
Concurrent use of multiple service locations using CMMF

## Slide 23: Multi-Service Location
M13d
Multi-CDN Client
Multi-CDN Technologies
DNS-based switching
MPEG-DASH client-side switching
Content steering driven switching
SAND4M-based switching
CMMF-based multi-source delivery

## Slide 24: Multi-Service Location – 5GMS AS/MNO offers several locations
CDN/Service Location 1
CDN/Service Location 2
Multi-CDN Processor
Multi-CDN Client
M13d
Locations differ by dynamic policies, slices, 3GPP access networks, etc.

## Slide 25: Multi-Service Location – 5GMS AS/MNO is one of several locations
CDN/Service Location 1
CDN/Service Location 2
Multi-CDN Processor
Multi-CDN Client
M13d
Locations differ by access networks or other type of business decisions

## Slide 26
Coded Multi-Source Media Format (CMMF) ETSI TS 103 973
CMMF is a media delivery standard format that enables simultaneous streaming from multiple sources (e.g., CDNs) using coded media segments. It improves reliability, reduces latency, and enhances playback quality over single-source or multi-CDN switching.
Integrated into 3GPP Release 19 for 5G Media Streaming (5GMS) Multi-service locations.
Media segments are encoded into redundant coded symbols using e.g. AL-FEC RaptorQ.
These symbols are distributed across multiple CDNs.
The player downloads any subset of symbols sufficient to reconstruct the original segment - no need to orchestrate / know which CDN will respond fastest.

## Slide 27: Stage-3 Support
Procedures for service chaining M10d and external interfaces M13d
General summary in TS 26.510, clause 10.3A, including 3 variants
  switching between multiple service locations during content distribution
  concurrent use of multiple service locations for content distribution
  support content steering for content distribution
DASH content distribution using multiple service locations, Annex G.4 of TS 26.512
  Content Preparation requirements to support multiple service locations
  Content Authoring and client requirements for
    client-side switching
    Content Steering for DASH (Reference to ETSI TS 103 998)
    SAND for Multi-network access mode (SAND4M) (Reference to 3GPP TS 26.247 and ISO/IEC 23009-5)
Media streaming in the 5GMS System using CMMF, Annex H of TS 26.512
  Procedures for downlink media streaming from multiple service locations using CMMF
  Protocols and formats for downlink media streaming using CMMF with reference to ETSI TS 103 973
  Many examples and informative implementation guidelines
Summarized in S4aI250158 (26.510) and S4aI250159, S4aI250160, S4aI250171(26.512)

## Slide 28: Stage-3 Implementation

## Slide 29: Topic #3:Multi-Access Media Delivery
Stage-2 S4aI250036  Informative Annex to TS 26.501, Annex F
Stage-3 S4aI250150

## Slide 30: Stage-2 Summary of Annex F
UEs connected to multiple access networks (whether they be a 3GPP access network or non-3GPP access network, multiple disjoint 3GPP networks, etc.) may deploy and utilise multi-access techniques using any of the following:
  The use of a multipath transport protocols such as MPTCP [RFC6897] or MPQUIC [MPQUIC] is one approach to enable multi-access media delivery. This approach requires implementation of the protocol(s) on both the UE and on the Application Server.
  Another method to enable multi-access media delivery is to use an application layer approach whereby a suitable object coding protocol is employed to enable efficient simultaneous use of the available access networks. The benefit of this approach is that the Application Server can remain agnostic of the UEs’ use of multiple access networks.
  The use of lower-layer network support using ATSSS (Access Traffic Steering, Switching, and Splitting) an optional feature for multi-access supported by the UE and 5G Core network and described in TS 23.501 [2]. The ATSSS feature enables a Multi-Access PDU Connectivity Service allowing for the exchange of PDUs between the UE and a Data Network by simultaneously using one or more 3GPP access networks and/or non-3GPP access networks.

## Slide 31: Stage-3 Extensions
Updates to procedures in clause 4.9 of TS 26.512
  The 5GMSd-Aware Application and the Media Session Handler may configure content delivery for downlink media streaming between the 5GMSd AS and the Media Player using the client API at reference points M7d and M11d respectively by populating the desiredContentDeliveryConfiguration object in the Media Player configuration as specified in clause 13.2.4.
    A list of content delivery protocols (see table 13.2.4 3) to be used at reference point M4d may be provided in order of preference.
    A preference for using a multipath transport protocol at reference point M4d may be expressed
Equivalent work for uplink streaming in clause 5.6 and 5.9
Extension of Service URL to configure multi-access in clause 12.4
Extensions to configuration and settings API in 13.2.4 to add
  Capabilities: A read-only list of Media Player capabilities.
  desiredContentDeliveryConfiguration: Desired configuration of content delivery at reference point M4d
  Adding error and status codes, as well as configuration parameters for multi-path
Stage-3 S4aI250150

## Slide 32: Implementation Efforts

## Slide 33: Topic #4:Distributing encrypted and high-value content

## Slide 34: Stage-2
Addresses the case that the content is prepared in the AS for encrypted distribution
The detailed steps for the workflow are presented
See clause 5.14 of TS 26.501

## Slide 35: Stage-3
Key exchange for encrypted content in clause 8.8 of TS 26.512
  In order to support exchange of public keys between the Encryptor/Packager on the 5GMSd AS and the external License Server and Authorization Server via reference point M2d, the 5GMSd AS shall support the Content Protection Information Exchange Format (CPIX) as specified in ETSI TS 103 799 at reference point M2d
Content Protection and DRM in DASH
  DASH content encoding requirements according to DASH-IF-IOP-6
  Media Player requirements and recommendations according to DASH-IF-IOP-6
  Content Preparation Template requirements
S4-251507

## Slide 36: 5G-MAG Reference Tool Implementation

## Slide 37: Topic #5:Improved QoS support for Media Streaming services

## Slide 38: Stage-2
5.7.9 ECN marking for L4S for downlink media streaming based on Dynamic Policy
6.9.8 Dynamic Policy of ECN marking for L4S for uplink media streaming
6.9.9 QoS monitoring of uplink media streaming based on Dynamic Policy
See TS 26.501

## Slide 39: Stage-3
5.2.7.1 General Procedure updates
  When a Policy Template prefers ECN marking for L4S functionality to be enabled according to RFC 9330 [X1], RFC 9331 [X2] and RFC 9332 [X3], the l4SEnablementPreference property shall be present and set to true. The Media AF shall reject the Policy Template if the Media AS does not support ECN marking for L4S functionality.
  When a Policy Template prefers QoS monitoring functionality to be enabled, the qoSMonitoringConfiguration property shall be populated with a QosMonitoringInformation object as specified in clause 5.14.2.1.6 of TS 29.122 [20].
5.4.3 Dynamic Policy invocation
  If the Media Access Function supports an L4S protocol stack, it shall subscribe to receive notifications from the Media Session Handler at reference point M11 concerning successful instantiation of Policy Templates that have ECN marking for L4S functionality enabled.
  If the Media Access Function is capable of consuming QoS monitoring results, it shall subscribe to receive notifications from the Media Session Handler at reference point M11 concerning successful instantiation of Policy Templates that have QoS monitoring enabled.
S4-251552

## Slide 40: 5G-MAG Reference Tool Implementation

## Slide 41: Topic #6:Media Streaming aspects of Network Slicing
Stage-2: S4-242016
Stage-3: S4-251486

## Slide 42: 5G-MAG Implementation

## Slide 43: Topic #7: In-session Unicast Repair for MBS/MBMS Object Distribution
Stage-2: S4aI250068
Stage-3: S4aI250149 (MBS), S4aI250148 (MBMS)

## Slide 44: Stage-2
For live and low-latency live services using the Object Distribution Method in MBS, in certain cases the transmission of an object is not successful. In this case, unicast repair for individual MBS Clients can improve the service quality. However, the timing of such requests needs to be carefully studied in order to avoid network overloads or significant latencies in the delivery. In TR 26.802, In-session unicast repair for MBS Object Distribution as introduced in clause 5.9 and based on the conclusions in clause has been motivated.
Added new reference point MBS-12
Extended 5.3 Procedures for User Service provisioning
Document call flows and procedures for both post-session and in-session unicast repair

## Slide 45: Stage-3
In-session repair signaling on session
  Repair-Start: the earliest date–time at which unicast repair may be started for the file object described by the FDT Instance.
  Repair-Limit-Percentage: the maximum number of unicast repairs that the MBMS Client may attempt over the last 100 objects received on this session.
  And other parameters (URLs, etc.)
In-Session object Repair procedures
  Parameters, general procedures
  Determination of non-completion
  Request prototocols
In-Session object Repair Protocol
  Mapping to MBSTF Client and MBS AS
Extend FDT – properties per object
  Repair-Start: the earliest date–time at which unicast repair may be started for the file object described by the FDT Instance.
  Repair-Limit-Percentage: the maximum number of unicast repairs that the MBMS Client may attempt over the last 100 objects received on this session.
Multiple objects transport indication in SDP
  Object sequence number rule (increment by 1)
  Sequential object sending rule
In-session unicast file repair
  Signaling by parameter mapping from MBS
  Procedures and requirements refer to MBS
  Mapping of requirements to MBMS Client and BM-SC
MBS owns repair protocol
MBMS owns multicast delivery protocol

## Slide 46: 5G-MAG Implementation
I learned last week that GPAC already implements this.
A bit of work

## Slide 47: Topic #8: Time Synchronization
Stage-2:
Stage-3: S4-251511

## Slide 48: 5G-MAG Implementation

## Slide 49: Rel-20
Approved new study